ECE  2504 Homework Set #2

Introduction to Computer Engineering

Due date: 2/1/08 at 5 PM

This assignment is to be done individually

Complete the following problems. Show all work.

- Decode the following 7-bit ASCII codes:

1010010 1000101 1001101 1000101 1001101 1000010 1000101 1010010 0100000

1010100 1001000 1000101 0100000 1000001 1001100 1001101 1001111 0101110

- Find the decimal equivalent of the following two’s complement numbers: 1110101, 1000000, 01011011, 100000000, 111111111, 10111000

- Perform the addition of the following 8-bit two’s complement numbers and show the decimal result. Show all work. 
11101101 + 01001010;  01001001 + 00101001;  01110010 + 11110010; 
11101110 + 11111110

- Perform the subtraction of the following numbers represented in two’s complement form and show the decimal result:

01100100-01101101; 11101001-10001111; 11000000-11000000; 11101111-10000000;

1000001-00000011

- Find the smallest negative value expressed in 2’s complement form that when added to itself, the sum causes an overflow to occur. For this problem, smallest negative number means a negative value closest to zero.

- Problems: 3-14, 3-15, 3-19

- Convert the decimal value 328.071875 to a 32-bit floating point number in IEEE standard format.

- Convert  AD46B000H, which is in the 32-bit floating point number in IEEE standard format, to a decimal value.