Student Name: ______________________

Student Number:_____________________

EE2504       EXAMINATION  1         Spring

Form  A

Instructions:  Read and follow the instructions carefully.

1. Do not open the examination until the instructor tells you to do so.

2. This is a closed book, closed notes examination.  No calculators of any kind may be used.

4. This examination will be machine graded.  Print your NAME, COURSE, STUDENT NUMBER, FORM and DATE on the top of the OPSCAN sheet.

5. Encode your STUDENT NUMBER and FORM on the OPSCAN sheet by filling in exactly one circled number or letter under each symbol.

6. Since this exam will be machine graded, the following instructions must be followed exactly:

a)  Use a Number 2 pencil only.

b)  Make sure all marks are heavy and dark.

c)  Make any erasures completely clean.  Do not leave any smudges.

d)  Do not make a mark in more than one circle for each question.

7.  Check the projection screen for additional instructions and information.

8.  The cover sheet of this examination booklet and the OPSCAN sheet must be turned in.

9.  I have neither given nor received any aid while working on this examination.  I have not used a calculator nor referenced any material while working on this examination.

Signature _____________________________

(Blank Page)

1. Convert 3B.116 into binary.

| 1) 111011.0001 *** | 2) 111011.1 |
| --- | --- |
| 3) 111011 | 4) 110011.1 |
| 5) 1111110.001 | 6) 111011.111... |
| 7) None of the above |  |

2.	Convert 25.22510 to hexadecimal.

| 1) C9.CCC... | 2) C9.C |
| --- | --- |
| 3) 19.3999...*** | 4) 19.3 |
| 5) 11001.224 | 6) 31.14 |
| 7) None of the above |  |

3	Obtain the 2's complement of 0000.

| 1) 0000 *** | 2) 10000 |
| --- | --- |
| 3) 1111 | 4) 0001 |
| 5) 1000 | 6) None of the above |

4. An 8-bit register stores integer numbers in signed 2's complemented form. What is the range of the numbers which can be stored in the register.

| 1) 0 ~ 255 | 2) -127 ~ 127 |
| --- | --- |
| 3) -128 ~ 127 *** | 4) -128 ~ 128 |
| 5) None of the above |  |

5. Perform the binary arithmetic of the two 6-bit numbers in signed 2's complement form. (Note that the result should be in signed 2's complement form.)

101011 - 100110 = ?

| 1) 111001 | 2) 001101 |
| --- | --- |
| 3) 1000101 | 4) 000101 *** |
| 5) 111011 | 6) 000110 |
| 7) None of the above |  |

6. Two positive numbers in signed 2's complement form are to be added. An overflow occurs if

1) Carry into the sign bit is 1. ***

2) Carry into the sign bit is 0.

3) Carry out of the sign bit is 1

4) Carry out of the sign bit is 0.

5) None of the above

7. A 32-bit register stores a floating-point number in IEEE single precision format. Find the equivalent decimal number represented by the register whose content is BF40000016.

| 1) -1.1 | 2) -0.15 |
| --- | --- |
| 3) -0.1 x 2126 | 4) -1.1 x 2126 |
| 5) -0.75 *** | 6) -0.11 |
| 7) -0.55 | 8) None of the above |

8. A decimal number +3.25 is to be stored in a register in IEEE single precision format. Find the content of the register in hexadecimal.

| 1) CFD0 0000 | 2) 5FD0 0000 |
| --- | --- |
| 3) 3FD0 0000 | 4) 4058 0000 |
| 5) 40D0 0000 | 6) 4050 0000 *** |
| 7) None of the above |  |

9. A 32-bit register stores the smallest number represented in IEEE single precision format. Find the content of the register in hexadecimal.

Note: 	-1.0 x 21 > -1.1 x 21

-1.0 x 21 > -1.0 x 22

| 1) 807F FFFF | 2) FFFF FFFF *** |
| --- | --- |
| 3) FF80 0000 | 4) 8070 0000 |
| 5) 8000 0000 | 6) None of the above |

10. A valid identity is ...

| 1) (xy)' = x'y' | 2) x(y+z) = xy + z |
| --- | --- |
| 3) x + 0 = 0 | 4) y + xy' = x + y *** |
| 5) x + yz = (x+y)z | 6) x + x' = 0 |
| 7) xx' = 1 | 8) None of the above |

11. The logic function of the circuit given below is ...

| 1) x + y | 2) x' + y |
| --- | --- |
| 3) x' + y' | 4) x + y' |
| 5) x'y | 6) xy |
| 7) xy' *** | 8) x'y' |
| 9) None of the above |  |

12. A function has 3 variables, x, y and z. Find a minterm of the function from the given choices.

| 1) x + y + z | 2) x'y'z *** |
| --- | --- |
| 3) xy | 4) x |
| 5) x' + y' + z | 6) y |
| 7) None of the above |  |

13. A function f(x,y,z) = x  y  z, where   is Exclusive-OR operation. Find f(x,y,z) in the sum of minterm form.

| 1) (0,1,2,3) | 2) (0,1,2,4,5) |
| --- | --- |
| 3) (4,5,6,7) | 4) (3,4,5,6,7) |
| 5) (0,3,5,6) | 6) (1,3,5,7) |
| 7) (0,2,4,6) | 8) (1,2,4,7) *** |
| 9) (0,2,4,6,7) | 10) None of the above |

14. We know that any logic functions can be expressed in canonical SOP (Sum-Of-Product) form or canonical POS (Product-Of-Sum) form. Is it true that any logic functions can be implemented by using only 2-input NAND gates?

| 1) Yes *** | 2) No |
| --- | --- |
| 3) Not enough information |  |

15. Find the logic function implemented by the circuit given below.]

1) (x + y + z) (w + x' + y) (w' + z) ***

2) (x' + y' + z') (w' + x + y') (w + z')

3) xyz + wx'y + w'z

4) x'y'z + w'xy' + wz'

5) None of the above

16. Simplify the function f with don't cares d.

f(w,x,y,z) = (0,1,2,8,9.12,13)

d(w,x,y,z) = (7,10,11,14,15)

| 1) w + x'y + x'yz' | 2) wy' + x'y' + wyz + w'x'z' |
| --- | --- |
| 3) wy' + x'yz' | 4) w + x'y' |
| 5) w + x'y' + x'z' *** | 6) w + w'x' |
| 7) wx + x'z' | 8) None of the above |

17. A logic function f(w,x,y,z) =  (1, 3, 7, 8, 9, 10, 11, 14, 15) is given. Simplify the function in POS (Product-Of-Sum) form.

1) (w + x') (w + y) (y + z) (x' + z)

2) (w' + x) (w' + y') (y' + z' ) (x + z')

3) (x + y') (w' + z')

4) (x' + y) (w + z) ***

5) (x + y') (w + z)

6) (x' + y) (w' + z')

7) None of the above

For the next two problems, consider the FF given below.

18. Find the characteristic table of the FF.

|  | (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A B | Q(t+1) | Q(t+1) | Q(t+1) | Q(t+1) | Q(t+1) | Q(t+1) |  |
| 0 0 | 0 | Q'(t) | 1 | Q(t) | Q(t) | 1 | None |
| 0 1 | Q(t) | 0 | Q'(t) | 1 | 0 | Q(t) | of |
| 1 0 | 1 | Q(t) | 0 | Q'(t) | Q'(t) | 0 | them |
| 1 1 | Q'(t) | 1 | Q(t) | 0 | 1 | Q'(t) |  |
|  |  |  | *** |  |  |  |  |

19. The current state of the FF is 0. Show all the possible input combinations of A and B which make the next state of the FF to 1.

| 1) AB = 0X *** | 2) AB = X0 |
| --- | --- |
| 3) AB = 1X | 4) AB = X1 |
| 5) AB = 00 only | 6) AB = 11 only |
| 7) AB = 01 only | 8) AB = 10 only |
| 9) None of the above |  |

20. The speed of a computer is ultimately determined by ...

(Choose the best answer.)

1) Fan-out limit of gates

2) Propagation delay of gates ***

3) Noise margin of gates

4) Power dissipation of gates

5) Logic types of gates

6) Complexity of gates

21.

We want to build a circuit which turns on a light for odd numbers, number 0 and number 6. The number is coded in 2421 code. Let (a,b,c,d) represents the bits for an input whose corresponding number is obtained as 2a+4b+2c+1d. Only the input combinations given in the table are applied to the circuit. When the output of the circuit f is 1, the light is turned on.

a) Fill in the following truth table. (5 points)

| a b c d | output f |
| --- | --- |
| 0 0 0 0 |  |
| 0 0 0 1 |  |
| 0 0 1 0 |  |
| 0 0 1 1 |  |
| 0 1 0 0 |  |
| 1 0 1 1 |  |
| 1 1 0 0 |  |
| 1 1 0 1 |  |
| 1 1 1 0 |  |
| 1 1 1 1 |  |

b)

i) Fill the Karnaugh map. Use x for don't cares.

ii) Show the groups of minterms to be combined.

iii) Show the product term associated with each group.

iv) Obtain the simplified function f.

f =

You have to turn in both the cover sheet of this exam booklet and the OPSCAN sheet. Make sure that you have put your name and id on the OPSCAN sheet.