## Slide 1: Light and Color
Computer Vision
Jia-Bin Huang, Virginia Tech
Empire of Light, 1950 by Rene Magritte

## Slide 2: Administrative stuffs
Signed up Piazza discussion board?
Sample final project ideas posted
Installed MATLAB?
  Akrit (TA) will hold a tutorial session next Friday
Reviewed Linear Algebra?
Questions about the course logistics?
Search for Teammates!

## Slide 3: Previous class: Introduction
Overview of computer vision
Examples of computer vision applications
Safety
Health
Security
Comfort
Access
Fun

## Slide 4: Today’s class
What determines pixels’ brightness?
What determines pixels’ color?
What can we infer about the scene from pixel intensities?

## Slide 5: Why should we care?
Photometric Stereo

## Slide 6: Why should we care?
Exposing Photo Manipulation from Shading and Shadows [Kee et al. TOG 14]

## Slide 7: Why should we care?
White and gold?
Or
Black and blue?

## Slide 8: Why should we care?
Object and scene categorization [Sande et al. PAMI 2010]

## Slide 9: What determines pixels’ brightness?

## Slide 10: Image Formation
Digital Camera
The Eye
Film

## Slide 11: Sensor Array
CMOS sensor

## Slide 12: What humans see
Slide credit: Larry Zitnick

## Slide 13: What computers see
243 | 239 | 240 | 225 | 206 | 185 | 188 | 218 | 211 | 206 | 216 | 225
242 | 239 | 218 | 110 | 67 | 31 | 34 | 152 | 213 | 206 | 208 | 221
243 | 242 | 123 | 58 | 94 | 82 | 132 | 77 | 108 | 208 | 208 | 215
235 | 217 | 115 | 212 | 243 | 236 | 247 | 139 | 91 | 209 | 208 | 211
233 | 208 | 131 | 222 | 219 | 226 | 196 | 114 | 74 | 208 | 213 | 214
232 | 217 | 131 | 116 | 77 | 150 | 69 | 56 | 52 | 201 | 228 | 223
232 | 232 | 182 | 186 | 184 | 179 | 159 | 123 | 93 | 232 | 235 | 235
232 | 236 | 201 | 154 | 216 | 133 | 129 | 81 | 175 | 252 | 241 | 240
235 | 238 | 230 | 128 | 172 | 138 | 65 | 63 | 234 | 249 | 241 | 245
237 | 236 | 247 | 143 | 59 | 78 | 10 | 94 | 255 | 248 | 247 | 251
234 | 237 | 245 | 193 | 55 | 33 | 115 | 144 | 213 | 255 | 253 | 251
248 | 245 | 161 | 128 | 149 | 109 | 138 | 65 | 47 | 156 | 239 | 255
190 | 107 | 39 | 102 | 94 | 73 | 114 | 58 | 17 | 7 | 51 | 137
23 | 32 | 33 | 148 | 168 | 203 | 179 | 43 | 27 | 17 | 12 | 8
17 | 26 | 12 | 160 | 255 | 255 | 109 | 22 | 26 | 19 | 35 | 24
Slide credit: Larry Zitnick

## Slide 14: How does a pixel get its value?
Light emitted
Sensor
Lens
Fraction of light reflects into camera
Slide credit: Derek Hoiem

## Slide 15: How does a pixel get its value?
Major factors
  Illumination strength and direction
  Surface geometry
  Surface material
  Nearby surfaces
  Camera gain/exposure
Light emitted
Sensor
Light reflected to camera
Slide credit: Derek Hoiem

## Slide 16: Basic models of reflection
Specular: light bounces off at the incident angle
  E.g., mirror
Diffuse: light scatters in all directions
  E.g., brick, cloth, rough wood
incoming light
specular reflection
incoming light
diffuse reflection
Slide credit: Derek Hoiem

## Slide 17: Lambertian reflectance model
Some light is absorbed (function of albedo)
Remaining light is scattered (diffuse reflection)
Examples: soft cloth, concrete, matte paints
light source
light source
absorption
diffuse reflection
Slide credit: Derek Hoiem
Notes: albedo is the fraction of light reflected

## Slide 18: Lambertian reflectance model
Some light is absorbed (function of albedo)
Remaining light is scattered (diffuse reflection)
Examples: soft cloth, concrete, matte paints
light source
light source
absorption
diffuse reflection
Slide credit: Derek Hoiem
Notes: albedo is the fraction of light reflected

## Slide 19: Diffuse reflection: Lambert’s cosine law
Intensity does not depend on viewer angle.
  Amount of reflected light proportional to
  Visible solid angle also proportional to
http://en.wikipedia.org/wiki/Lambert%27s_cosine_law
Slide credit: Derek Hoiem

## Slide 20: Specular Reflection
Reflected direction depends on light orientation and surface normal
  E.g., mirrors are fully specular
  Most surfaces can be modeled with a mixture of diffuse and specular components
light source
specular reflection
Flickr, by suzysputnik
Flickr, by piratejohnny
Slide credit: Derek Hoiem

## Slide 21: Most surfaces have both specular and diffuse components
Specularity = spot where specular reflection dominates (typically reflects light source)
Photo: northcountryhardwoodfloors.com
Typically, specular component is small
Slide credit: Derek Hoiem

## Slide 22: Intensity and Surface Orientation
Intensity depends on illumination angle because less light comes in at oblique angles.
Albedo: fraction of light that is reflected
directional source
surface normal
reflected intensity
Slide credit: Forsyth

## Slide 23
1
2

## Slide 24: Recap
When light hits a typical surface
  Some light is absorbed (1-)
    More absorbed for low albedos
  Some light is reflected diffusely
    Independent of viewing direction
  Some light is reflected specularly
    Light bounces off (like a mirror), depends on viewing direction
specular reflection
diffuse reflection
absorption
Slide credit: Derek Hoiem

## Slide 25: Other possible effects
light source
transparency
light source
refraction
Slide credit: Derek Hoiem

## Slide 26
λ1
light source
λ2
fluorescence
t=1
light source
t>1
phosphorescence
Slide credit: Derek Hoiem

## Slide 27
λ
light source
subsurface scattering
Slide credit: Derek Hoiem

## Slide 28: BRDF: Bidirectional Reflectance Distribution Function
surface normal
Slide credit: S. Savarese
Model of local reflection that tells how bright a surface appears when viewed from one direction when light falls on it from another

## Slide 29: Reflection models
Lambertian: reflection all diffuse
Mirrored: reflection all specular
Glossy: reflection mostly diffuse, some specular

## Slide 30: Dynamic range and camera response
Typical scenes have a huge dynamic range
Camera response is roughly linear in the mid range (15 to 240) but non-linear at the extremes
  called saturation or undersaturation

## Slide 31: What determines pixels’ color?
https://upload.wikimedia.org/wikipedia/commons/b/b1/Colouring_pencils.jpg

## Slide 32: The Eye
The human eye is a camera!
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Slide by Steve Seitz

## Slide 33: Retina up-close
Light
Notes: Floaty things in your vision are white blood cells in capillaries. Some animals have two foveas (some birds) and some have none (cats and dogs). 100x sensors than nerve fibers: much processing (e.g., center surround) in retina itself

## Slide 34
© Stephen E. Palmer, 2002
Cones
cone-shaped
less sensitive
operate in high light color vision
Two types of light-sensitive receptors
Rods
rod-shaped
highly sensitive
operate at night
gray-scale vision
slower to respond
Slide Credit: Efros

## Slide 35: Distribution of Rods and Cones
© Stephen E. Palmer, 2002
Night Sky: why are there more stars off-center?
Slide credit: Efros

## Slide 36: Find your blind spot

## Slide 37: The Physics of Light
http://www.yorku.ca/eye/photopik.htm
Human Luminance Sensitivity Function
Light: Electromagnetic energy whose wavelength is between 400 nm and 700 nm. (1 nm = 10 -9 meter)
Slide Credit: Efros
Notes: At least 3 spectral bands required (e.g. R,G,B)

## Slide 38: Visible Light
Why do we see light of these wavelengths?
© Stephen E. Palmer, 2002
…because that’s where the
Sun radiates EM energy

## Slide 39
The Physics of Light
Any patch of light can be completely described
physically by its spectrum: the number of photons
(per time unit) at each wavelength 400 - 700 nm.
© Stephen E. Palmer, 2002

## Slide 40
The Physics of Light
Some examples of the spectra of light sources
© Stephen E. Palmer, 2002

## Slide 41
The Physics of Light
Some examples of the reflectance spectra of surfaces
Wavelength (nm)
% Photons Reflected
Red
400 700
Yellow
400 700
Blue
400 700
Purple
400 700
© Stephen E. Palmer, 2002

## Slide 42
The Psychophysical Correspondence
There is no simple functional description for the perceived
color of all lights under all viewing conditions, but …...
A helpful constraint:
Consider only physical spectra with normal distributions
area
mean
variance
© Stephen E. Palmer, 2002

## Slide 43
The Psychophysical Correspondence
Mean
Hue
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 44
The Psychophysical Correspondence
Variance
Saturation
Wavelength
# Photons
© Stephen E. Palmer, 2002

## Slide 45
The Psychophysical Correspondence
Area
Brightness
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 46: Question: draw a “pink” light
Wavelength
# Photons

## Slide 47
© Stephen E. Palmer, 2002
Three kinds of cones:
Physiology of Color Vision
Why are M and L cones so close?
Why are there 3?

## Slide 48: Trichromacy
Rods and cones act as filters on the spectrum
  To get the output of a filter, multiply its response curve by the spectrum, integrate over all wavelengths
    Each cone yields one number
S
M
L
Wavelength
Power
  How can we represent an entire spectrum with 3 numbers?
  We can’t! Most of the information is lost
    As a result, two different spectra may appear indistinguishable
      such spectra are known as metamers
Slide by Steve Seitz

## Slide 52: Correcting Colorblind?
http://enchroma.com/

## Slide 53
© Stephen E. Palmer, 2002
Color Constancy
The “photometer metaphor” of color perception:
Color perception is determined by the spectrum of light
on each retinal receptor (as measured by a photometer).

## Slide 54
© Stephen E. Palmer, 2002
Color Constancy
The “photometer metaphor” of color perception:
Color perception is determined by the spectrum of light
on each retinal receptor (as measured by a photometer).

## Slide 55
© Stephen E. Palmer, 2002
Color Constancy
The “photometer metaphor” of color perception:
Color perception is determined by the spectrum of light
on each retinal receptor (as measured by a photometer).

## Slide 56
© Stephen E. Palmer, 2002
Color Constancy
Do we have constancy over
all global color transformations?
60% blue filter
Complete inversion

## Slide 57
Color Constancy
© Stephen E. Palmer, 2002
Color Constancy: the ability to perceive the
invariant color of a surface despite ecological
Variations in the conditions of observation.
Another of these hard inverse problems:
Physics of light emission and surface reflection
underdetermine perception of surface color

## Slide 58: Practical Color Sensing: Bayer Grid
Estimate RGB at ‘G’ cels from neighboring values
http://www.cooldictionary.com/ words/Bayer-filter.wikipedia
Slide by Steve Seitz

## Slide 59: Color Image
R
G
B

## Slide 60: Images in Matlab
Images represented as a matrix
Suppose we have a NxM RGB image called “im”
  im(1,1,1) = top-left pixel value in R-channel
  im(y, x, b) = y pixels down, x pixels to right in the bth channel
  im(N, M, 3) = bottom-right pixel in B-channel
imread(filename) returns a uint8 image (values 0 to 255)
  Convert to double format (values 0 to 1) with im2double
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column

## Slide 61: Color spaces
How can we represent color?
http://en.wikipedia.org/wiki/File:RGB_illumination.jpg

## Slide 62: Color spaces: RGB
0,1,0
0,0,1
1,0,0
Image from: http://en.wikipedia.org/wiki/File:RGB_color_solid_cube.png
Default color space
R
(G=0,B=0)
G
(R=0,B=0)
B
(R=0,G=0)
RGB cube
  Easy for devices
  But not perceptual
  Where do the grays live?
  Where is hue and saturation?

## Slide 63: HSV
Hue, Saturation, Value (Intensity)
  RGB cube on its vertex
Decouples the three components (a bit)
Use rgb2hsv() and hsv2rgb() in Matlab
Slide by Steve Seitz

## Slide 64: Color spaces: HSV
Intuitive color space
H
(S=1,V=1)
S
(H=1,V=1)
V
(H=1,S=0)

## Slide 65: Color spaces: L*a*b*
“Perceptually uniform” color space
L
(a=0,b=0)
a
(L=65,b=0)
b
(L=65,a=0)

## Slide 66: So far: lightsurfacecamera
Called a local illumination model
But much light comes from surrounding surfaces
From Koenderink slides on image texture and the flow of light

## Slide 67: Inter-reflection is a major source of light

## Slide 68: Inter-reflection affects the apparent color of objects
From Koenderink slides on image texture and the flow of light

## Slide 69: Scene surfaces also cause shadows
Shadow: reduction in intensity due to a blocked source

## Slide 70: Shadows

## Slide 71: Models of light sources
Distant point source
  One illumination direction
  E.g., sun
Area source
  E.g., white walls, diffuser lamps, sky
Ambient light
  Substitute for dealing with interreflections
Global illumination model
  Account for interreflections in modeled scene

## Slide 72: Questions
1
2
3
4
5
6
7
8
9
Why is (2) brighter than (1)? Each points to the asphalt.
Why is (4) darker than (3)? (4) points to the marking.
Why is (5) brighter than (3)? Each points to the side of the wooden block.
Why isn’t (6) black, given that there is no direct path from it to the sun?
Why (7) brighter than (8)? Both point to the yellow paints.
Why is (9) green, given that the sun light contains all visible wavelengths?

## Slide 73: What does the intensity of a pixel tell us?
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
im(234, 452) = 0.58

## Slide 74: The plight of the poor pixel
A pixel’s brightness is determined by
  Light source (strength, direction, color)
  Surface orientation
  Surface material and albedo
  Reflected light and shadows from surrounding surfaces
  Gain on the sensor
A pixel’s brightness tells us nothing by itself

## Slide 76: And yet we can interpret images…
Key idea: for nearby scene points, most factors do not change much
The information is mainly contained in local differences of brightness

## Slide 77: Darkness = Large Difference in Neighboring Pixels

## Slide 78: What is this?

## Slide 80: What differences in intensity tell us about shape?
Changes in surface normal
Texture
Proximity
Indents and bumps
Grooves and creases
Photos Koenderink slides on image texture and the flow of light
Notes: So far, most people have gotten away with just knowing that differences are important and designing features that measure differences.

## Slide 81: Shadows as cues
From Koenderink slides on image texture and the flow of light
Slide: Forsyth

## Slide 82: Color constancy
Interpret surface in terms of albedo or “true color”, rather than observed intensity
  Humans are good at it
  Computers are not nearly as good

## Slide 83: One source of constancy: local comparisons

## Slide 84
http://www.echalk.co.uk/amusements/OpticalIllusions/colourPerception/colourPerception.html

## Slide 85: Perception of Intensity
from Ted Adelson

## Slide 86: Perception of Intensity
from Ted Adelson

## Slide 87: Color Correction
Simple idea: multiply R, G, and B values by separate constants
=
How to choose the constants?
  “White world” assumption: brightest pixel is white
    Divide by largest value
  “Gray world” assumption: average value should be gray
    E.g., multiply r channel by avg(r) /avg((r+g+b)/3)
  White balancing: choose a reference as the white or gray color

## Slide 88
Discount the blue side
Discount the gold side

## Slide 89: Things to remember
Important terms: diffuse/specular reflectance, albedo
Color vision: physics of light, trichromacy, color consistency, color spaces (RGB, HSV, Lab)
Observed intensity depends on
  light sources,
  geometry/material of reflecting surface,
  surrounding objects,
  camera settings
Objects cast light and shadows on each other
Differences in intensity are primary cues for shape

## Slide 90: Thank you
Next class: Image Filters