## Slide 1: Single-view Metrology and Camera Calibration
Computer Vision
Jia-Bin Huang, Virginia Tech
Many slides from S. Seitz and D. Hoiem

## Slide 2: Administrative stuffs
HW 2 due 11:59 PM on Oct 9th
Ask/discuss questions on Piazza
Office hour

## Slide 3: Perspective and 3D Geometry
Projective geometry and camera models
  What’s the mapping between image and world coordiantes?
Single view metrology and camera calibration
  How can we estimate the camera parameters?
  How can we measure the size of 3D objects in an image?
Photo stitching
  What’s the mapping from two images taken without camera translation?
Epipolar Geometry and Stereo Vision
  What’s the mapping from two images taken with camera translation?
Structure from motion
  How can we recover 3D points from multiple images?

## Slide 4: Last Class: Pinhole Camera
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Principal Point (u0, v0)
v
u

## Slide 5: Last Class: Projection Matrix
Ow
iw
kw
jw
t
R
Notes: As review:
1) Example of my eye and their eye, where both coordinate frames are known. Suppose that I know a 3D point on the board in relation to me, and I want to figure out where that point will appear on their retina. First, I translate from my eye to their eye. Then, I rotate from my orientation to theirs. Finally, I project from 3D onto the 2D visual field.
2) Suppose I know x, K, R, and t. Can I compute X? What can I know about X?

## Slide 6: Last class: Vanishing Points
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 7: This class
How can we calibrate the camera?
How can we measure the size of objects in the world from an image?
What about other camera properties: focal length, field of view, depth of field, aperture, f-number?

## Slide 8: How to calibrate the camera?

## Slide 9: Calibrating the Camera
Method 1: Use an object (calibration grid) with known geometry
  Correspond image points to 3d points
  Get least squares solution (or non-linear solution)
Known 3d locations
Known 2d image coordinates
Unknown Camera Parameters

## Slide 10
Known 3d locations
Known 2d image coords
Unknown Camera Parameters

## Slide 11
Known 3d locations
Known 2d image coords
Unknown Camera Parameters
Method 1 – homogeneous linear system. Solve for m’s entries using linear least squares
[U, S, V] = svd(A);
M = V(:,end);
M = reshape(M,[],3)';

## Slide 12
Method 2 – nonhomogeneous linear system. Solve for m’s entries using linear least squares
Ax=b form
M = A\Y;
M = [M;1];
M = reshape(M,[],3)';
Known 3d locations
Known 2d image coords
Unknown Camera Parameters

## Slide 13: Calibration with linear method
Advantages
  Easy to formulate and solve
  Provides initialization for non-linear methods
Disadvantages
  Doesn’t directly give you camera parameters
  Doesn’t model radial distortion
  Can’t impose constraints, such as known focal length
  Doesn’t minimize projection error
Non-linear methods are preferred
  Define error as difference between projected points and measured points
  Minimize error using Newton’s method or other non-linear optimization

## Slide 14: Can we factorize M back to K [R | T]?
Yes!
You can use RQ factorization
  (note – not the more familiar QR factorization).
R (right diagonal) is K, and Q (orthogonal basis) is R. T, the last column of [R | T], is inv(K) * last column of M.
  Need post-processing to make sure that the matrices are valid.
  See http://ksimek.github.io/2012/08/14/decompose/
Slide credit: J. Hays

## Slide 15: Calibrating the Camera
Method 2: Use vanishing points
  Find vanishing points corresponding to orthogonal directions
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 16: Calibration by orthogonal vanishing points
Intrinsic camera matrix
  Use orthogonality as a constraint
  Model K with only f, u0, v0
What if you don’t have three finite vanishing points?
  Two finite VP: solve f, get valid u0, v0 closest to image center
  One finite VP: u0, v0 is at vanishing point; can’t solve for f
For vanishing points

## Slide 17: Calibration by vanishing points
Intrinsic camera matrix
Rotation matrix
  Set directions of vanishing points
    e.g., X1 = [1, 0, 0]
  Each VP provides one column of R
  Special properties of R
    inv(R)=RT
    Each row and column of R has unit length

## Slide 18: How can we measure the size of 3D objects from an image?
Slide by Steve Seitz

## Slide 19: Perspective cues
Slide by Steve Seitz

## Slide 20: Perspective cues
Slide by Steve Seitz

## Slide 21: Perspective cues
Slide by Steve Seitz

## Slide 22: Ames Room

## Slide 24: Comparing heights
Vanishing
Point
Slide by Steve Seitz

## Slide 25: Measuring height
1
2
3
4
5
5.3
2.8
3.3
Camera height
Slide by Steve Seitz

## Slide 26
Which is higher – the camera or the man in the parachute?

## Slide 27: The cross ratio
A Projective Invariant
  Does not change under projective transformations
P1
P2
P3
P4
The cross-ratio of 4 collinear points
Can permute the point ordering
  4! = 24 different orders (but only 6 distinct values)
This is the fundamental invariant of projective geometry
Slide by Steve Seitz

## Slide 28: Measuring height
vZ
r
t
b
image cross ratio
B (bottom of object)
T (top of object)
R (reference point)
ground plane
H
C
scene cross ratio

scene points represented as
image points as
R
Slide by Steve Seitz

## Slide 29: Measuring height
R
H
vz
r
b
t
H
b0
t0
v
vx
vy
vanishing line (horizon)
image cross ratio
Slide by Steve Seitz

## Slide 30: Measuring height
vz
r
b
t0
vx
vy
vanishing line (horizon)
v
t0
m0
What if the point on the ground plane b0 is not known?
  Here the guy is standing on the box, height of box is known
  Use one side of the box to help find b0 as shown above
b0
t1
b1
Slide by Steve Seitz

## Slide 31: What about focus, aperture, DOF, FOV, etc?

## Slide 32: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 33: Focal length, aperture, depth of field
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
  Aperture of diameter D restricts the range of rays
focal point
F
optical center
(Center Of Projection)
Slide source: Seitz

## Slide 34: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil (aperture) - the hole whose size is controlled by the iris
  Retina (film): photoreceptor cells (rods and cones)
Slide source: Seitz
Notes: Note that the retina is curved

## Slide 35: Depth of field
Changing the aperture size or focal length affects depth of field
f / 5.6
f / 32
Flower images from Wikipedia http://en.wikipedia.org/wiki/Depth_of_field
Slide source: Seitz

## Slide 36: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide from Efros

## Slide 37: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects
Slide by Steve Seitz

## Slide 38: Shrinking the aperture
Slide by Steve Seitz

## Slide 39: Relation between field of view and focal length
Field of view (angle width)
Film/Sensor Width
Focal length

## Slide 40: Dolly Zoom or “Vertigo Effect”
http://www.youtube.com/watch?v=NB4bikrNzMk
http://en.wikipedia.org/wiki/Focal_length
Zoom in while moving away
How is this done?

## Slide 42: Variables that affect exposure
http://graphics.stanford.edu/courses/cs178-10/applets/exposure.html

## Slide 43: Review
How tall is this woman?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?
Notes: Find orthogonal vanishing points
Rotate image so that horizontal axis is in X direction
Draw horizon
Estimate camera height based on the standard size of Bocce balls (107 mm)
Estimate woman’s height based on camera height
Solve for intrinsic parameters and camera rotation from vanishing points

## Slide 44: Things to remember
Calibrate the camera?
  Use an object with known geometry
  Use vanishing points
Measure the size of objects in the world from an image?
  Use perspective cues
Camera properties
  focal length,
  field of view,
  depth of field,
  aperture,
  f-number?

## Slide 45: Next class
Image stitching
Camera Center
P
Q