## Slide 1: Boosting the Gain of the Transistor for High Frequency Oscillator and Amplifier Design
Dr. Kwang-Jin Koh
Laya Mohammadi

## Slide 2: Outline
Definition of maximum oscillation frequency (fmax)
Activity condition of two port device
How to increase power gain of the transistor near fmax
Oscillator design example
Amplifier design example
Conclusion

## Slide 3: Definition of maximum oscillation frequency(fmax)
Unilateral Power Gain and the Origin of fmax
Invariant function U for a linear two-port network (three-terminal device)
For any two-port device such as a transistor, U is only a function of the inherent characteristics of the device.
In a FET device, if we connect gate, source, and drain nodes to any of the three terminals the value of U remains the same.

## Slide 4: Definition of maximum oscillation frequency(fmax)
Here, we are interested in the other property of U. which is related to the activity of a device.
A device is called active at a certain frequency if it can generate power in the form of single sinusoidal signal at that frequency.
It is shown in [1], that if U>1 , the device is active. Similar to other device characteristics, U is also a function of frequency and, in most cases, decreases with frequency. The frequency that results in U=1 is called the maximum oscillation frequency (fmax).

## Slide 5: Activity condition of two port device
To ﬁnd the activity condition, ﬁrst we ﬁnd the real power ﬂowing out of a device.
Since we are interested in the sign of P , we can simplify:
To maximize P A and Φ should be maximized.
Real power:
For the device to be active, the net power ﬂowing out of the device should be positive, PR>0

## Slide 6: Activity condition of two port device
A and Φ describe the relation between the voltage amplitude and phase of the two ports of the transistor and for a given topology(oscillator), they are usually constant.
As a result, the maximum frequency of oscillation in a ﬁxed topology can be signiﬁcantly lower than the device limit.
By taking derivative of P with respect of A and Φ and equal each of them to zero, optimum value of A and Φ for maximizing P are obtained.

## Slide 7: Activity condition for oscillator design
Maximum Frequency of Ring Oscillators
fmax of FET in IBM8HP is around 160GHz.
N=2, cross-coupled oscillator.
N=3, 3-stage ring oscillator.

## Slide 8: Activity condition for oscillator design
Maximum Frequency of Ring Oscillators
fmax of HBT in IBM8HP is around 230GHz.
N=2, cross-coupled oscillator.
N=3, 3-stage ring oscillator.

## Slide 9: Negative Resistance
N=2, cross-coupled oscillator with HBT.
N=2, cross-coupled oscillator with FET.

## Slide 10
+ +
Zin in above equation still provides negative resistance at 190GHz. (rpi is not considered because we need the result after 100GHz.)
Negative Resistance of Colpitts

## Slide 11: Activity condition for oscillator design
Although HBTs have a higher fmax in comparison to FETs, the maximum frequency that they can oscillate with cross-coupled and ring oscillator topologies is lower than FETs.
This result shows that HBTs are not appropriate devices for ring oscillators.
FETs are more compatible with ring oscillator topology!!!
BJTs are more compatible with another topology (Colpitts) to exploit their higher power and fmax.

## Slide 12: Maximizing the power gain of a transistor

## Slide 13: Maximizing the power gain of a transistor

## Slide 14: How to Reach Gmax
For the same |V1| (the same input power), maximum PR (output power) results in maximum power gain of the device.

## Slide 15: Optimum Condition

## Slide 16: Maximum Achievable Gain(Gmax)

## Slide 17: Optimum Condition

## Slide 18: Conclusion
Each device, HBT or FET, works best with a particular topology, Colpitts or ring oscillator, respectively.
Optimum conditions (gain, phase) must be found for each device to maximize power output and frequency.
Circuit elements may be added to the active device to realize optimum conditions.

## Slide 19
References:
[1] O. Momeni, and E. Afshari, “High Power Terahertz and Millimeter-Wave Oscillator
Design: A Systematic Approach” IEEE JOURNAL OF SOLID-STATE CIRCUITS, VOL. 46, NO. 3, MARCH 2011
[2] O. Momeni, and E. Afshari, “ A High Gain 107GHZ Amplifier in 130 nm CMOS” CICC , 2011
[3] B. Razavi,”RF Microelectronics”, Printice Hall, 2012.

## Slide 20: Maximum Available Gain(Gma)

## Slide 21: Unilateral Gain (U)

## Slide 22: Maximum Achievable Gain(Gmax)

## Slide 23
The intriguing property of is that it is invariant under any 4-port, linear, lossless, reciprocal embedding shown in Fig.
In all of these oscillators, the oscillation frequency is around half of the of the transistors

## Slide 24
Signal generation at these frequencies is a major challenge solid-state electronics due to the limited cut-off frequency and breakdown voltage of active device.
The question that arises is whether the oscillators have exploited the full capacity of the active devices in terms of output power and frequency.
In other words, in any given process, it is essential to ﬁnd the maximum oscillation frequency of a circuit topology, considering the quality factor of the passive components. Furthermore, for a ﬁxed frequency, it is important to determine the topology that results in maximum output power.