## Slide 1
IBM 8HP Tapeout (12/03/12)
Report
Power Amplifers
Phased-Array Front-Ends
Virginia Tech:
Seyed Yahya Mortazavi
Sadia Lisa Afroz
Laya M. Mortzavi
Kwang-Jin Koh (kkoh@vt.edu)

## Slide 2: 1. 94 GHz 2-Stage Class-F PA (VCC=2.2V)
Part-I: Power Amplifier
2. 94 GHz 1-Stage Class-F PA (VCC = 2.2V)
3. 94 GHz 1-Stage Class-F PA (VCC = 1.3V)
4. 60 GHz 2-Stage Class-F PA (VCC=2.2V)
5. 60 GHz 1-Stage Class-F PA (VCC = 2.2V)
6. 60 GHz 1-Stage Class-F PA (VCC = 1.3V)
7. 60 GHz 1-Stage Class-F PA with coupled harmonic control

## Slide 3: 1. 94 GHz 2-Stage Class-F PA: Schematic
1
Class-F, 2-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~16 dBm, Output Psat: ~17 dBm
PAE: max 21-22 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 4: 1. 94 GHz 2-Stage Class-F PA: Simulations
2
These are simulation results including layout sonnet EM-model.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax = 21.8 %
P-1dB = 11.9dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 5: 1. 94 GHz 2-Stage Class-F PA: Layout
VBB1
VCC1
gnd
gnd
gnd
gnd
rfIn
rfOut
gnd
gnd
VCC2
VBB2
gnd
gnd
Size: 670μm x 490μm
3

## Slide 6: 2. 94 GHz 1-Stage Class-F PA (VCC = 2.2V): Schematic
4
Class-F, 1-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~15 dBm, Psat: ~16 dBm
PAE: max 19-20 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 7
5
These are simulation results including layout sonnet EM-model.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax = 21.8 %
P-1dB = 11.9dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21
2. 94 GHz 1-Stage Class-F PA (VCC = 2.2V): Simulations

## Slide 8
VBB
VCC
gnd
gnd
gnd
gnd
rfIn
rfOut
Size: 530μm x 400μm
gnd
gnd
6
2. 94 GHz 1-Stage Class-F PA (VCC = 2.2V): Layout

## Slide 9: 3. 94 GHz 1-Stage Class-F PA (VCC = 1.3V): Schematic
7
Class-F, 1-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~10 dBm, Psat: ~11.5 dBm
PAE: max 15-16 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 10: 3. 94 GHz 1-Stage Class-F PA (VCC = 1.3V): Simulations
8
These are simulation results including layout sonnet EM-model.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax =15.3 %
P-1dB = 7.7dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 11: 3. 94 GHz 1-Stage Class-F PA (VCC = 1.3V): Layout
VBB
VCC
gnd
gnd
gnd
gnd
rfIn
rfOut
gnd
gnd
Size: 535μm x 390μm
9

## Slide 12: 4. 60 GHz 2-Stage Class-F PA: Schematic
10
Class-F, 2-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~15 dBm, Psat: ~16 dBm
PAE: max 28-29 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 13: 4. 60 GHz 2-Stage Class-F PA: Simulations
11
These are simulation results including layout sonnet EM-model.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax =28.5 %
IP-1dB = 4.2dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 14: 4. 60 GHz 2-Stage Class-F PA: Layout
VBB1
VCC1
gnd
gnd
rfIn
rfOut
gnd
gnd
gnd
gnd
VBB2
VCC2
gnd
Size: 900μm x 400μm
12

## Slide 15: 5. 60 GHz 1-Stage Class-F PA (VCC = 2.2V): Schematic
13
Class-F, 1-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~9.7 dBm, Psat: ~15 dBm
PAE: max 29-30 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 16: 5. 60 GHz 1-Stage Class-F PA (VCC = 2.2V): Simulations
14
These are simulation results including layout sonnet EM-model.
Single stage design has ~15 dBm Psat with 29-30% PAE.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax =29 %
IP-1dB = 9.7dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 17: 5. 60 GHz 1-Stage Class-F PA (VCC = 2.2V): Layout
VBB
VCC
gnd
gnd
gnd
gnd
rfIn
rfOut
Size: 575μm x 410μm
gnd
gnd
15

## Slide 18: 6. 60 GHz 1-Stage Class-F PA (VCC = 1.3V): Schematic
16
Class-F, 1-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~11 dBm, Psat: ~12.5 dBm
PAE: max 25-26 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 19: 6. 60 GHz 1-Stage Class-F PA (VCC = 1.3V): Simulations
17
These are simulation results including layout sonnet EM-model.
Single stage design has ~12.5 dBm Psat with 25-26% PAE.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax = 25.8 %
P-1dB = 5.5dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 20: 6. 60 GHz 1-Stage Class-F PA (VCC = 1.3V): Layout
VBB
VCC
gnd
gnd
gnd
gnd
rfIn
rfOut
gnd
gnd
Size: 610μm x 410μm
18

## Slide 21: 7. 60 GHz 1-Stage Class-F PA with coupled harmonic control: Schematics
19
Class-F, 1-stage design: 2nd & 3rd harmonic controls
Harmonic filter: high-Z for fund & 3rd-harmonic, low-Z for 2nd-harmonic
OP-1dB: ~12.8 dBm, Psat: ~15 dBm
PAE: max 25-26 %
Notes: These figures conceptually summarize the benefits of phased arrays.
First, compared with this omni-directional pattern, in phaed array, we can generate highly directive beam pattern to a particular wanted direction. This means we can manipulate phases so that this interference signal can be place in the null of the radiation pattern, rejecting the interference.
Also, we can steer or generate multiple beams at the same time, so that same frequency, time or codes can be shared with different users, which means we can maximize communication resources.
Another point is that in phased array, we are collecting multiple signals using antenna arrays, and eventually add them in-phase. So coherent signal power will be added in square terms, while random noise can be added linearly as we increase the number of antenna. And therefore, we will get SNR benefit by a factor of N. This means we can increase channel capacity in log-scale with the increase of number of antenna.

## Slide 22: 7. 60 GHz 1-Stage Class-F PA with coupled harmonic control: Simulations
20
These are simulation results including layout sonnet EM-model.
Single stage design has ~15 dBm Psat with 25-26% PAE.
Pout (dBm)
Pin (dBm)
PAE (%)
PAEmax =25.5 %
P-1dB = 7.7dBm
S-parameter (dB)
Freq (GHz)
S22
S11
S21

## Slide 23: 7. 60 GHz 1-Stage Class-F PA with coupled harmonic control: Layout
VBB
VCC
gnd
gnd
gnd
gnd
rfIn
rfOut
gnd
gnd
Size: 710μm x 410μm
21

## Slide 24: 1. 94 GHz Design
Part-2: Phased-Array Front-End
2. 120 GHz Design

## Slide 25
Phased Array Front End Architecture (common to 94G & 120 GHz designs)

: LNA

&: Switch Amplifier
(functioning as an active switch)

: VGA

90o Hybrid
90o Hybrid
Rat-Race

## Slide 26
1. 94 GHz Phased Array Front End : S parameter Simulation
Frequency(GHz)
Phase(S21) in degree
Continuous 360o phase control (shown only 3-bit control here)
S21: 21-25 dB @94 GHz
These gain variation can be offset by adjusting VGA (not shown here)
NF: 8-9 dB @94 GHz
Frequency(GHz)
S21
NF=8-9 dB @94 GHz
S21,NF (dB)

## Slide 27: 1. 94 GHz Phased Array Front End : Simulations
Frequency(GHz)
S11(dB),S22(dB)
Pin (dBm)
Pout (dBm)
S22
S11
S11, S22 < -10 dB @90-100 GHz
Input PldB: -23.7 dBm @94 GHz(worst case: @ 25 dB of max. gain)

## Slide 28: 1. 94 GHz Phased Array Front End: Layout
Gnd
VCC
Gnd
Gnd
Gnd
Gnd
Gnd
RFin
RFout
Vc1
Vc3
Vc2
Vc4
Vc6
Vc5
Vc7
Size: 1833μm x 603.5μm
Supply 2.5 V , Total current 44mA

## Slide 29
2. 120 GHz Phased Array Front End : S parameter
Simulation
S21,NF (dB)
Frequency(GHz)
Frequency(GHz)
S21
NF (11-12 dB @120 GHz)
Continuous 360o phase control (shown only 3-bit control here)
S21: 16-20 dB @120 GHz
These gain variation can be offset by adjusting VGA (not shown here)
NF: 11-12 dB @120GHz
Phase(S21) in Degree

## Slide 30: 2. 120 GHz Phased Array Front End : Simulations
Frequency(GHz)
S11(dB),S22(dB)
Pout (dBm)
Pin (dBm)
S22
S11
S11, S22 < -10 dB @115-135 GHz
Input PldB: -21.5 dBm @120 GHz(worst case: @ 20 dB of max. gain)

## Slide 31: 2. 120 GHz Phased Array Front End: Layout
Size: 1592μm x 600μm
Supply 2.5V ,Total Current 37mA
Gnd
VCC
Gnd
Vc1
Vc3
Vc2
Vc4
Vc6
Vc5
Vc7
Gnd
Gnd
RFin
Gnd
Gnd
RFout