## Slide 1: Weekly report

## Slide 2: Last week
Paper survey on phased array system for the paper writing
Designed Wilkinson combiner in SONNET, Full EM simulation of 180 deg coupler,90 deg coupler(optimization needed)
Design VGA with DAC, for phase shifter resolution less than 10 degree

## Slide 3: Wilkinson power combiner @ 94 GHz (2to 1)
100 ohm resistance is included between port 4 and 5 in ADS
Insertion loss 3.5 dB
Isolation and Matching <-23 dB

## Slide 4: Simulation results : Inserting 100 resistance in ADS

## Slide 5: 180 Hybrid Sonnet Verification
S12=-3 dB,S13=-4 dB
Isolation <-22 dB
Macthing = 13
(comparable to the Cadence simulation)
MOM Cap=23 fF
Port for MIM Cap

## Slide 7: 3 bit control VGA with DAC

## Slide 8: 3 bit VGA response
Gain (Mag)

## Slide 9: Phase shifter response with DAC
Phase Resolution is 10
3 bit VGA
Gain variation is 17-20 dB
Phase (deg)
Frequency (GHz)

## Slide 10: Next week
Integration with phase shifter with Mixer and combiner.
Studying for chip measurement
EM simulation of couplers and optimization
Optimization f DAC for decreasing the phase variation