## Slide 1: Filter Response

## Slide 2: Schematic of Filter with input matching (one stage)

## Slide 3: One Stage 7.2GHz, Input matched with 50 ohm (JAZZ Tech)
By optimization best IIP3 = -5 dBm, NF=14 dB, Q=3 @ 7.2GHz
NF can be decreased to 10 dB by reducing IIP3,in that case IIP3=-11dBm
Q can be increased from 3 but Linearity is decreased.
IIP3= -5dBm
IIP3= -9dBm
NF= 14 dB
Frequency

## Slide 4
Trade of between NF,Q
A gain is observed because input CB has gain
IIP3= -8.5dBm
NF= 11dB
Q= 2
IIP3= -11dBm
Q=4
NF=11 dB
Trade of between Q and IIP3
Frequency
Frequency

## Slide 5: Compare of multiple stage filter @7.24GHz, Input matched with 50 ohm(JAZZ Tech)
As number of stages increases, NF and Linearity degrades.
1 stage ,IIP3= -6.5dBm,Q=3.3,NF=14 dB
2 stage ,IIP3= -8.75dBm, Q=5,NF=19 dB
3 stage ,IIP3= -10 dBm, Q=6.3,NF=20 dB
Frequency

## Slide 6: Notes
Common Base configuration is used for wide band input matching
With changing frequency, Linearity and Noise figure does not change, if the control current source are not changed.
The best IIP3 is got is -5dBm with optimization.
IBM and JAZZ shows almost same performance ,Noise figure is slightly better with IBM