## Slide 1: Centre frequency 83.5GHz (Using Ideal Inductor and ideal Capacitor)
Q varies from 4-20 by changing R from 0-150 ohm (Inductor L=30pH,Capacitor C=245fF)
NF is 11-16 dB,IIP3 >20 dBm
Q can be decreased by increasing current but Frequency shifting occurs
Frequency (GHz)
Gain (dB)

## Slide 2: Centre frequency 83.5GHz (Using Real Inductor(Q=21) and ideal Capacitor)
Q varies from 3.6-14 by changing R from 0-150 ohm (Inductor L=30pH,Capacitor C=245fF)
NF is 13-19 dB,IIP3 >15 dBm
Frequency (GHz)
Gain (dB)

## Slide 3: Centre frequency 83.5GHz (Using Real Inductor and Real Capacitor)
Q varies from 4.5-12 by changing R from 0- 150 ohm
NF is 13-20 dB,IIP3 >15 dBm
Frequency (GHz)
Gain (dB)

## Slide 4: Centre frequency 94GHz (Using Real Inductor and Real Capacitor)
Q varies from 5-14 by changing R from 0- 150 ohm
NF is 11-20 dB,IIP3 >10 dBm
Frequency (GHz)
Gain (dB)