## Slide 1: Weekly report
Sadia Afroz
06/15/2013

## Slide 2: Last week
Designed VGA
Optimization of Phase shifter for linearity ,Power consumption and Gain
Verified the phased shifter with ADS.

## Slide 3: VGA using current steering technique To fine control of Gain and Matching
Gain Varies from 8.4 dB to 0 dB,
Worst case IIP3 -0.886 dBm (Done in ADS)
Maximum Power consumption 14mW (requires supply 1.8V and 2V)
Gain Can be further increase keeping power same, at a cost of linearity.

## Slide 4: LNA and switch amplifier
Gain 9 dB, NF=7.5 dB
IIP3= -0.58 dBm (Verified in ADS)
Power consumption=16mW
Switch Amplifier (1)
Gain= 5 dB, IIP3=-0.35 dBm
Power consumption 20mW
Input and Output is matched for any case
Switch Amplifier (2)
Gain 6 dB
Power consumption 16 mW
IIP3 -0.6345 dBm
Input is not matched for one case

## Slide 5
Gain Variation | P1 dB compression point(worst case) | Power Consumption(worst case)
19-22 dB | -28 dBm | 85mW
15-18 dB | -26 dBm | 77mW
16.5-19 dB | -26 dBm | 69 mW
Gain Variation | P1 dB compression point(worst case) | Power Consumption(worst case)
19-22 dB | -28 dBm | 85mW
 | -26 dBm | 77mW
 | -26 dBm | 69 mW
Switch Amplifier 1 is used
switch amplifier 2 is used

## Slide 6: Next week
Redesigned and Optimization of Front end with mixer
Layout
Verification of components in SONNET