## Slide 1
ECE 5220 RFIC Technology & Design (Noise)

## Slide 2: Noise (introduction)
The broadest definition of noise is “everything except the desired signal”.
In practice, the term “noise” is used to refer to “random noise” having Gaussian distribution of its amplitude.
In a strict sense “Interferer” is not random noise, but artificial man-made noise.
Before the early 1900’s, it was widely thought that the sensitivity of a system can be simply improved by cascading amplifiers with finite gain.
Input
Output

## Slide 3: Noise (introduction)
When it became possible to design amplifiers with enough gain using vacuum tubes in the early 1900’s, it was observed that simply cascading amplifiers did not improve the sensitivity of the system.
Input
Output
The degradation of the sensitivity of the system is observed as a continuous “hiss” in audio systems and a characteristic “snow” in video systems.

## Slide 4: Noise (introduction)
Nyquist, Johnson and Schottky were the first to publish a series of papers which carefully measuring and explaining the origin of noise.
The existence of noise in electronics is basically due to the fact that the movement of electrical carriers (electrons and holes) is not continuous, but discrete, and they have randomness in movement due to thermal energy and defects in semiconductor.
Study of noise is important because it allows us to determine the lower limit to the size of signal that can be detected.
Types of noise (covered in the lecture):
- Thermal noise
- Shot noise
- Flicker noise (1/f noise)

## Slide 5: Quantifying Noise Power
Let’s think about how to quantify random noise Xn(t) which can be either random voltage or current signal.
Xn(t)
Random noise is unpredictable, but one thing well-known is that its time average is zero.
So, we need a different way to quantify the noise. Let’s mean square-value of Xn(t).
Because most noise is real quantity.
This is called mean-square power (or just power) of Xn(t)
(with respect to 1W).

## Slide 6: Quantifying Noise Power
Apparently, mean-square power of Xn(t) is not zero, but it’s still difficult to calculate because of infinite time integral.
Xn(t)
Any easy way ? Well, let’s try it in an experimental way. First, imagine a tunable bandpass filter where center frequency fo is tunable and passband BW is 1Hz having brick-wall type ideal unity gain response (mental model).
Transfer function (|Vo/Vi|)
Then apply the square of noise Xn(t) to the input of the filter.
Hz

## Slide 7: Quantifying Noise Power
|Vo/Vi|(fo is tunable.)
Xn(t)
Output frequency response (magnitude)
Now, you can measure frequency response of the X2n(t) for every frequency per 1Hz step.
Hz
This is basic concept of “power spectral density or power spectrum Sx(f)” of Xn(t).
Once Sx(f) is known, power can be calculated by integrating Sx(f) over the frequency band of interest (fL-fU).
Power spectral density [V2/Hz] or [A2/Hz]
Hz
Sx(f)

## Slide 8: Quantifying Noise Power
In reality, it’s impossible to have 1Hz BW tunable bandpass filter.
Alternatively, we take sufficient number of Xn(t) for a sufficient amount of time period T. Then take Fourier transform of each sample and calculate power of each sample in frequency domain. Finally average all the power. This gives approximate of real power spectral density of Xn(t).
T
T
T
0
0
0
f
f
f
f
f
f
f
Energy
Power

## Slide 9: Resistor Thermal Noise
If ambient temperature is not absolutely zero, then there is thermal energy everywhere (“Blackbody radiation”). In semiconductors including resistors, electrons (and holes) will be agitated by this thermal energy, which causes random movement of the carriers. This is the basic source of noise current (and therefore, noise voltage) in resistors.
time
This fundamental physical phenomenon because discrete movement of electron charges. You will see later that this kind of noise also appears in antennas, which is basic noise source from the antennas.
Some different names of thermal noise: Johnson noise, Nyquist noise

## Slide 10: Resistor Thermal Noise
time
It is know that the power spectral density of the resistor thermal noise, Vn(t), is given as:
h: Plank’s constant = 6.2 x 10-34 J∙sec
k: Boltzman constant = 1.38 x 10-23 J/K
T: Absolute temperature = (273+oC) K
Df: Bandwidth (Hz)
This assumption is valid for most of RF IC designs.
Apply this.

## Slide 11: Resistor Thermal Noise
time
It is know that the power spectral density of the resistor thermal noise, Vn(t), is given as:
f
-f
Sn(f)
2kTR
f
-f
Sn(f)
4kTR
We call this as
“double sided spectrum”
We call this as
“single sided spectrum”
(standard convention)
Note: No frequency dependency (white noise)

## Slide 12: Resistor Thermal Noise - Modeling
time
Now, let’s define noise power and effective noise voltage:
Now, we can model resistor thermal noise as voltage source (Thevenin form) or current source (Norton form):

## Slide 13: Resistor Thermal Noise - Modeling
Rule of thumb:
1 kW, T=300 K, Df=1 Hz, Vn=4 nVrms
50 W, T=300 K, Df=1 Hz, Vn=1 nVrms
Example:
Consider a 50-W wireless system with 1 MHz signal bandwidth. The noise voltage from a 1 MHz BW for a 50-W resistor is 1nVrms x 1000=1uVrms. Therefore, the signal voltage with a BW of 1MHz needs to be more than 1uV to be detectable.

## Slide 14: Noise Algebra
Now, let’s add two resistors in series. Then, how much is the overall noise voltage (Df=1Hz) ?
Don’t calculate like this:
Why ?

## Slide 15: Noise Algebra
Now, let’s add two resistors in series. Then, how much is the overall noise voltage (Df=1Hz) ?
When adding two noises, we need to consider correlation between the noises.
These terms will be zero, because noises from R1 and R2 are not correlated; i.e., time average of multiplication of two uncorrelated noise samples will be zero.
Note: we have to add noise in power domain or resistance, not voltage.

## Slide 16: Shot Noise
Noise source: any electron (e-) and hole (h+) has slightly different random energy level (not uniform energy). These different energy level causes randomness in the # of carrier hopping the energy barrier in the P-N junction under forward biasing.
Current
Time
PSD
Freq.
ID
These randomness of # of carriers (e-, h+) arriving at the contact generates random noise pulse of current.
Note: this is white noise and has Gaussian distribution.

## Slide 17: Shot Noise
Condition for shot noise:
There must be DC current flow.
There must potential barrier (P-N junction) over which a charge carrier hops.
Any diode and P-N junction device exhibits shot noise current. Noise of diode can be represented by a noise current source in parallel with the diode as shown in figure below.
+
-
Ex) Rule of Thumb:
- 1mA of DC current produces 18 pA/√Hz of rms noise current density.
- 1mA of DC current produces 18 nA of rms noise current of a BW=1MHz.

## Slide 18: Flicker Noise
Condition for flicker noise: Flow of DC current
Flicker noise is caused by the randomness of being captured (recombination) and released (injection) of charge in a crystal defect states (traps).
Ex) In diode/BJT, P-N junction depletion region has some contamination and crystal defects, which play as trap states.
Ex) In MOSFETs, the interface between the gate oxide and the silicon substrate contains many dangling bonds acting as trap sites.
The traps capture and release carriers in a random fashion, and the time constants associated with the process give rise to the 1/f nature of the noise power spectral density (mostly low-frequency dominant noise).
PSD
Freq.
Kf, af, ef will be depending on fabrication process (but mostly ef ~ 1).
It is observed that in typical IC process, BJT exhibits less 1/f-noise than CMOS.

## Slide 19: Flicker Noise in Junctions
Flicker noise in a forward biased junction can be expresses as:
A more complete noise model of a forward biased diode is shown below:
+
-
Total flicker noise in a bandwidth from f1 and f2 is (assume af=ef=1):
PSD
Freq.
f1
f2

## Slide 20: Flicker Noise
Total flicker noise in a bandwidth from f1 and f2 is (assume af=ef=1):
PSD
Freq.
f1
f2
Same ratio of frequencies gives same 1/f-noise. For example, 1/f-noise in a bandwidth from 30 Hz to 300 Hz is the same as the noise in a bandwidth from 300 Hz to 3000 Hz.
More specifically, the 1/f-noise is constant for decade of frequency.
Ex) diode area A=1um x 1um, IDC=1mA, BW=10-100 Hz, then

## Slide 21: Antenna Noise
Previous discussion allows this simple modeling of antenna in terms of signal for RF IC designs.
Rs is not real resistance, but called as “radiation resistance”.
For 50-W system, Rs=Zo=50 W
For 75-W system, Rs=Zo=75 W
A
B
A
B
Vs is an effective open source voltage induced in antenna.
Vs,far is an equivalent source that generate E-field in the far-field air medium.

## Slide 22: Antenna Noise
We need to consider one more thing in this modeling.
In real world,
Antenna receives not only signal energy but also noise energy.
Recall that every object above absolute temperature emits thermal energy which will be noise energy if it’s not coming from the signal (“Blackbody radiation”).
Signal
Noise
A
B
A
B
Q) How can we model the antenna noise ?

## Slide 23: Antenna Noise
Noise
Blackbody
(noise source surrounding antenna area)
Let’s assume that the antenna is facing a blackbody with a temperature Tant.
The carriers in the antenna are thermally agitated by the radiation from the blackbody source.
It is known that the available noise power depends on the temperature of the blackbody and BW of the system under Z-matched condition.
k: Boltzman constant = 1.38 x 10-23 J/K
T: Absolute temperature = (273+oC) K
Df: Bandwidth (Hz)

## Slide 24: Antenna Noise
Noise
Blackbody
(noise source surrounding antenna area)
The noise from the antenna can be modeled as a voltage source in series with the matched impedance.
+
-
The equivalent noise voltage can be determined by this equation.

## Slide 25: Antenna Noise
Noise
Blackbody
(noise source surrounding antenna area)
The noise from the antenna can be modeled as a voltage source in series with the matched impedance.
+
-
Q) How do we determine Tant ?
Ans) Normal convention is to take ambient temperature, i.e., Tant=300 K. But in reality, it could be a bit higher due to cosmic rays from outer space.
Note that the equivalent noise voltage is the same form as in that of noisy resistor, although Zo is not physical resistor.

## Slide 26: MOSFET Noise Model
The channel resistance of MOSFET exhibits thermal noise just like a normal resistor, and causes drain thermal noise current.
gm: transconductance,
g: drain thermal noise coefficient (~2/3 for long channel,
> 3-4 for short channel device)

## Slide 27: MOSFET Noise Model
Atomic bonds at the interface of gate oxide and silicon substrate is not perfect, but there are many dangling bonds which plays trap states. These traps give rise to flicker noise.
Dangling bonds play as traps
Refer to gate side

## Slide 28: MOSFET Noise Model
Drain noise current has two components; channel thermal noise and 1/f –noise.
Drain current noise PSD (dB)
Freq.
fc
Ex) Kf=3x10-24 V2∙F (for 0.18 um CMOS)
Cox=1 uF/cm2 (for 0.18 um CMOS)
W= 60 um, L=0.18 um
gm=20 mS
 fc ~ 10MHz

## Slide 29: MOSFET Noise Model
In actual layout of MOSFET, the gate is made of poly silicon which has a finite resistance. The parasitic resistance generates its own thermal noise.
Gate
Drain
Source
Finite resistance in poly silicon gate
Rg

## Slide 30: Small Signal MOSFET Model (with noises)
Now, we can generate first-order small signal model for noise analysis of MOSFET (for high frequency applications).
You can drop this term to simplify analysis.
If your circuit is operating above fc, then you can drop this term in noise analysis.

## Slide 31: Equivalent Input Noise Generators
We want to represent a noisy 2-port by a noiseless 2-port with equivalent noise source(s) outside the 2-port network, as shown below.

## Slide 32: Equivalent Input Noise Generators
Let’s start with introducing an equivalent noise voltage source. Where can we put such a noise source? First let’s try to put the noise voltage source in parallel with the 2-port network.
What’s the problem in this configuration?
Let us put the noise voltage source in series with the 2-port network.

## Slide 33: Equivalent Input Noise Generators
The equivalent noise source should be able to generate the equivalent noise power at the output port regardless of the input drive source and the output termination conditions.
What if Zs=∞ ?
If Zs=∞, then the noise voltage can play nothing, and output noise power will be zero. Clearly this not the case for all noisy 2-port networks. For instance, in CMOS, even though the input is open, there would be output noise current as long as it is biased. Therefore, using Vneq as the only noise generator is inadequate.

## Slide 34: Equivalent Input Noise Generators
Let’s introduce a noise current source in series with noise voltage source.
Let us put the noise current source in parallel with the 2-port network.
Then, the noise current source will block any signal current from source, not to mention the noise voltage source (not acceptable).

## Slide 35: Equivalent Input Noise Generators
Now, let’s check the model.
All the signal current will go to the 2-port network.
If Zs=0, Vneq will generate output noise (ineq will do nothing).
If Zs=∞, Ineq will generate output noise (Vneq will do nothing).
If 0<Zs<∞, both Vneq and Ineq will participate to generate output noise.
The model is working fine, but we missed just one thing here, which is correlation between Vneq and Ineq. We will see later how we should handle the correlation between the two noise amounts.

## Slide 36: Equivalent Output Noise Generators
We can represent the equivalent noises at the output side also.

## Slide 37: Computing Equivalent Input Noise Sources
How would we compute the equivalent noise voltage and current for a given noisy 2-port network ?
Computing Vneq :
Set Zs=0 and Vs=0 for both networks. Under this condition, ineq plays no role.
Calculate output noise in the original network
Calculate output noise in the equivalent network due to Vneq.
By equating these two noise amount, Vneq can be determined.

## Slide 38: Computing Equivalent Input Noise Sources
How would we compute the equivalent noise voltage and current for a given noisy 2-port network ?
Computing ineq :
Set Zs=∞ for both networks. Under this condition, Vneq plays no role.
Calculate output noise in the original network
Calculate output noise in the equivalent network due to ineq.
By equating these two noise amount, ineq can be determined.

## Slide 39: MOSFET Equivalent Input Noise Generators
As an example, let’s compute input equivalent noises in NMOS.

## Slide 40: MOSFET Equivalent Input Noise Generators
First let’s find ineq. In order to do that, open Gate and Source for both cases.
(1)=(2),

## Slide 41: MOSFET Equivalent Input Noise Generators
Next let’s find vneq. In order to do that, short Gate and Source for both cases.
Short
Short
(1)=(2),∴

## Slide 42: MOSFET Equivalent Input Noise Generators
Now we calculate equivalent noise voltage and current sources in NMOS. But the noise sources have correlation part with each other.
Correlation parts
Later, we will come back to this correlation issue to minimize noise of a system.

## Slide 43: Input Referred Noise
This is general representation of input equivalent noises, which will be valid at any input source impedance.

## Slide 44: Input Referred Noise
However, if input source impedance is clearly known, then the noisy 2-port network can be represented as:
Equivalent noise voltage in series with noiseless 2-port, or
Equivalent noise current in parallel with noiseless 2-port.
This is called input referred noise. And for many case of RFIC designs, we just input referred noise for analysis.

## Slide 45: MOSFET Input Referred Noise
Most case of RFIC designs, input source and output load impedances will be defined clearly.
Input referred voltage noise

## Slide 46: MOSFET Input Referred Noise
Assume, Vs=0, RL=noiseless.
(1)=(2),∴

## Slide 47: Noise Factor
What we have been investigating is to model the noisy 2-port network with input equivalent noise sources or input referred noise sources.
input equivalent noise sources : when input source impedance is not clearly defined.
input referred noise sources : when input source impedance is clearly defined.
Next topic is to characterize the noise of the 2-port network using single number.

## Slide 48: Noise Factor
Let’s start with an example (assume RL is noiseless, but Rs is noisy).
noiseless
Apparently there is no additional noise from amplifier.
Now it’s noiseless.
noiseless
Now it’s noiseless.
Output noise due to input noise source only
Output noise by the noisy amplifier

## Slide 49: Noise Factor
Now, let’s take output noise power ratio of (1) and (2) in previous slide.
This is basically noise factor of the amplifier.
Noise factor (F) definition:
Meaning of noise factor (F) : Noise factor is a measure of relative amount of noise added by a 2-port noisy network, compared with the noise added by the source.

## Slide 50: Noise Figure
Noise Figure (NF) is just dB-scale of noise factor (F).
(dB)
Rule of thumb
Noise Factor (F) | Noise Figure (NF) | Meaning
1 | 0 dB | No noise in the 2-port
1.5 | 1.76 dB | The 2-port will add 50% of the noise added by the input noise source
2 | 3 dB | The 2-port will add the same noise amount as input noise source
Typical LNA NF performances
CMOS, SiGe : 2~3.5 dB (with gain > 20 dB)
GaAs, InP: 1 ~ 2 dB (very good designs <1 dB, with gain > 20 dB)

## Slide 51: Another Definition of Noise Factor
Another way of defining noise factor (F): it’s just different way of same meaning.
SNRin
SNRout
Sin: input signal power
Sout: output signal power
Nin: input noise power
Nout: output noise power
Ap: power gain of 2-port network
This gives short-cut to calculate noise factor (see next page).

## Slide 52: Short Cuts to Noise Factor (from Input Referred Noise)
Recall that if source impedance is well defined, the noisy 2-port network can be represented with input referred noise voltage or current.
Input noise voltage due to Zs
Input noise current due to Ys
Thevenin form
Norton form
F
F

## Slide 53: MOSFET Noise Factor
Previously we calculate input referred noise voltage of NMOS.
F
apply
F
Ex) If you apply, Rs=50W, Rg=3W, g=3.5, w=2px2.5 GHz, W=180um, L=0.18um, Cox=1uF/cm2 (for 0.18um CMOS), Cgs=2/3 CoxWL=324 fF, gm=60mS,
then, F=2.31, NF=10log(F)=3.64 dB.

## Slide 54: MOSFET Noise Factor
Let us think about how we can minimize F.
F
From the noise factor equation, we can observe that in order to minimize F,
Increase gm (more current  more power consumption).
There is optimum Rs where F can be minimized, which can be found by this equation:
Ex) If you apply, Rg=3W, g=3.5, w=2px2.5 GHz, W=180um, L=0.18um, Cox=1uF/cm2 (for 0.18um CMOS), Cgs=2/3 CoxWL=324 fF, gm=60mS,
then, Rs,opt=201.5W, F=1.62, NFopt=10log(F)=2.1 dB.
This result is a lot better than previous one. Can we do better?

## Slide 55: Classical 2-Port Noise Theory (intro)
As we have seen in the previous example, there is optimum source impedance, Zs, where noise factor will be minimized for a given noisy 2-port network.
How can we find the optimum Zs? To answer this question, we need to develop a classical 2-port noise theory.

## Slide 56: Classical 2-Port Noise Theory (1)
First, let’s draw noisy 2-port network with equivalent input noise sources.
Next, apply input source with Norton equivalent form (Ys: source admittance, is: noise current from the source admittance) .
Then let’s change whole input part in Norton form.

## Slide 57: Classical 2-Port Noise Theory (2)
Then let’s change whole input part in Norton form.
Let’s calculate noise factor of the system.
In this equation,
is and in are not correlated.
is and vn are not correlated.
vn and in are correlated.
We need to develop some math to handle this correlation.

## Slide 58: Classical 2-Port Noise Theory (3)
Let’s decompose in into two components.
: noise component correlated to
: noise component uncorrelated to
Now let’s define correlation admittance as:
How can we calculate Yc?
This term will go zero because of no correlation.

## Slide 59: Classical 2-Port Noise Theory (4)
Let’s substitute the equations in the previous page into noise factor equation.
Now let’s define these variables.
These are just change of variables.
These are decomposition of source admittance and correlation admittance.
Apply these variables into noise factor equation (the result is in next slide).

## Slide 60: Classical 2-Port Noise Theory (5)
When new variables applied into the noise factor equation,
Remind that all the objective of these mathematics is to find optimum Ys=Gs+jBs to minimize the noise factor.
Clearly to minimize F,
1. Bs=-Bc (possible)
2. Gs=-Gc (not possible, why?).

## Slide 61: Classical 2-Port Noise Theory (6)
The condition on Gs for optimum noise factor can be found by differentiating the F with respect to Gs and setting it to zero.
The condition for source impedance for minimum noise factor can be summarized as:
=

## Slide 62: Classical 2-Port Noise Theory (7)
By substituting the Ys,opt into the noise factor equation, we can get minimum noise factor of a system.
=
A general equation of noise factor can be expressed using the Fmin as:.

## Slide 63: Classical 2-Port Noise Theory (summary)
Find input equivalent voltage and noise current sources.
Find correlation admittance.
Find uncorrelated noise current.
Find Rn & Gu.
Compute Gs,opt & Bs,opt
=
Calculate Fmin & F
=

## Slide 64: MOSFET Minimum Noise Factor (step-1)
Find input equivalent voltage and noise current sources.
Assume Rg <<1/wCgs
We already computed these noise amounts.

## Slide 65: MOSFET Minimum Noise Factor (step-2 & 3)
Find input equivalent voltage and noise current sources.
Find correlation admittance.
Assume gmRg <<1
Find uncorrelated noise current.

## Slide 66: MOSFET Minimum Noise Factor (step-4 & 5)
Find input equivalent voltage and noise current sources.
Find correlation admittance.
Find Rn & Gu.
Find uncorrelated noise current.
Compute Gs,opt & Bs,opt
=
=
-

## Slide 67: MOSFET Minimum Noise Factor (step-6)
Find input equivalent voltage and noise current sources.
Find correlation admittance.
Find Rn & Gu.
Calculate Fmin
=
Ex) If you apply, Rg=3W, g=3.5, w=2px2.5 GHz, W=180um, L=0.18um, Cox=1uF/cm2 (for 0.18um CMOS), Cgs=2/3 CoxWL=324 fF, gm=60mS,
then, Gs,opt=1.154 mS, Bs,opt=-5.1 mS, Fmin=1.136, NFmin=10log(Fmin)=0.55 dB.

## Slide 68: MOSFET Noise Matching
Rg=3W, g=3.5, w=2px2.5 GHz, W=180um, L=0.18um, Cox=1uF/cm2 (for 0.18um CMOS), Cgs=2/3 CoxWL=324 fF,
gm=60mS
NF: 3.64 dB
NF: 2.1 dB
NF: 0.55 dB
For a given bias condition and device parameters, there is optimum source impedance, Zs,opt (Ys,opt) where F (NF) is minimum.
Matching source impedance to Zs,opt is called “noise matching”.
Usually it’s difficult to match source impedance to optimum noise point and maximum power transfer at the same time.
We will study how to handle this issue in LNA design section.

## Slide 69: Cascaded Noise Factor (General Case)
Until now, we have focused on characterization of single-stage 2-port network. Let’s continue computing NF of multiple cascaded system.
Let’s think about noiseless 2-port network with applying signal source.
Simply, we can model the noiseless 2-port network using parameters, input impedance (Rin), output impedance (Rout) and voltage gain (Av).

## Slide 70: Available Power vs. Transducer Power (review)
Before continuing further, let’s review available power gain (Pav) and transducer power gain (PL)
rms value
Available power (Pav)
The possible maximum power deliverable to a load
Happens when Rs=RL (matched condition).
=
Depends on source impedance only.
Transducer power (PL)
Actual power delivered to a load
=
Depends on both source and load impedances.
=

## Slide 71: Available Power Gain (Gav)
Let’s calculate available power gain (Gav) in the first stage.
=
=
=
Note that available power is only dependent of source impedance, since it is assumed matched condition.

## Slide 72: Transducer Power Gain (GT)
Let’s calculate available power gain (Gav) in the first stage.
=
=
=
=
Apparently, if Rout1=Rin2, then, Gav=GT.

## Slide 73: Cascaded Noise Factor (General Case)
Let’s consider noisy cascaded 2-port network.
Vin1
Vin2
Thevenin equivalence

## Slide 74: Cascaded Noise Factor (General Case)
Now let’s calculate Vin2.
Vin1
Vin2
Thevenin equivalence

## Slide 75: Cascaded Noise Factor (General Case)
From previous results,
Noise voltage :
Noise power :
Cascaded Noise Factor (F) :

## Slide 76: Cascaded Noise Factor (General Case)
F
==
=
=
=
1st-stage F
Change this in terms of available power gain of 1-st stage , Gav1.
Note that 2nd –stage noise is divided by available power gain of the 1-st stage.

## Slide 77: Cascaded Noise Factor (General Case)
F=
=
Another form of noise factor of cascaded system
Change this in terms of transducer power gain of first stage.
Using the 2-stage cascaded noise factor expression, you can verify this Frii’s Formula.
=

## Slide 78: Some Noise Considerations in Cascaded System
=
Each stage in a cascaded system adds noise to the system. As a consequence of this SNR gets worse toward the end of the cascaded chain. And therefore, if SNR drops below acceptable range in intermediate stage, you should stop the design, and rethink the design.
In typical RF systems, the first few stages set overall noise level of the system. This is particularly the reason why the noise performance of LNA and mixer is very crucial in determining the NF of the system.

## Slide 79: Cascaded Systems and Noise Margin
=
=
In cascading two systems, the choice of optimum arrangement for low-noise is simple.
Compare and pick the arrangement giving less noise factor.

## Slide 80: Cascaded Systems and Noise Margin
But when cascading many blocks, we need to consider many different combination of the arrangement of each block, and the choice is time consuming work.
A generalized technique to resolve this issue is to consider “noise margin” of each building block and place the block having lower noise margin first in cascading the systems.

## Slide 81: Cascaded Systems and Noise Margin
What is noise margin (NM) ?
Noise power
Freq
Ni
No
D1
No=GxNi
Noise power
Freq
Ni
No
D2
No=GxNi+Nadded
Nadded
=
Once we know F & G of each block, we can figure out NM of the block.
To achieve minimum F, place the block with lower NM first (verify this claim !).

## Slide 82: Loss of Filters and T-lines
In typical RF systems, a filter will be placed before LNA to filter wanted signal band, and it typically has a loss, L (< 2-3 dB).
Zo=50 W
Zo=50 W
How to define loss L in passive filter ?
=
=
Rs=RL=Zo=50 W
This is Vin of the duplexer.
Loss of transmission lines can be defined using the same way.

## Slide 83: Loss of Attenuator
Attenuator is a resistor network whose input and output impedance are matched to Zo (=50 W), and signal power is attenuated by a specific number.
Rs=RL=Zo=50 W
Attenuator
Zin
Zout
Vin=1/2 Vs
+
-
VL
=
Ex) Rx=8.55 W, Ry=141.9 W, will give Zin=Zout=50 W, and L=3 dB.

## Slide 84: Noise Factor of Attenuator
Let’s think about noise factor of attenuator.
Rs=RL=Zin=Zout=Zo=50 W
Attenuator loss = Pin/Pout=L
Zin
Zout
Vin=1/2 Vs
+
-
VL
, where
, where
No change !
Loss=Noise Factor
Q: How should we interpret this ?

## Slide 85: Noise Factor of Attenuator
Noise behaves just like signal and the input noise due to Rs will be attenuated by the attenuator.
Rs=RL=Zin=Zout=Zo=50 W
Attenuator loss = Pin/Pout=L
Zin
Zout
, where
Noise behaves just like signal.
But, the resistors in the attenuator will generate the exactly same amount of noise power lost in the attenuator. In overall there is no noise power loss in the network (Proof of this is HW).

## Slide 86: Noise Factor of Passives
Both have loss factor (L).
In general under matched condition, duplexer and T-line having a loss can be modeled as attenuator within passband frequency range.
And we can apply the same theory developed in previous slides, and confirm that the loss factor L is the noise figure of the passive devices.
Generally speaking, under matched condition noise power delivered to a load from a pure passive device will be KTDf.

## Slide 87: Minimum Noise Floor of Receiver
Minimum Noise Floor
Noise factor of receiver
Noise power from antenna
Noise power
Freq
Ni
Min. Noise Floor=Ni x F
The minimum noise floor of a receiver is total noise power which is noise power from antenna plus equivalent input noise power of a receiver.

## Slide 88: Minimum Detectable Signal (MDS)
In typical wireless comm., we need certain level of signal to noise ratio for an acceptable bit-error-rate required by a system. We call this SNRmin ( typ. 10-20 dB).
Noise power
Freq
Ni
Min. Noise Floor =Ni x F
SNRmin
MDS=Ni x F x SNRmin
This means the minimum detectable signal (MDS) for a given system is
MDS= Ni x F x SNRmin.
Ex) Df=2 MHz, T=300 K, F=2 (3dB), SNRmin=10 dB
Ni=KTDf x F= -174 dBm+10log(2MHz) + 3 dB=-108 dBm
MDS=Ni x SNRmin=-108 dB + 10 dB = -98 dBm