## Slide 1
ECE 5220 RFIC HW -1 (Due: 02/06/2012, Hand in by the end of class time, 10:45AM)
Homework will still be acceptable by 4:30PM (office hour) 02/06/2012 after class with 20% degradation of the point you would earn otherwise.

## Slide 2: Problem-1: Power penalty for mismatch
When load impedance is not perfectly matched to source impedance, calculate power reduction factor (PL/Pmax) for the mismatch.
Derive output power (PL) delivered to load resistance RL under the mismatched condition.
Derive a power reduction factor, which is a ratio of PL/Pmax , where is Pmax is the maximum power deliverable to load under perfect matched condition.
Based on the result in 2), fill in empty column in table below.
DXs/Xs | PL/Pmax (%)
5% | 
10% | 
20% | 
50% | 
Assume DRs=0 | 
DRs/Rs | PL/Pmax (%)
5% | 
10% | 
20% | 
50% | 
Assume DXs=0 | 

## Slide 3: Problem-2: Power penalty for inductor loss
Definition:
Assume that inductor in the matching circuit shown below has finite resistance, Rind.
Derive output power (PL) delivered to load resistance RL under the finite Qind of inductor.
Derive power (Pind) delivered to Rind.
Derive efficiency defined by
Express in terms of QT and Qind.

## Slide 4: Problem-3: Power penalty for inductor loss
Definition:
Repeat the same problems in Problem-2 for the case of impedance down conversion shown below figure.
Derive output power (PL) delivered to load resistance RL under the finite Qind of inductor.
Derive power (Pind) delivered to Rind.
Derive efficiency defined by
Express in terms of QT and Qind.

## Slide 5: Problem-4: LNA input matching
In this problem, use only given small signal parameters of NMOS: Rg, Cgs and gm.
Derive input impedance Zin.
Under directly being driven by source, calculate Vgs and output current iout.
Calculate voltage gain
Zin

## Slide 6: Problem-4: LNA input matching
In this problem, use only given small signal parameters of NMOS: Rg, Cgs and gm.
4) Assume that real part of Zin in 1) is equal to Rs. Design lossless matching network for maximum power transfer (assume woL < 1/(woCgs), where wois target frequency for matching ).
5) Under matched conditions, calculate Vgs and output current iout.
6) Calculate voltage gain , and compare the result with that of 3).
7) Explain the role of source inductor Ls in view of impedance matching.
lossless