## Slide 1
ECE 5220 RFIC HW -2 (Due: 03/05/2012, Hand in by the end of class time, 10:45AM)
Homework will not be acceptable after the class.

## Slide 2: Problem-1: Noise concept
Assumption: Temperature T=300 K.
Calculate effective noise voltage Vo.
How often will the magnitude of the noise voltage be greater than 88 mV? (you may need a numerical calculator for compute probability, or alternatively you can use a Gaussian distribution table which is uploaded in the “resource” part of “Scholar class website”.)
Ideal bandpass filter (noise BW=25 MHz)
This resistor is inside a “boiling water “(T=373 K).
This resistor is inside a “dry-ice bath” (T=194 K).
3) Compute net power flow and direction of the system shown in left side.

## Slide 3: Problem-2: Noise consideration in lossy network
Calculate noise power delivered to load by the source resistor only.
Calculate noise power delivered to load by each of three resistors in the attenuator one by one.
From 1) and 2), verify that noise power keep constant between input and output of attenuator.
Verify that noise factor, F=L (L=loss).
Numerical example: Repeat 1)-4) when Ro=50W, Rx=8.55W, Ry=141.9W.
Assumption: RL is noiseless.

## Slide 4: Problem-3: BJT noise factor calculation
BJT can be modeled as shown in the figure at RF, where Rb is base resistance Vnb is the effective noise voltage from the base resistance, and inb and inc are effective shot noise current from bias currents of IB and IC, respectively.
Calculate input referred noise (assume RL is noiseless).
Calculate noise factor of the system.
Noisy BJT model at RF
Source noise
Assumption: RL is noiseless.

## Slide 5: Problem-4: NF Measurement (1)
Driving source (voltage)
Let’s do some mental experiment to measure noise factor (F) of the device under test (DUT). The only known factor of the DUT is input and output impedance which are matched to Ro, and available power gain, G.
Step-1) make Vs=0, then measure out put power delivered to load, RL.
Step-2) turn on Vs, and adjust Vs so that your output power delivered to RL can be twice of the power in Step-1.
Q) Calculate F from the results in Step-1 and Step-2 (assume DUT bandwidth is Df).
Assumption: RL is noiseless.

## Slide 6: Problem-4: NF Measurement (2)
Driving source (current)
IDC
RDC
Noisy diode having shot noise current (no flicker noise).
Let’s do similar mental experiment to measure noise factor (F) of the device under test (DUT). The only known factor of the DUT is input and output impedance which are matched to Ro, and available power gain, G (now, you don’t know the DUT bandwidth).
Step-1) turn on switch and no DC current. Then measure out put power delivered to load, RL.
Step-2) turn off the switch and adjust VDC so that your output power delivered to RL can be twice of the power in Step-1.
Q) Calculate F from the results in Step-1 and Step-2.
(Note: You don’t need to know the gain of the DUT either in this method.)
Assumption:
RL is noiseless.
Diode output resistance is much larger than Rs.
C: blocks DC current and passes all noise current from diode.
L: blocks any noise current from RDC and pass DC current from VDC.

## Slide 7: Problem-5: Inductively degenerated LNA
Assumption:
RL is noiseless and no flicker noise in NMOS.
No drain-gate parasitic capacitance, Cgd.
Rg << 1/wCgs
gmRg << 1
Calculate equivalent input noise generators (voltage and current generators).
Calculate input referred noise (voltage or current) with an assumption of source impedance of Rs.
Calculate correlation admittance between the voltage and current noises in 1), and separate the current noise into correlated and uncorrelated parts.
Find optimum admittance for minimum F.
Find expression for Fmin.

## Slide 8: Problem-6: Common-gate LNA
Calculate equivalent input noise generators (voltage and current generators).
Calculate input referred noise (voltage or current) with an assumption of source impedance of Rs.
Calculate correlation admittance between the voltage and current noises in 1), and separate the current noise into correlated and uncorrelated parts.
Find optimum admittance for minimum F.
Find expression for Fmin.
Assumption:
RL is noiseless and no flicker noise in M1 and M2.
No drain-gate parasitic capacitance, Cgd.
gm of M1=gm1, gm of M2=gm2.
Cgs of M1=Cgs1, Cgs of M2=Cgs2.
Rg << 1/wCgs (for M1 and M2)
gmRg << 1 (for M1 and M2)