## Slide 1: Introduction to SPECTRE
ECE 4220 Analog IC

## Slide 2: Configuring access to the CAD and Visualization Lab
Establish a user account with the CAD and Visualization Lab (CVL) at http://computing.ece.vt.edu/wiki/Getting_Started.
  Under How to Set Up An Account with CVL, click link to create or change your CVL Accounts to set up your CVL account.
  Under Main Page Info, click How to gain Remote Access to the CVL over the Internet and follow the instructions for your operating system.
  WINDOWS SYSTEMS ONLY
    Follow installation instructions for Xming and PuTTY on http://computing.ece.vt.edu/wiki/How_to_gain_Remote_Access_to_the_CVL_over_the_Internet
    Enter the data as stated on the link above; the screenshots below show the proper settings. When you are done, type a meaningful name like ECE4220 into the box below Saved Sessions and click Save.

## Slide 3: Accessing Cadence Spectre software in the CAD and Visualization Lab
Verify that Xming is running by checking for its icon in the task manager.
Start PuTTY, and double click session ECE4220.
Enter your CVL login and password at the prompt.

## Slide 4: First Time Cadence Spectre Users
Enter the commands shown in the window below to
Create a directory for class projects
Copy the design library into the directory
Enter the directory
Verify that the design library has been copied
You will use this directory for class projects.

## Slide 5: Starting Cadence Spectre
After logging in, navigate to the ECE4220 directory
Type the following case-sensitive commands at the prompt
  tcsh
  source CA18_ece4220.cshr
  cdsprj CA18prjs
  Cadence
  icfb &

## Slide 6: Setting Library Path
Click Tools->Library Manager
Click on your library: CA18Prjs_yourPID

## Slide 7: Creating a New Schematic
Opening Schematic Window:
Click File->New->Cellview.
Enter a Cell Name and click OK.
A schematic window opens.

## Slide 8: Adding Circuit Elements
Circuit elements can be added by either way of:
Clicking the Instance button on the left side of the window.
Pressing the letter i on the keyboard.

## Slide 9: Adding a Circuit Element Instance
Select the library by clicking Browse.
For this example, we want a DC voltage source.
  Click analogLib->Independent->vdc->symbol
  Click Close.

## Slide 10: Placing a Circuit Element Into the Schematic
The circuit element can be placed into the schematic using the left mouse button.
To stop placing a component, press the Esc key.
Pressing R on the keyboard will rotate the component by 90 degrees.
To edit the component properties, click on the component to highlight it and press Q on the keyboard.

## Slide 11: Completing the Schematic
Complete the schematic diagram by selecting components from the appropriate libraries and placing them.
Wire the components together by clicking and dragging from one red node to the next.
After drawing schematic, press the Check and Save icon on top left pane.

## Slide 12: DC Analysis - Simulation
Go to tools.
Select “Analog Environment”.

## Slide 13: DC Analysis - Simulation
(1)
(1)
(2)
(2)
(3)
Doing analysis
: Choose analysis type.
: Define the value if you have variables.
: Select “Netlist and Run” for simulation.
Give start-stop value.

## Slide 14: DC Analysis - Sweep
Steps for sweep simulation
: Choose analysis type.
: Define the value if you have variables.
: Select “Netlist and Run” for simulation.
Give sweep range.

## Slide 15: DC Analysis - Results
Results -> Direct Plot -> Main Form
Select the function you want.
Click a node on schematic.

## Slide 16: AC Analysis - Simulation
Draw schematic. (See Fig. 1.)
Go to tools -> Analog environment -> Analysis -> Choose analysis -> ac -> Specify sweep variable, give sweep range and sweep types. (See Fig. 2.)
Select ac in the window that pops up.
Give sweep variable, sweep range and sweep type.
Outputs -> To be saved -> select on schematic.
Select simulate -> Netlist and run. (See Fig. 3.)
Select results -> Plot output. (See Fig. 4.)

## Slide 17: AC Analysis - Simulation
Add vsin instance for AC simulation.
Fig. 1.
Fig. 2.

## Slide 18: AC Analysis - Simulation
Fig. 3.
Fig. 4.

## Slide 19: Tran. Analysis - Simulation
Draw schematic. (See Fig. 5.)
Go to tools -> Analog environment -> Analysis -> Choose analysis
Select tran in the window that pops up.
Give start time and stop time. (See Fig. 6.)
Select options if you need.
Select outputs -> To be saved -> select on schematic.
Select simulate -> Netlist and run (See Fig. 7.)
Select Results -> Plot output (See Fig. 8.)

## Slide 20: Tran. Analysis - Simulation
Define the Freq. value for Tran. Simulation.
Fig. 5.
Fig. 6.

## Slide 21: Tran. Analysis - Simulation
Fig. 7.
Fig. 8.

## Slide 22: Reference
[1] Cadence tutorial from http://ocw.mit.edu/
[2]http://www.mics.ece.vt.edu/ICDesign/Tutorials/Cadence/analog_pg1.html