## Slide 1
ECE 5220 RFIC Technology & Design (Linearity)

## Slide 2: Linearity (introduction)
Pin
GNi
Output Min. Noise Floor =GNi x F
SNRmin
Output MDS=GNi x F x SNRmin
Pout
Pin,min
Pin,MDS
Pin,max
Pout,max
G: Power Gain
Most RF and analog electronics have limited input range where input and output gain has linear relationship.
After certain input power level, output starts to be saturated due to a nonlinearity of a system.
Determined by noise of a system.
Determined by a nonlinearity of a system.
Pin,min=kTDf x F, Pin,MDS=kTDf x F x SNRmin

## Slide 3: Nonlinearity Source (from DC point of view)
Where does the nonlinearity come from? Let’s think about LNA design.
VBias
IBias
VDC
IDC
Linearize NMOS at a bias point.
=
NMOS DC characteristic is non-linear (typically square-law behavior with long channel NMOS).
If applied Vin is small enough (for instance, Vin ~mV range), then the linearization will be valid.
However, if the Vin is getting large (> ~ mV range), then the linearization no longer holds, and the LNA shows nonlinear behavior.

## Slide 4: Nonlinearity Source (from AC point of view)
Where does the nonlinearity come from? Let’s think about LNA design.
These small signal equivalent parameters are nonlinear.
The small signal equivalent parameters are not static, but depending on input and output signals, which causes a nonlinearity of the system.

## Slide 5: Weak & Strong Nonlinearities
Weak nonlinearity
If input and output signal levels are reasonable small (< ~-20 dBm, ~10’s mV), the degree of nonlinearity will not be strong.
This is the most cases of RF and analog front-end receiver blocks; LNAs, mixers baseband amplifiers and filters.
Still, we can characterize the circuits approximately, using small signal model with modeling output current in terms of power series of input Vin.
Strong nonlinearity
If input and output signal levels are large (> 0 dBm, ~100’s mV), the degree of nonlinearity will be quite strong.
This is the most cases of power amplifiers.
We need large signal model and large signal S-parameter to characterize the nonlinearity (we will be back to this issue in power amplifier section).

## Slide 6: Gain Compression (Self-Jamming)
Let’s assume a weak nonlinear system. All weak nonlinear function can be described by a power series.
Nonlinear system
Vin
Vout
≈
Apply
fundamental
2nd –harmonic + DC
fundamental+ 3rd -harmonic

## Slide 7: Gain Compression (Self-Jamming)
Let’s assume a weak nonlinear system. All weak nonlinear function can be described by a power series.
Nonlinear system
Vin
Vout
≈
Apply
fundamental
2nd –harmonic + DC
fundamental+ 3rd -harmonic
Nonlinear system
For most systems, polarity of a3 is the opposite of a1.
Because of this 3rd-harmonic term, gain will be decreased from ideal value.
(“gain desensitization” or “self-jamming effect”)

## Slide 8: Input & Output P1dB Compression Point
We need a parameter to describe the self-jamming effect.
Self-jamming factor
1dB
The input 1dB compression point Pin,-1dB is the input power at which output power drops by 1dB from the predicted output power based on the small signal power gain.
The output 1dB compression point Pout,-1dB is the output power at which output power drops by 1dB from the predicted output power based on the small signal power gain.

## Slide 9: Gain Compression (Adjacent Ch. Jamming)
When a large interference signal is received along with the desired weak signal, the output of the desired signal gets compressed similar to the case of self-jamming. This behavior is referred to as “adjacent channel jamming”.
Nonlinear system
Vin
Vout
≈
t
Fundamental component due to adjacent channel interference

## Slide 10: Gain Compression (Adjacent Ch. Jamming)
Nonlinear system
Vin
Vout
≈
t
Jamming threshold: signal level of wadj where the gain of wanted signal gets reduced by 3dB.
3dB
Adjacent channel input power (dBm)
Wanted channel output power (dBm)
Jamming threshold input power of adjacent channel

## Slide 11: Cross Modulation
Nonlinear system
Vin
Vout
≈
t
Cross modulation is a form of intermodulation, where the amplitude modulation of a strong signal modulates the amplitude of a weak signal at another frequency.
This cross modulated signal is superimposed on top of wanted signal due to 3rd -order nonlinear term of a3.
This is commonly experienced by listener s of AM radio as they drive past a large powerful transmitting station while listening to another AM station. The amplitude modulation of the large transmitting station gets superimposed on top of the station the listener is tuned to.

## Slide 12: Fractional 2nd–order Harmonic Distortion (HD2)
HD2 is defined as the amplitude ratio of 2nd –order harmonic to fundamental component.
Nonlinear system
Vin
Vout
≈
Apply
fundamental
2nd –harmonic + DC
fundamental+ 3rd -harmonic

## Slide 13: Fractional 3rd–order Harmonic Distortion (HD3)
HD3 is defined as the amplitude ratio of 3rd –order harmonic to fundamental component.
Nonlinear system
Vin
Vout
≈
Apply
fundamental
2nd –harmonic + DC
fundamental+ 3rd -harmonic

## Slide 14: Total Harmonic Distortion (THD)
Total Harmonic Distortion (THD) is defined as the sum of all the fractional harmonic distortion terms, i.e.,
THD is often quoted by audio manufacturers who “spec” their amplifiers for spectral purity. The THD values less than 0.1%=-60 dB are hard to discern by the human ear.
In most communication systems, a very narrow bandwidth signal is modulated by very high frequency carrier. In such systems, the second and higher order harmonics lie outside the frequencies of interest and can therefore be easily filtered away.
Easy to filter out 2nd and higher order term.
Audio frequency band: 20 Hz - 20 KHz
2nd and higher order harmonics could reside in audio band and hard to be filtered out

## Slide 15: Intermodulation Distortion (IMD)
Until now we injected single frequency tone into a nonlinear system. But in reality, several other signals closely spaced to the desired signal are received and processed by the front end RF systems; LNAs and mixers.
Typical way of characterizing nonlinearity of RF system is two-tone test; apply two closely spaced frequency tones which have same amplitude into the nonlinear system.
Nonlinear system
Vin
Vout
≈
A
B
C

## Slide 16: Intermodulation Distortion (2-tone test)
A
B
C

## Slide 17: Intermodulation Distortion (2-tone test)
Easy to filter out 2nd and higher order terms.
These IMD tones are folded into signal bandwidth and degrade linearity.
These IMD tones play detrimental role, depending on receiver architecture.
Filtering

## Slide 18: 3rd –order Intermodulation Distortion (IM3)
1
3
Pout (dBm)
Pin (dBm)

## Slide 19: 3rd –order Input Intercept Point (IIP3)
1
3
Pout (dBm)
Pin (dBm)
IIP3 is defined as the signal level at which the extrapolated output signal levels at ws1 (or ws2) and 2ws1-ws2 (or 2ws2-ws1) equal each other. The corresponding output power level is referred to as the third-order output intercept point (OIP3).
Note that the 3rd –order intermodulation distortion corrupts the signal since it falls in the same frequency band as the signal of interest. IIP3 is therefore very crucial for high frequency communication systems.
IIP3
OIP3

## Slide 20: Relating IIP3 to Input P1dB
1
3
Pout (dBm)
Pin (dBm)
IIP3
OIP3
P-1dB
10 dB
Note: IIP3 is two-tone test, while input P1dB is single-tone test.

## Slide 21: 2nd –order Intermodulation Distortion (IM2)
1
2
Pout (dBm)
Pin (dBm)

## Slide 22: 2nd –order Intermodulation Distortion (IM2)
1
2
Pout (dBm)
Pin (dBm)
IIP2 is defined as the signal level at which the extrapolated output signal levels at ws1 (or ws2) and ws2-ws1 equal each other. The corresponding output power level is referred to as the second-order output intercept point (OIP2).
IIP2
OIP2

## Slide 23: 2nd –order Intermodulation Distortion (IM2)
1
2
Pout (dBm)
Pin (dBm)
Note that the second –order intermodulation products are well separated from the frequency band of interest, and therefore they can be easily filtered out.
IIP2
OIP2
However, for certain types of receiver architectures, () can not be filtered out, and IM2 could cause linearity degradation of a system substantially (we will visit this issue in mixer designs).

## Slide 24: Estimating IIP3 Experimentally
1
3
Pout (dBm)
Pin (dBm)
IIP3
OIP3
Nonlinear system
Vin
Vout
Apply input ,Pinput, well below of P-1dB
P-1dB
)
Apply weak two-tone input signals so that output is not saturated, then IIP3 will be calculate as:
Q) Why?

## Slide 25: Estimating IIP2 Experimentally
Nonlinear system
Vin
Vout
)
Apply weak two-tone input signals so that output is not saturated, then IIP2 will be calculate as:
Q) Why?
Apply input ,Pinput, well below of P-1dB
P-1dB
1
2
Pout (dBm)
Pin (dBm)
IIP2
OIP2

## Slide 26: Effect of Feedback on Nonlinearity
Nonlinear system
Vin
Vout
Nonlinear system
Vin
Vout,f
+
Feedback
Negative feedback is often applied to improve linearity of a system.
≈
≈
Without feedback :
With feedback :
-

## Slide 27: Effect of Feedback on Nonlinearity
Nonlinear system
Vin
Vout,f
+
f
≈
≈
Without feedback :
With feedback :
-
=
=

## Slide 28: Effect of Feedback on Nonlinearity




## Slide 29: Effect of Feedback on IIP2
Nonlinear system
Vin
Vout,f
+
f
≈
≈
Without feedback :
With feedback :
-
IIP2 increment factor due to feedback
IIP2 without feedback

## Slide 30: Effect of Feedback on IIP3
Nonlinear system
Vin
Vout,f
+
f
≈
≈
Without feedback :
With feedback :
-
IIP3 increment factor due to feedback
IIP3 without feedback

## Slide 31: Cascaded IIP3
Nonlinear system 1
Vin1
Nonlinear system 2
Vout1= Vin2
Vout2
Overall cascaded nonlinear response:

## Slide 32: Cascaded IIP3
Nonlinear system 1
Vin1
Nonlinear system 2
Vout1= Vin2
Vout2
Overall cascaded nonlinear response:

## Slide 33: Cascaded IIP2
Nonlinear system 1
Vin1
Nonlinear system 2
Vout1= Vin2
Vout2
Overall cascaded nonlinear response:

## Slide 34: Comments on Cascaded Input Intercept Points
Nonlinear system 1
Vin1
Nonlinear system 2
Vout1= Vin2
Vout2
The second stage IIP2 and IIP3 are divided by gain of the first stage. Therefore, linearity of the second stage plays dominant role for the cascaded system.
In general IIP2 & IIP3 of latter stage are divided by all the cascaded gain of preceding stages, and dominate overall linearity performance.
By the same reason, in LNA & mixer cascaded system, mixer linearity tends to be more emphasized than LNA.

## Slide 35: Effective Noise Floor Due to Nonlinearity
The 3rd-order intermodulation outputs contribute additional noise; “unwanted signal” which would degrade the SNR at the output if they become larger than the noise floor.
Nonlinear noisy amplifier
f1
f2
f1
f2
2f2-f1
2f1-f2
The 3rd-order IM tones are basically noise to the system, and their powers can be normalized by the BW, resulting in added noise floor on top of system noise floor.
Net effect of spurious tone is degrading SNR of a system.
System noise floor
Due to 3rd-order IM tones

## Slide 36: Spurious Free Dynamic Range (SFDR)
Pin,min
=kTDf x F
Pin (dBm)
OIP3
Nonlinear noisy amplifier
IIP3
Noise factor: F
Input source noise power: Ni
GNi
FxGNi
(output noise floor)
1
3
Pout (dBm)
SFDR
G
“SFDR” is the difference between the system input noise floor and the largest signal that can be accommodated before the 3rd-order IM product rises above the noise floor.
In this expression, we generally assume that SNRmin=1 (0 dB).

## Slide 37: Spurious Free Dynamic Range (SFDR)
Pin,min
=kTDf x F
Pin (dBm)
OIP3
Nonlinear noisy amplifier
IIP3
Noise factor: F
Input source noise power: Ni
GNi
FxGNi
(output noise floor)
1
3
Pout (dBm)
SFDR
G
“SFDR” is the difference between the system input noise floor +SNRmin and the largest signal that can be accommodated before the 3rd-order IM product rises above the noise floor.
This is more general definition of SFDR.
SNRmin
SNRmin