## Slide 1
ECE 5220 RFIC Technology & Design (Impedance Matching)

## Slide 2: Introduction to Impedance Matching
These are critical blocks for impedance matching.
In typical wireless radios (< 6 GHz), these will be integrated on a single chip, and impedance matching between each block may not be necessary.

## Slide 3: Introduction to Impedance Matching
Q) Where do we need impedance matching?
Ex: Wireless radio: Any interface with antenna needs to be matched with 50W. Any RFIC driving external RF component (e.g. SAW filter, image rejection filter) needs to be matched with 50W. Usually PA is external component and needs 50W interface.
If integrated on a chip, usually we don’t need 50W match between interfaces.
Q) Why 50W
(not 500W for instance)?
Usually we call this as 50W system.

## Slide 4: Introduction to Impedance Matching
Q) Where do we need impedance matching?
Ex) Video receiver (TV) system: Any interface with antenna (for terrestrial TV) and coaxial cable (for cable TV) needs to be matched with 75W .
Q) Again, why 75W?
Usually we call this as 75W system.
Video transmitter
Video receiver

## Slide 5: RF Energy Flow from Antenna to Radio
Air :
Radio electronics :
RF energy exists in the for m of E- & H-field energy in the air, and it propagates by alternating its form between E- & H-field. The ratio of strength of E- & H-field is characteristic impedance, Zair (also called as “wave impedance”)
RF energy exists in the form of V & I.
And characteristic impedance will be expressed by the ratio of V/I.
Example numbers,
If electrical field strength (E) is measured at a receiving antenna is 1 mVrms/m. Then, magnetic field strength (H) = 1 (mVrms/m) / 377 W = 2.65 nArms/m. Power density (P/m2) = E x H = 1x 10-6 x 2.65 x 10-9 = 2.65 x10-15 W/m2. If receiving antenna effective area is 5 m2, the overall incident power into antenna is P = 2.65 x10-15 W/m2 x 5 m2 = 13.25 fW = -108.77 dBm
mo= permeability of air= 4p x 10-7 H/m
eo= permittivity (dielectric constant) of air= 8.854x 10-12 F/m
mr= relative permeability, air: mr = 1
er= relative permittivity , air: er = 1

## Slide 6: RF Energy Flow from Antenna to Radio
Air :
Radio electronics :
RF energy exists in the for m of E- & H-field energy in the air, and it propagates by alternating its form between E- & H-field. The ratio of strength of E- & H-field is characteristic impedance, Zair (also called as “wave impedance”)
RF energy exists in the form of V & I.
And characteristic impedance will be expressed by the ratio of V/I.

## Slide 7: RF Energy Flow from Antenna to Radio
Air
So, antenna can be regarded as a “sensor” or “transducer” which transforms the RF energy from wave energy (in E- & H-fields) to electrical energy (in V and I forms).
Radio electronics

## Slide 8: RF Energy Flow from Antenna to Radio
Air
Now we have two different impedance systems, and we can approximately model them as this:
Electronics
Mental model
of far-field air medium
under wave propagation.
Radio electronics
Vs,far is an equivalent source that generate E-field in far-field air medium.

## Slide 9: RF Energy Flow from Antenna to Radio
Air
Now we have two different impedance systems, and we can approximately model them as this:
Vs,far is an equivalent source that generate E-field in far-field air medium.
Mental model
of far-field air medium
under wave propagation.
Electronics
Energy flow
Antenna is the device to maximize this energy flow.
Radio electronics

## Slide 10: Maximum Energy (Power) Transfer
Mental model
of far-field air medium
under wave propagation.
Electronics
Energy flow
Zin
Zout
Q) To maximize the energy flow from air medium to electronics, what should be Zin and Zout?
Q) To maximize the power flow from air medium to electronics, what should be Zin and Zout?
Vs,far is an equivalent source that generate E-field in far-field air medium.

## Slide 11: Maximum Power Transfer Theory
To answer the question, let’s review “Maximum Power Transfer Theory”
For arbitrary load resistance, RL,
Power delivered to the load RL
PL will be maximum at RL=Rs,
Note, VL is jus ½VS at RL=Rs; i.e. voltage efficiency is only 50%. This just what we can do best when maximizing power delivery.

## Slide 12: Maximum Power Transfer Theory
For arbitrary source impedance of Zs and load impedance of ZL,
Conclusion: For maximum power transfer to the load, we need to match the load impedance ZL to the conjugate of source impedance Zs. This is called “conjugate matching”, and when we say “impedance matching” usually it means for the conjugate matching for maximum power transfer .
Caution: there is also “impedance matching for minimum noise figure”, called “noise matching”. We will discuss it later in noise lecture.
when ZL=Zs* (you can verify this easily).

## Slide 13: Maximum Energy (Power) Transfer
Mental model
of far-field air medium
under wave propagation.
Electronics
Power flow
Zin
Zout
Now let’s come back to this issue:
Q) To maximize the power flow from air medium to electronics, what should be Zout?
This discussion provides another point of view of the antenna; i.e., it is impedance transformer from air characteristic impedance to electronic characteristic impedance.
Ans) Zin should be Zin = Zair = 377W, and Zout should be Zout = Zo = 50W.
Vs,far is an equivalent source that generate E-field in far-field air medium.
*In a strict sense, it’s not quite true, and it’s hard to define exact impedance at near-field region of antenna.

## Slide 14: Objective 0f Impedance Matching
Until now, we have considered maximum power transfer in the antenna
Now, let’s examine how we can make maximum power transfer inside RFIC.
To do this, let’s think about this LNA design.

## Slide 15: Objective 0f Impedance Matching
Typical LNA design is based on common-source amp.
Let’s change NMOS with simple 1st –order model.
Vin
Vout
Vout
Vin
Objective) To maximize the signal power delivered to load, RL, from input Vin.

## Slide 16: Maximize Power Delivered to Load
Vout
Vin
First, let’s calculate power delivered to the load, RL.
Apparently, to maximize POut,
voltage across Cgs needs to be maximized.
(since, gm is constant for a given bias condition of the NMOS)
Q) How can we maximize voltage across Cgs ?

## Slide 17: Power Transfer Through Direct Connection
How about direct connection ?
eox=3.97x8.85x10-14 F/cm
tox=50 nm
W=100 um
L=0.18 um
Rg=5 W
Virtually all of Vs appears across Cgs. Not bad !!
Q) Can we do better ?

## Slide 18: Improved Power Transfer Technique
Voltage across Cgs will be maximized by maximizing current through Cgs (iin).
Maximum current through Cgs leads to maximum power delivered to input port.
Conclusion: We might be able to build more voltage across Cgs by maximizing the power delivered to the input port.
Think like this !
Q) How can we do this ?

## Slide 19: Improved Power Transfer Technique
Eventually, we will find that by inserting some lossless network, we can maximize power delivered to the input port, and thereby, Vgs can be even larger than Vs.
Let’s examine this !
Voltage across will be maximized by maximizing current through Cgs (iin).
Maximum current through Cgs leads to maximum power delivered to input port.
Conclusion: We might be able to build more voltage across Cgs by maximizing the power delivered to the input port.
Think like this !
Q) How can we do this ?

## Slide 20: Impedance Matching
Recall “Maximum Power Transfer Theory”
If we design the lossless network such that impedance looking back from NMOS to source is Zin*, we will get maximum power transfer from the source
to the input port
We call this as “impedance matching” and the lossless network as “impedance matching network”.
Let’s examine how to design the matching network !

## Slide 21: Impedance Matching
Let’s consider how to perform impedance matching for a general load and source impedance
If we design a lossless network such that Zout=ZL*, then Zin=Zs*.
The converse in also true, i.e., if we design the lossless network such that Zin=Zs*, then Zout=ZL*.
Can you come up with a simple intuitive explanation (without using equation) as to why the above statements are true ?

## Slide 22: Impedance Matching: The First Step
Zin=Rs
Zout=RL
First, let’s cancel the imaginary parts of Zs and ZL. This can be done by an appropriate choice of capacitor or inductor sizes.
The problem is now reduced to how to design the core lossless network to match load resistance RL to source resistance Rs.
We have two cases; 1) Rs > RL & 2) Rs < RL.
Let’s think about the case-1) first.

## Slide 23: Impedance Up-Conversion
Case-1) Rs > RL
We need to convert the smaller load impedance to a larger value of Rs (this is referred as upward impedance conversion).
Think !!!
If we generate smaller voltage across RL using the source voltage Vs, this would results in smaller current being drawn through RL. This makes RL look like a larger R.
How can we do this ? Note we are only allowed to use lossless elements, i.e., inductors and capacitors.

## Slide 24: Impedance Up-Conversion
iR1 > iR2
Let’s put an inductor in series with the resistor. This would increase input impedance which would result in smaller current being drawn by the resistor.
Case-1) Rs > RL
Now the impedance is no longer purely real value, and we need to turn the impedance into a purely real value. How about adding C in series with the L ?
NO !!!
The C will be resonated with L in series,
and undo what the L was intended to do;
i.e., reduce current through the RL.
iR1=iR2, same as the original.

## Slide 25: Impedance Up-Conversion
iR1 > iR2
Let’s put an inductor in series with the resistor. This would increase input impedance which would result in smaller current being drawn by the resistor.
Case-1) Rs > RL
Now the impedance is no longer purely real value, and we need to turn the impedance into a purely real value. How about adding C in parallel with the L & RL?
YES !!!
The C will be resonated with L in parallel, which gives pure resistance. iR2 is still smaller than original, and therefore, effective RL will be increased. Let’s verify this !

## Slide 26: Impedance Up-Conversion
ZLR
Yin
Let’s calculate input admittance !

## Slide 27: Impedance Up-Conversion
ZLR
Yin
From the final form of the admittance,
Roughly, RL is increased by a factor of square of the impedance ratio of L & RL
(impedance is up-converted) .
Imaginary part will be cancelled at this condition. Note is the characteristic impedance of L & C.

## Slide 28: Impedance Up-Conversion (ex)
Let’s take an example.
In previous example, Rg=5 W, Cgs=84 fF, freq=2 GHz.

## Slide 29: Impedance Up-Conversion (ex)
Let’s take an example.
In previous example, Rg=5 W, Cgs=84 fF, freq=2 GHz.
First, let’s apply Lg to nullify reactance of Cgs at 2GHz through series resonance.
Lg=75.39 nH
, @ =2π2GHz

## Slide 30: Impedance Up-Conversion (ex)
Let’s take an example.
In previous example, Rg=5 W, Cgs=84 fF, freq=2 GHz.
Next, apply L & C to convert Rg (5W) to Rs ( 50W).
L=1.19 nH
C=4.78 pF

## Slide 31: Impedance Up-Conversion (ex)
Now, let’s calculate voltage across Cgs, Vgs.
In previous example, Rg=5 W, Cgs=84 fF, freq=2 GHz.
Now after matching,
Rout = Rg
Change to Thevenin Equivalence

## Slide 32: Impedance Up-Conversion (ex)
Now, let’s calculate voltage across Cgs, Vgs.
30.0xVs using impedance matching !!
In previous example,
C=9.56 pF, Rs=50 W, Rg=5 W, Cgs=84 fF, freq=2 GHz.
30.0VS

## Slide 33: Impedance Matching for Analog Design
Q) Why is impedance matching not used in analog circuits?
L=2.39 uH
C=9.56 nF
In this example, just change freq=2 MHz (from 2 GHz)
Rs=50 W, Rg=5 W, Cgs=84 fF.
These values are almost impossible to realize in IC.
Also, note that large values of L imply large values of parasitic resistors to the inductor. This large parasitic resistor will take up most of power delivered by the source; hence, only a small fraction of the power will be delivered to the transistor input port (impractical for most cases of analog IC designs).

## Slide 34: Impedance Down-Conversion
Impedance down-conversion is just reciprocal of the up-conversion.
Q) Can you explain intuitively how the impedance down-conversion work ?
Rs > RL
Impedance up-conversion
Impedance down-conversion
We call this type of L-C matching circuit as L-matching circuit.

## Slide 35: Impedance Down-Conversion
Let’s think about this !
When we apply very small test signal across the L & C series circuit, a large voltage will be developed across C due to a series resonance.
VC
+
-
VC
+
-
When we place resistor, Rs, across C, the capacitor will provide a large current to the resistor. This current can be much larger than that driven directly by Vtest.
This makes the Rs looks smaller effectively, when looking at the source side.
compare iRS
This is the behind logic of the downward impedance conversion.

## Slide 36: Impedance Down-Conversion
YRC
Zin
Let’s drive input impedance Zin.

## Slide 37: Impedance Down-Conversion
YRC
Zin
From the final form of Zin,
Roughly, RS is decreased by a factor of square of the admittance ratio of C & RS
(impedance is down-converted) .
Imaginary part will be cancelled at this condition. Note is the characteristic impedance of L & C.

## Slide 38: Impedance Conversion Summary
Rs > RL
Impedance up-conversion
Impedance down-conversion
Note for similarity !
Change form to admittance
QRL: Quality factor of series of L-RL
QRC: Quality factor of parallel of C-RS
Impedance (admittance) up & down conversion is always related with a factor of (1+Q2).
Q) What is Q ?
To answer this, we need to consider frequency response of the matching network , first.

## Slide 39: Frequency Response of Matching Network
Let’s drive in-out transfer function, VL/VS.

## Slide 40: Bandwidth of Matching Network
Freq (w)
Voltage across RL
w=wo
Dw
Observation: Circuit delivers power to the load at other frequencies around w=wo which is resonance frequency of the circuit. This means there is a power loss around at w=wo+Dw.
Typical simulation result (conceptual)
-3dB frequency can be calculated by equating this,

## Slide 41: Bandwidth of Matching Network
Freq (w)
Voltage across RL
w=wo
Observation: For a fixed impedance transform ratio (Rs/RL), the bandwidth (BW) is fixed.
In many RF systems, narrowband operation is preferable, since we don’t want to lose any input power around signal bandwidth. Also, narrower band means more filtering of unwanted signals.
Q) Can we design matching network to have more narrower band operation (red-curve) for a given fixed impedance transform ratio?

## Slide 42: Quality Factor (Q)
To answer the question, we need to introduce a very important concept in RF systems, referred to as “Quality Factor (Q)”.
In its simplest form, Q is used to measure the “quality” of capacitors and inductors
An inductor/capacitor with large resistor has poor Q
An inductor/capacitor with zero series resistance has infinite Q
Let us now define the quality factor for a general network :
Recall, Energy (J) = Average power (W) x Cycle period (T)

## Slide 43: Q of Lossy Inductor
Let’s consider simple example of a lossy inductor.

## Slide 44: Q of Lossy Capacitor
Let’s consider simple example of a lossy capacitor.

## Slide 45: Q of Series LCR Network
Let’s consider another simple example of a series L-C-R network.
This is not correct ! What was wrong ? Don’t apply the formula in a blind manner !

## Slide 46: Q of Series LCR Network
Note: in inductor and capacitor, voltage and current have 90o (quadrature, or orthogonal) phase relationship.
90o phase difference

## Slide 47: Q of Parallel LCR Network
Another example of parallel LCR network.
Following the same manner with applying AC-voltage, Vpk, you can verify that the Q of the parallel of LCR network at resonance frequency will be given as,
Note, is the characteristic impedance of L-C network.

## Slide 48: Series L-R to Parallel L-R
It is quite useful to change series network to parallel or vice versa, which allow great simplification of circuit analysis.
If Zin, series = Zin,parallel, then two circuits are identical.
Zin, series
Zin, parallel
Resistance is increased in parallel from by a factor of Qs2 (if Qs >>1)
Inductance will be about the same in parallel form, if Qs >>1

## Slide 49: Parallel L-R to Series L-R
It is quite useful to change series network to parallel or vice versa, which allow great simplification of circuit analysis.
If Zin, series = Zin,parallel, then two circuits are identical.
Zin, series
Zin, parallel
Resistance is decreased in series from by a factor of Qp2 (if Qp >>1)
Inductance will be about the same in series form,
if Qp >>1
You can also verify that,
Qs=Qp

## Slide 50: Series C-R to/from Parallel C-R
You are encouraged to verify this.
Point is that if network Q is large enough (Qs=Qp >>1), there will be little change in the capacitance, but big change in resistance between series & parallel forms (key to impedance up/down conversion).

## Slide 51: Q of Matching Network (Z up-conversion)
These L-C will be resonated at the target frequency. As a result there will be pure matched resistances, Rs and Rp.
Let’s revisit this matching circuit
(Rs > RL).

## Slide 52: “Loaded Q” vs. “Unloaded Q”
Let’s use this matching circuit to illustrate between “loaded Q” and “unloaded Q”.
Unloaded Q: the driving source impedance is not included in the measurement of Q.
Loaded Q: the driving source impedance is included in the measurement of Q.

## Slide 53: Various Forms of Q (unloaded)
When we call Q (or network Q), it usually means unloaded Q.
Expressed in series R-L
Expressed in parallel R-L
Expressed in terms of impedance transform ratio
Rs > RL

## Slide 54: Impedance Matching With Higher Q
Freq (w)
Voltage across RL
w=wo
Revisiting bandwidth consideration
(Rs > RL) :
BW
The higher the Q of the network, the narrower the BW of the matching network.
For a given impedance ratio, the BW is fixed.
Q) How can we design a network with higher Q for a given Rs and RL ?

## Slide 55: An Idea for Impedance Matching With Higher Q
The network Q depends on the impedance ratio.
For single L-C matching circuit, the impedances of Rs and RL are fixed, and so is Q.
What if we down-convert the RL to a smaller value of RI (intermediate impedance), and then up-convert to the desired Rs in second stage (2-step conversion) ?
Let’s propose this !
Rs=50 W
RL=10 W
RI=2 W
Direct conversion
Indirect (2-step) conversion
This is higher Q path than direct conversion
Let’s examine this idea to see if this would allow us to design a network with higher Q for a give impedance transform from RL to Rs.

## Slide 56: Implementation of Higher Q Impedance Matching (p-Matching)
RI
RI’
Let’s cascade two L-matching networks such that first L-matching (L1-C1) down-converts the load impedance to RI, and the second L-matching (L2-C2) up-converts the impedance to the desired value.
Apparently, RI’=RI (why ?)
Let’s continue the analysis.
RL
Rs

## Slide 57: Q of P-Matching Network (Up-Conversion)
RI
RI
RI
RI

## Slide 58: Q of T-matching Network (Down-Conversion)
Rs=50 W
RL=500 W
RI=5000 W
Direct conversion
Indirect (2-step) conversion
This is higher Q path than direct conversion
Similarly, we can think 2-step high Q matching network to down-convert from high load resistance to smaller source resistance; First, up-convert to higher impedance, and then down-convert to the desired impedance.

## Slide 59: Q of T-matching Network (Down-Conversion)
RI
RI
L1-C1 up-converts RL to RI, after that, C2-L2 down-converts RI to Rs. (Students are encouraged to verify this.)

## Slide 60: Other Matching NWs: Tapped Cap. Resonator
Rs > RL
Down conversion
Up conversion
So far we have seen that P- and T-matching networks provide more flexibility in choosing Q of the network. This is yet another example for higher Q matching network, and called as “capacitor tapped resonator transformer”.

## Slide 61: Other Matching NWs: Tapped Cap. Resonator
Rs > RL
Down conversion
Up conversion
Note, without C2, it is a simple L-C matching circuit. But with C2, the C2 will reduce RL effectively by a factor of (1+Q2), where Q is unloaded-Q formed by C2-RL parallel network.
Without C2
With C2

## Slide 62: Other Matching NWs: Tapped Cap. Resonator
Rs > RL
Without C2
With C2
This is similar concept of 2-step conversion in P- or T-matching network; i.e., RL  RI (= Req)  Rs.
RI
RI*

## Slide 63: Other Matching NWs: Tapped Cap. Resonator
Rs > RL
Down conversion
Up conversion
Without C2
With C2
Also, it can be easily verified that the impedance transform ratio will be given by the capacitance ratio, approximately; i.e.,
This tapped capacitor resonator is used popularly in “Colpitts VCO” designs, which we will discuss later.

## Slide 64: Other Matching NWs: Tapped Ind. Resonator
Rs > RL
Down conversion
Up conversion
Using the same logic and mathematical flow, you can verify that this transformer network, called as “tapped inductor resonator”, also provides higher Q-matching.
This topology is not popular compared with previous topology, since it needs two inductors which will take more space than previous one in IC designs (But students are encouraged to develop math for this).

## Slide 65: Other Matching NWs: Transformer
Transformer is also widely used for impedance matching at board level as an external component, mainly at low-frequencies.
Transformer basics:
Voltage will be amplified by a factor of turn ratio (N) at the output; i.e., Vout=N x Vin.
ideal transformer is pure passive and no loss, therefore there will not be any power loss; i.e., Pin = Vin x iin = Vout x iout =Pout & iout=iin/N (why ?).

## Slide 66: Other Matching NWs: Transformer
Let’s find input and output impedance relationships.
Rin
Rout
Maximum input power will be delivered to the load via transformer when input impedance is matched, i.e, Rs=Rin (recall “maximum power transfer theory”);
Once RL and Rs is given, you can determine N for maximum power delivered to load.

## Slide 67: Other Matching NWs: Transformer
Let’s find input and output impedance relationships.
Rin
Rout
Q) How much is voltage gain in this system?

## Slide 68: Similarity btw Transformer and LC matching
Rs < RL
Transformer matching
L-C matching
Note: N in the transformer and Q in the LC matching network play similar role.
Rs < RL

## Slide 69: Transformer Matching Example: Audio App.
One popular use of transformer matching is in the loudspeaker driving systems.
Typically 4-8 W
Output impedance is very low, < 0.1 W, for maximum efficiency.
For maximum power transfer,
In RFIC (< 5GHz), impedance conversion using transformer is not popular, because of unavailability of good quality on-chip transformer.

## Slide 70: 50 W Question ?
Very often in RF IC designs, it is required that the input & output ports are matched with 50 W. One might ask
Why 50 W?
Why not 500 W?
Once we understand the reason for 50 W, we can judiciously choose when to follow the 50 W match, and when to choose another level of impedance match condition (500 W for example).
50 W –cable (why ?)

## Slide 71: Maximum Power Delivered Using Coax Cable
Let’s examine a coaxial cable with a characteristic impedance of Zo:
Dielectric (Air, Teflon, Polyethylene …)
Maximum power (P) delivered to the load using such a coaxial cable can be expressed as:
Maximum power will be delivered to the load when
V is maximized, and
Zo is minimized.
Let’s calculate the characteristic impedance of the coaxial cable.

## Slide 72: Characteristic Impedance of Coaxial T-Line
The coaxial transmission line can be represented as shown in figure below:
L & C represent line inductance and capacitance with infinitesimal length (this is common technique to extract characteristic impedance of a T-line).

## Slide 73: Characteristic Impedance of Coaxial T-Line
The capacitance and inductance of a coaxial cable are given as
(refer to any microwave textbook):
To maximize power delivered to load, V needs to be maximized in the coaxial transmission line. But there is a limit of V because of breakdown of the dielectric beyond some point of V across the inner and outer diameter.
Ro
Ri
Ro: outer diameter
Ri: inner diameter

## Slide 74: Maximum Electric Field in a Coaxial Cable
When we increase V, electric field will be increased between inner and outer conductors. And the maximum E-field depends on the radius of the inner and outer conductors as well as the voltage across the conductors.
Ro
Ri
What happens when we decrease the diameter of the inner conductor?
Ans) The electric field increases significantly as the radius of the inner conductor, Ri, is made smaller and smaller.
Ans) This increase in E-field strength eventually causes a breakdown of the dielectric between the two conductors (at a fixed voltage).

## Slide 75: Zo for Max. Power Handling
Now we have everything to re-evaluate the maximum power deliverable to the load.
The condition for maximum of power delivered can be obtained by differentiating the P with respect to Ri and setting it to zero:
This result gives the optimum characteristic impedance for the maximum power handling capability as:
=60 W

## Slide 76: Minimum Attenuation using Coaxial Cable
Let’s re-examine the coax cable from the standpoint of signal attenuation. The metal conductors used for the coax cable have finite resistance which causes signal attenuation, even for the case of perfect matching.
Ro
Ri
The resistance of the cable keeps increasing as Ri and Ro decreased (note that at RF, current flows through only the skin of the conductors). As the resistance of the cable keeps increasing, the signal gets more attenuated.

## Slide 77: Zo for Min. Attenuation
The attenuation constant is given by:
To find the optimum condition for the minimum attenuation, we differentiate the expression for attenuation with respect to Ri:
This result gives the optimum characteristic impedance for the minimum signal attenuation as:
= 0

## Slide 78: Conclusion from Analysis of “50W Question”
Some conclusions (and conventions in RF systems) can now be drawn:
For TV reception, signal attenuation is an issue because the signals are weak , therefore, TV equipment uses 75-W system to minimize attenuation.
For systems involved in pure transmission, a 30-W systems allows maximum signal handling capability.
For systems involved in both transmission and reception of signals, both signal attenuation (for received signal) and signal power handling capability (for transmission signals) are important. And therefore, 50-W system (approximate average of 30-W and 77-W) is chosen.

## Slide 79: Conclusion from Analysis of “50W Question”
Typical wireless RF systems (including measure instruments) use 50-W systems. And 50-W interface needs to be followed with external environment.
However, if signals are not going out of the chip, 50-W specification need not be followed. Note, in IC environment typical interface impedance is 0.1~1 kW range. So, if you try to match every interface with 50-W inside chip, you might end up with wasting a lot of signal power.
One of main philosophies in IC design paradigm of SoC is to minimize 50-W interface and hence to save power. In old days of radios based on discrete elements on board level, each function blocks need substantial power consumption to drive 50-W interface to other external blocks

## Slide 80: Filter Characteristics Vs. Impedance Matching
Zo=50 W
50 W
Loss (dB)
Freq (Hz)
Rx BW
Tx BW
Typical duplexer characteristic
Typical insertion loss of duplexer will be 1~2 dB range and its performance can be significantly affected by the degree of the impedance matching between LNA.
If not matched well to 50-W, duplexer characteristic can be poor. Loss can be higher than 3-5 dB, which will do detrimental effect on the entire system NF.