## Slide 1: Millimeter wave Mixer

## Slide 2: IQ Mixer
LNA output
Signal 120GHz,
conversion gain=5dB,DSB NF=18.5dB,P1 dB=-10dBm(
Including unity gain buffer to match 50ohm)
Min power consumption is 56mW(not mentioned)
A Fundamental Frequency 120-GHz SiGe BiCMOS
Distance Sensor With Integrated Antenna

## Slide 3
245-GHz LNA, Mixer, and Subharmonic
Receiver in SiGe Technology
Signal 245GHz,LO=60GHz
conversion gain=5dB,DSB NF=18.5dB,P1 dB=-10dBm(
Including unity gain buffer to match 50ohm)
Min power consumption is 56mW(not mentioned)

## Slide 4
SiGe:C tech
Signal 122GHz,LO=60GHz,
conversion gain with IF amplifier=8dB,
SSB NF=21dB,LO power=9dBm,IF=1GHZ

## Slide 5
SiGe:C tech
Signal 122GHz,LO=60GHz,supply=6.6V
conversion gain with IF amplifier=23dB,
SSB NF=21dB,LO power=3dBm,IF=1GHZ

## Slide 6
.25um SiGe:C tech
Signal 94GHz,LO=46GHz,supply=3.3V
conversion gain=8db
SSB NF=15dB,LO power=8dBm,IF=2GHZ
P1=-8dBm

## Slide 7
.13um SiGe tech
Signal 77GHz,LO=73GHz,supply=2.5V
conversion gain with IF amplifier=8-11db
DSB NF=12.5-14.5dB,LO power=-2dBm,
IF=1GHZ
OP1=5dBm
A Low-Voltage 77-GHz Automotive Radar Chipset