## Slide 1: LNA and Mixer Design in Millimeter wave
Presented By
Sadia Afroz

## Slide 2: Outline
Challenges in mm-wave design and passive components
LNA design
  General LNA topology
  Design example of W-band LNA
Challenges of mm-wave Mixer design
  Homodyne and Heterodyne Mixer
  Subharmonic Mixer
  Mm-wave Passive Mixer
Layout Methodology

## Slide 3: Challenges in mm-wave Design
Wavelength is few millimeters. λ= so when signal traverse components with appreciable size of wavelength, their true nature is like wave .so distributed effect must be considered as a part of design process.
Transmission lines provide better model accuracy than inductors due to well define ground planes.
Ground shielded Coplanar waveguide (G-CPW) is widely used for matching of interconnection.
Use of T-lines results noticeable increase in chip-area, alternatively SW-CPW are used.
CPW (IBM SIGe BiCMOS process)
SW-CPW
Notes: For same phase delay,SW-CPW has lower loss than microstrip line.Metal strips are placed beneath the top conductor to increase the capacitance. This results in decrease in wave speed thus more phase shift with smaller size.

## Slide 4: Passive components
Folded Microstrip lines can also be used for inductor.
Transformer based balun is widely used to make single ended to differential. Usually Baluns are routed with top two thick metal layers.
Metal-insulator-metal (MIM) capacitor terminations must be considered as T-lines and modeled consequently.
Folded Microstrip line (90nm CMOS Tech.)
Octagonal Transformer (center tapped)
Square Transformer (SONNET Layout)
3pF MIM Capacitor and its equivalent model
(0.13um SiGe BiCMOS process)

## Slide 5: LNA Design in mm-wave
Simultaneous conjugate matching and noise matching at LNA input.
Multistage LNA: Inter-stage matching and stability.
Transistors operate close to their Lower gain
higher NF
Device requirement : High -current gain, cutoff frequency and breakdown voltage.

## Slide 6: LNA topology
Common gate topology:
Reference: Bezad Razavi,Fellow,IEEE ,“Design of millimeter-wave CMOS Radios:A tutorial” ,IEEE transactions on circuits and systems,regular papers,VOL 56,
No.1 Jan 2009
Two Serious Issues:
Matching and Gain degrades because of a parasitic inductance between and its connections to gate and to ground.
Gain of CG stage is much lower at mm-wave frequency.
Notes: While considered to provide robust input and gain in mm-wave design,CG LNA faces two problem at very high frequency and deep submicron technology.first the gate of the input transistor must see a very low impedance return path to ground so as to avoid degrading the input match and gain. but due to the parasitic inductance of Cg and to the gate and ground connection leads to a high impedance,degrades matching and gain.Morever,for the impedance of Cg to remain low,capacitance should be very high,unfortunately,L1 and L2 inevitabley lead to long interconnections from Cg to the gate and/or ground.
CG LNA faces two serious issue in mm-wave :
  and its connections to gate and to ground exhibit a parasitic inductance which appears in series with gate at very high frequency. So matching and gain degrades.
  Gain of CG stage is much lower at mm-wave frequency.
While considered to provide robust input and gain in mm-wave design,CG LNA faces two problem at very high frequency and deep submicron technology.first the gate of the input transistor must see a very low impedance return path to ground so as to avoid degrading the input match and gain. but due to the parasitic inductance of Cg and to the gate and ground connection leads to a high impedance,degrades matching and gain.Morever,for the impedance of Cg to remain low,capacitance should be very high,unfortunately,L1 and L2 inevitabley lead to long interconnections from Cg to the gate and/or ground.
CG LNA faces two serious issue in mm-wave :
  𝐶_𝐺 and its connections to gate and to ground exhibit a parasitic inductance which appears in series with gate at very high frequency. So matching and gain degrades.
  Gain of CG stage is much lower at mm-wave frequency.

## Slide 7: LNA topology (cont.)
Inductively degenerated cascode topology:
Input matching depends on package parasitic.
GND return path for and should display very low inductance. So careful layout consideration is needed.
A pole (in the order of ) adversely impact the gain and noise figure.
All inductors must be integrated on chip.

## Slide 8: LNA topology (cont.)
.
.
Cascading three stage
Reference: Bezad Razavi,Fellow,IEEE ,“Design of millimeter-wave CMOS Radios:A tutorial” ,IEEE transactions on circuits and systems,regular papers,VOL 56,
No.1 Jan 2009
can be used as Series resonance, acts as inter-stage matching.
Wide Band impedance &
noise matching
Transformer feedback LNA
Notes: It is W band Cascode LNA ,is designed in 65nm Technology, provides a NF 7dB and gan 17dB,drawing current 24mA,transformer feed back allows optimiztion for input matching and noise figure.

## Slide 9: W-band LNA
Next stage
Reference: Zhiming cheng,chun-cheng wang,Hsin-cheng yao,Payam heydari,”A BiCMOS W-band 2 focal-plane Array with On-chip Antenna”,
IEEE journal of Solid State Circuits,Vot.47,No.10,Octobar 2012.
Four stage LNA, Gain=25 dB, NF=8.3 dB, 0.18um SiGe BiCMOS technology.
Capacitance of GSG pad should be absorbed by input matching network.
is put as close as possible to the base of to minimize parasitic inductance and ensure stability.
Local decoupling network for power supply is
To reduce footprint ,lumped inductors are used instead of T-lines, as well as inter-stage matching.

## Slide 10: Common base topology for BJT
Reference: Yanfei Mao,K. schmalz,J. Borngraber,J.C scheytt,“A 245GHz CB LNA in SiGe” ,Proceedings of 6th European Microwave Integrated circuits Conference
245 GHz LNA, Gain=12 dB, NF= 9.4 dB, BW=26 GHz, Power consumption=28mW
Common base can achieve higher gain, wider bandwidth and higher isolation than CE stage.
Parasitic inductance at base introduces negative resistance at emitter by equation (1).
Stability is ensured by reducing collector current which reduces .
Parasitic inductance can increase gain and lower NF.
improve isolation between CB stages.
Notes: Parasitic inductance is used here to boost, optimizing the current for stability.

## Slide 11: Challenges in Mixer Design in mm-wave
Homodyne Mixer : High performance silicon base oscillator is very challenging in mm-wave frequency. so for direct conversion, LO is generated at a fraction of RF frequency and then use a multiplier prior to the frequency translation.
Heterodyne Mixer: Double conversion mixer is used to relax oscillator and frequency divider requirement in mm-wave application.
IQ Mixer: Generation of I Q phases of LO at mm-wave frequency and its balanced distribution is problematic. Quadrature operation typically degrades phase noise in mm-wave frequency.
LO distribution is difficult because of significant loss and mismatch in interconnects at high frequency.
AT mm-wave frequencies, it is difficult to get large LO signal, so conversion gain is low with weak LO signal.
Parasitic and layout consideration is an important issue for port to port isolation and stability.
Homodyne mixer
N frequency
multiplier
IF amplifier
Mixer

## Slide 12: Conversion Gain or Loss
Conversion gain or loss is the ratio of the desired IF output (voltage or power) to the RF input signal value ( voltage or power).
Improve Gain
LO
CG
Transmission line is used to reduce the parasitic at the common node of switches.
Optimize Transconductor bias current for high gain.
To increase Gain:

## Slide 13: Homodyne Mixer in Millimeter wave
O.C for 2
O.C for
S.C @ 2
Reference: Saverio trotta ,bernhard Dehlink ,herbert Knapp ,Klaus Aufinger, Thomas F. Meister ,Josef Bock, Werne Simburger and Arpad L. Scholtz ,“Design considerations for low noise, Highly Linear Millimeter-wave Mixer in SiGe Bipolar Technology”
@ RF
@ 2RF
@ RF
RF=76GHZ, CG=15dB, SSB NF=11.2dB, IIP3=8.5dBm, Supply=5.5V, SiGe:C technology.
Nonlinearity of B-E junction creates harmonics. High , L3-C1 represents very low impedance path for components generated by T1.
The feedthrough 2can increase IM3,both , 2 is highly attenuated by Low pass filter consisting of Ccs-L1,as RF and LO frequency are quite close.
The effect of parasitic capacitance at node A is lowered by L1 which also improves NF.
L2 and R1 improves stability.
Notes: Very large transistors are used for transconductance.Second harmonics generated at node C is attenuated by Cbc-L3-C1 and Low pass filter L1-Ccs

## Slide 14: Folded structure
@ RF
,
Gain ,NF
RC lowpass improves LO-IF isolation
Reference: S.trotta,B.Dehlink,R. Reuter,Y.Yin,J.John,J.Kirchgessner,D.Morgan,P.welch,J.J.Lin,B.Knappenberger,I.To and M.Huang,”A multi-channel Rx for 76.5GHz
Automotive Radar Applications with 55dB IF Channel-to-Channel Isolation”, 4th European Micorwave Integrated Circuits Conference,2009.
RF=76.5GHz, LO=38.25GHz, CG with IF amplifier=18dB, Supply 3.3V, 200 GHz SiGe BiCMOS technology.
Transistors are biased to get highest stable gain.
Current in the input RF-pair can be optimized to improve NF and linearity.
LO switch quad are biased in low current to reduce noise injected by these transistors.
Voltage headroom available at the IF output help to avoid the clipping of mixer core.

## Slide 15: Heterodyne Mixer
LO @ 52GHz
@ 26 GHz
@ 26 GHz
Second quadrature LO is generated by dividing first LO by 2. Single frequency synthesizer can be used as first and second LO generation.
Shielded T-lines are used for matching circuits because required reactance is small, also These lines has high isolation, reduced coupling to adjacent circuits.
Second Mixer achieves 6dB conversion gain and BW=8GHz in base band.
Reference: Aydin babakhani,Xiang Guan,Abbas komijani,Arun Natarajan,Ali hajimiri,”A &&GHz phased array transceiver with on chip antennas in
Silicon:receiver and Antennas”,IEEE journal of Solid State Circuit,vol.41,no.12,December 2006
Two step down conversion scheme with RF =76-81 GHz,
IF= 25-27 GHz. CG=5dB,BW=10GHz,NF=11dB

## Slide 16: Subharmonic Mixer
Subharmonic mixer offers an alternative solution to fundamental mixers in mm-wave range since they allow for an LO at lower frequency.so this technique avoids separate multiplier and associated circuitry, resulting in lower power consumption and low active area.
Second harmonic or fourth harmonic of LO frequency are commonly used to downconvert RF signal to IF frequency.
To increase the gain of subharmonic mixer, the desired harmonic mixing product should be maximized. Harmonic component of LO signal is a function of conduction duty cycle.

## Slide 17: Subharmonic Mixer :Topology 1
Second Harmonic of LO is used. Completely Doubled Balanced Gilbert cell.
This topology uses just two level of transistors hence lower supply voltage.
Differential Two stage ring oscillator is used to generate quadrature phase.
The some of the collector current of all switching pair has component indicating frequency doubling.
Ring oscillator
Reference: R.M. kodkani and L.E. larson,“An integrated 50GHz SiGe Subharmonic Mixer/downconverter with a quadrature ring VCO” ,IEEE 2007
RF= 50GHz,LO=24 GHz,peak CG=9dB,NF=11.8 dB from 3.3V supply, 0.12um SiGe BiCMOS process.

## Slide 18: Subharmonic mixer: Topology 2
Second Harmonic of LO is used.
Quadrature signal is applied to the stacked LO stages yields the product of twice the LO switching cycle.
Reduced size 90 degree Hybrid coupler is used to generate quadrature LO signal.
This topology Requires High supply voltage, Supply 6.6V,power consumption 150mW.
C=90fF
Reference: A.M¨ uller,M.Thiel,H.Irion,and H.-O.Ruoß,” A 122 GHz SiGe Active Subharmonic Mixer”.
RF =122GHz,LO=60GHz,CG=23dB with +3dBm LO power ,SSB NF=12 dB, SiGe:C HBT technology.

## Slide 19: Subharmonic Mixer: Topology 3
Fourth Harmonic of LO is used.
Transconductance mixing topology : Switching core may not work as a switch at frequency near .
Reference: Yanfei Mao,Klaus schmalz,johannes Borgraber and john christoph scheytt ,”245GHz LNA, Mixer and Subharmonic receiver in SiGe technology”,
IEEE transactions On Microwave theory and Technique ,vol 60,no.12,december 2012.
RF=245GHz,LO=60GHz,conversion gain 0.7dB, NF=23dB,=-9.1dBm.SiGe:C BiCMOS Technology, =300GHz.

## Slide 20: Passive Mixer
At very high frequency active mixers becomes complicated. In that case passive mixer can be used. As there is no conversion gain, passive mixer can reduce sensitivity of the receiver.
RC low pass filter
Matching circuit
Balun
Matching circuit
Reference: (1)16.9-mW 33.7-dB Gain mmWave Receiver Front-End in 65 nm CMOS, hun-Hsing Li and Chien-Nan Kuo, 2012 IEEE
(2)Double-Balanced 130-180 GHz Passive and Balanced 145-165 GHz Active Mixers in 45 nm CMOS , Ozgur Inac, Andy Fung2 and Gabriel M. Rebeiz, 2011 IEEE
Single balanced Mixer
65nm CMOS process
67~75GHz RF
Doubled balanced Mixer
45nm CMOS IBM12SOI process
Wide band RF 130GHz-180GHz
Conversion loss 12-13dB with 3dBm LO power

## Slide 21: Layout Methodology : Isolation
LO-RF Isolation
Reference:Low Power and High Gain Double-Balanced Mixer dedicated to 77 GHz Automotive Radar Applications, A. Mariano, T. Taris,
B. Leite, C. Majek, Y. Deval, D. Belot, 2010 IEEE
RF frequency=77GHz,LO Frequency=80GHz,130nm BiCMOS Technology
For X junction, reducing the width of path at crossing point allows minimizing the coupling effect.

## Slide 22: Layout Methodology (cont.)
Bias signals from large signal circuits (like the VCO and PA) must not be shared with sensitive circuit LNA.
When bias lines of different blocks must be crossed, local ground plane should be placed between them to minimize their capacitive coupling.
LNA should be placed as far as possible from frequency divider, PA .
Capacitance of the metal planes contribute on-chip decoupling which prevents the propagation of high frequency noise between adjacent blocks.so power bias and ground planes are interlaced to increase their capacitance.
Circuit blocks should be surrounded by n-well and p-well isolation ring to prevent noise from emerging or leaving.
Local GND plane used
for isolation
Metal planes for bias and
Power distribution (SiGe Tech.)

## Slide 23: Summary
Different passive components are described in mm-wave range. All passive components and transistor interconnections should be verified by EM simulation at this high frequency.
A number of techniques have been described to design LNA and mixer that ameliorate the challenges in mm-wave design.
Systematic methodologies in layout, coupling among building blocks through the power lines and substrate are critical tasks that must be addressed.

## Slide 24: Thank you