## Slide 1: LNA and Mixer Design in Millimeter wave
Presented By
Sadia Afroz

## Slide 2: Outline
Challenges in mm-wave design and passive components
LNA design
  General LNA topology
  Design example of W-band LNA
Challenges of mm-wave Mixer design
  Homodyne and Heterodyne Mixer
  Subharmonic Mixer
  Mm-wave Passive Mixer
Layout Methodology

## Slide 3: Challenges in mm-wave Design
Wavelength is few millimeters. λ= so when signal traverse components with appreciable size of wavelength, their true nature is like wave .so distributed effect must be considered as a part of design process.
Transmission lines provide better model accuracy than inductors due to well define ground planes.
Ground shielded Coplanar waveguide (G-CPW) is widely used for matching of interconnection.
Use of T-lines results noticeable increase in chip-area, alternatively SW-CPW are used.
CPW (IBM SIGe BiCMOS process)
SW-CPW

## Slide 4: Passive components
Folded Microstrip lines can also be used for inductor.
Transformer based balun is widely used to make single ended to differential. Usually Baluns are routed with top two thick metal layers.
Metal-insulator-metal (MIM) capacitor terminations must be considered as T-lines and modeled consequently.
Folded Microstrip line
(90nm CMOS Tech.)
Octagonal Transformer (center tapped)
Square Transformer (SONNET Layout)
3pF MIM Capacitor and its equivalent
Model (0.13um SiGe BiCMOS process)

## Slide 5: LNA Design in mm-wave
Simultaneous conjugate matching and noise matching at LNA input.
Multistage LNA: Inter-stage matching and stability.
When Transistors operate close to their ,lower gain and higher NF is observed.so devices should have high -current gain, cutoff frequency and breakdown voltage.

## Slide 6: LNA topology
CG LNA faces two serious issue in mm-wave :
  and its connections to gate and to ground exhibit a parasitic inductance which appears in series with gate at very high frequency. So matching and gain degrades.
  Gain of CG stage is much lower at mm-wave frequency.
Common gate topology:
Reference: Bezad Razavi,Fellow,IEEE ,“Design of millimeter-wave CMOS Radios:A tutorial” ,IEEE transactions on circuits and systems,regular papers,VOL 56,
No.1 Jan 2009
Needs very low impedance return path to ground

## Slide 7: LNA topology (cont.)
Inductively degenerated cascode topology:
Input matching depends on package parasitic.
It can operate in mm-wave range only if all the inductors are integrated on chip and GND return path for and display very low inductance.so careful layout consideration is needed.
Pole (in the order of ) introduced at node P adversely impact the gain and noise figure in mm-wave.
Exhibits a pole @ P

## Slide 8: LNA topology (cont.)
.
.
can be used as Series resonance , acts as inter-stage matching.
Transformer feedback LNA
Wide Band impedance and noise matching
Cascading three stage
Reference: Bezad Razavi,Fellow,IEEE ,“Design of millimeter-wave CMOS Radios:A tutorial” ,IEEE transactions on circuits and systems,regular papers,VOL 56,
No.1 Jan 2009

## Slide 9: W-band LNA
Four stage LNA, Gain=25dB, NF=8.3dB, 0.18um SiGe BiCMOS technology.
Capacitance of GSG pad is absorbed by input matching network.
To minimize parasitic inductance and ensure stability, is put as close as possible to the base of .
Local decoupling network for power supply.
To reduce footprint ,lumped inductors are used instead of T-lines, as well as inter-stage matching.
Next stage
Reference: Zhiming cheng,chun-cheng wang,Hsin-cheng yao,Payam heydari,”A BiCMOS W-band 2 focal-plane Array with On-chip Antenna”,
IEEE journal of Solid State Circuits,Vot.47,No.10,Octobar 2012.

## Slide 10: Common base topology for BJT
245GHz LNA, Gain=12dB, BW=26GHz , NF=9.4dB, power consumption=28mW.
Common base can achieve higher gain, wider bandwidth and higher isolation than CE stage.
Parasitic inductance at base terminal and bypass capacitor (ac ground) introduces negative resistance at emitter terminal by the equation (1).
For stability, collector current is reduced ( is reduced) to reduce .
With ensuring stability, parasitic inductance can increase gain and lower NF.
form a low pass filter improve isolation between CB stages.
Reference: Yanfei Mao,K. schmalz,J. Borngraber,J.C scheytt,“A 245GHz CB LNA in SiGe” ,Proceedings of 6th European Microwave Integrated circuits Conference
Negative Resistance seen from emitter due to , ……(1)

## Slide 11: Challenges in Mixer Design in mm-wave
Homodyne Mixer : High performance silicon base oscillator is very challenging in mm-wave frequency. so for direct conversion, LO is generated at a fraction of RF frequency and then use a multiplier prior to the frequency translation.
Heterodyne Mixer: Double conversion mixer is used to relax oscillator and frequency divider requirement in mm-wave application.
IQ Mixer: Generation of I Q phases of LO at mm-wave frequency and its balanced distribution is problematic. Quadrature operation typically degrades phase noise in mm-wave frequency.
Homodyne mixer
N frequency
multiplier
IF amplifier
Mixer

## Slide 12: Challenges in Mixer Design (Cont.)
LO distribution is difficult because of significant loss and mismatch in interconnects at high frequency.
AT mm-wave frequencies, it is difficult to get large LO signal, so conversion gain is low with weak LO signal.
Parasitic and layout consideration is an important issue for port to port isolation and stability.

## Slide 13: Conversion Gain or Loss
Conversion gain or loss is the ratio of the desired IF output (voltage or power) to the RF input signal value ( voltage or power).
LO
Transmission line is used to reduce the parasitic at the common node of switches.
Transconductor bias current is optimized for high gain. Base emitter area and number of finger of transconductance should be high.
Improve Gain
CG

## Slide 14: Homodyne Mixer in Millimeter wave
Reference: Saverio trotta ,bernhard Dehlink ,herbert Knapp ,Klaus Aufinger, Thomas F. Meister ,Josef Bock, Werne Simburger and Arpad L. Scholtz ,“Design considerations for low noise, Highly Linear Millimeter-wave Mixer in SiGe Bipolar Technology”
RC low-pass improves LO-IF Isolation
Balun
Balun
Small Signal Equivalent Circuit
RF=76 GHZ, CG=15 dB, SSB NF=11.2 dB, IIP3=8.5 dBm, Supply=5.5 V, SiGe:C technology.
Notes: LO signal is applied to the switching pairs of the mixer core via 50 ohm input matched LO balun,the coupling capacitances and two pairs of emitter follower.these emitter fllowers set the dc levels for the LO switching pairs,providing also low input impedance at this interface.C2 provides a path to GND to avoid potential parasitic oscillations.VbLo is onchip.

## Slide 15: Homodyne Mixer (Cont.)
Nonlinearity of B-E junction creates harmonics. High , L3-C1 represents very low impedance path for components generated by T1.
The feedthrough 2can increase IM3,both , 2 is highly attenuated by Low pass filter consisting of Ccs-L1,as RF and LO frequency are quite close.
The effect of parasitic capacitance at node A is lowered by L1 which also improves NF.
L2 and R1 improves stability.
- Filters 2
@
@ (O.C)
@ 2 (S.C)
Improve stability

## Slide 16: Folded structure
RF=76.5 GHz, LO=38.25 GHz, CG with IF amplifier=18 dB, Supply 3.3 V, 200 GHz SiGe BiCMOS technology.
Current in the input RF-pair can be optimized to improve NF and linearity. So Transistors are biased to get highest stable gain.
LO switch quad are biased in low current to reduce noise injected by these transistors.
Voltage headroom available at the IF output help to avoid the clipping of mixer core.
Reference: S.trotta,B.Dehlink,R. Reuter,Y.Yin,J.John,J.Kirchgessner,D.Morgan,P.welch,J.J.Lin,B.Knappenberger,I.To and M.Huang,”A multi-channel Rx for 76.5GHz
Automotive Radar Applications with 55dB IF Channel-to-Channel Isolation”, 4th European Micorwave Integrated Circuits Conference,2009.
T-Lines
,
Gain , NF
@ RF
RF pair is separated from Switching quad

## Slide 17: Heterodyne Mixer
LO @ 52 GHz
@ 26 GHz
@ 26 GHz
Two step down conversion scheme with RF =76-81 GHz, IF= 25-27 GHz. CG=5 dB,BW=10 GHz ,NF=11 dB.
Second quadrature LO is generated by dividing first LO by 2. Single frequency synthesizer can be used as first and second LO generation.
Shielded T-lines are used for matching circuits because required reactance is small, also These lines has high isolation, reduced coupling to adjacent circuits.
Second Mixer achieves 6dB conversion gain and BW=8 GHz in base band.
Reference: Aydin babakhani,Xiang Guan,Abbas komijani,Arun Natarajan,Ali hajimiri,”A &&GHz phased array transceiver with on chip antennas in
Silicon:receiver and Antennas”,IEEE journal of Solid State Circuit,vol.41,no.12,December 2006

## Slide 18: Subharmonic Mixer
Subharmonic mixer offers an alternative solution to fundamental mixers in mm-wave range since they allow for an LO at lower frequency.so this technique avoids separate multiplier and associated circuitry, resulting in lower power consumption and low active area.
Second harmonic or fourth harmonic of LO frequency are commonly used to downconvert RF signal to IF frequency.
To increase the gain of subharmonic mixer, the desired harmonic mixing product should be maximized. Harmonic component of LO signal is a function of conduction duty cycle.

## Slide 19: Subharmonic Mixer :Topology 1
RF= 50GHz,LO=24 GHz,peak CG=9dB,NF=11.8 dB from 3.3V supply, 0.12um SiGe BiCMOS process.
Second Harmonic of LO is used. Completely Doubled Balanced Gilbert cell.
This topology uses just two level of transistors hence lower supply voltage.
Differential Two stage ring oscillator is used to generate quadrature phase.
The some of the collector current of all switching pair has component indicating frequency doubling.
Ring oscillator
Reference: R.M. kodkani and L.E. larson,“An integrated 50GHz SiGe Subharmonic Mixer/downconverter with a quadrature ring VCO” ,IEEE 2007

## Slide 20: Subharmonic mixer: Topology 2
RF =122GHz,LO=60GHz,CG=23dB with +3dBm LO power ,SSB NF=12 dB, SiGe:C HBT technology.
Second Harmonic of LO is used.
Quadrature signal is applied to the stacked LO stages yields the product of twice the LO switching cycle.
Reduced size 90 degree Hybrid coupler is used to generate quadrature LO signal.
This topology Requires High supply voltage, Supply 6.6V,power consumption 150mW.
Reference: A.M¨ uller,M.Thiel,H.Irion,and H.-O.Ruoß,” A 122 GHz SiGe Active Subharmonic Mixer”.
C=90fF

## Slide 21: Subharmonic Mixer: Topology 3
RF=245 GHz,LO=60 GHz,conversion gain .7 dB,NF=23 dB,=-9.1 dBm.SiGe:C BiCMOS Technology, =300 GHz.
Fourth Harmonic of LO is used.
Transconductance mixing topology : Switching core may not work as a switch at frequency near .
Reference: Yanfei Mao,Klaus schmalz,johannes Borgraber and john christoph scheytt ,”245GHz LNA, Mixer and Subharmonic receiver in SiGe technology”,
IEEE transactions On Microwave theory and Technique ,vol 60,no.12,december 2012.

## Slide 22: Passive Mixer
At very high frequency active mixers becomes complicated. In that case passive mixer can be used. As there is no conversion gain, passive mixer can reduce sensitivity of the receiver.
Balun
Reference: (1)16.9-mW 33.7-dB Gain mmWave Receiver Front-End in 65 nm CMOS, hun-Hsing Li and Chien-Nan Kuo, 2012 IEEE
(2)Double-Balanced 130-180 GHz Passive and Balanced 145-165 GHz Active Mixers in 45 nm CMOS , Ozgur Inac, Andy Fung2 and Gabriel M. Rebeiz, 2011 IEEE
Single balanced Mixer.
65nm CMOS process.
67~75 GHz RF.
Doubled balanced Mixer.
45nm CMOS IBM12SOI process.
Wide band RF 130GHz-180 GHz.
Conversion loss 12-13dB with 3dBm LO power.
RC low pass filter
Matching circuit
Matching circuit

## Slide 23: Layout Methodology : Isolation
LO-RF Isolation
Reference:Low Power and High Gain Double-Balanced Mixer dedicated to 77 GHz Automotive Radar Applications, A. Mariano, T. Taris,
B. Leite, C. Majek, Y. Deval, D. Belot, 2010 IEEE
RF frequency=77GHz,LO Frequency=80GHz,130nm BiCMOS Technology.
For X junction, reducing the width of path at crossing point allows minimizing the coupling effect.

## Slide 24: Layout Methodology (cont.)
Bias signals from large signal circuits (like the VCO and PA) must not be shared with sensitive circuit LNA.
When bias lines of different blocks must be crossed, local ground plane should be placed between them to minimize their capacitive coupling.
LNA should be placed as far as possible from frequency divider, PA .
Capacitance of the metal planes contribute on-chip decoupling which prevents the propagation of high frequency noise between adjacent blocks.so power bias and ground planes are interlaced to increase their capacitance.
Circuit blocks should be surrounded by n-well and p-well isolation ring to prevent noise from emerging or leaving.
Local GND plane used
for isolation
Metal planes for bias and
Power distribution (SiGe Tech.)

## Slide 25: Summary
Different passive components are described in mm-wave range. All passive components and transistor interconnections should be verified by EM simulation at this high frequency.
A number of techniques have been described to design LNA and mixer that ameliorate the challenges in mm-wave design.
Systematic methodologies in layout, coupling among building blocks through the power lines and substrate are critical tasks that must be addressed.

## Slide 26: Thank you

## Slide 27: Back up

## Slide 29
Passive mixer 1:power consumtion 16.9mW from 1 V supply
IF is 8MHz is measured with LO power -2dBm,the highest gain is 33dB with Three stage LNA front end,NF of the front end is 12.2dB,IIP3 is -19dBm(overall)
As Rd isncreases gain is also increasedused rD is 2k,but linearity degraed with high Rd,so it has a good trade off between gain and linearity.

## Slide 30
Passive 2:CMOS SOI has ft 220GHz,balun loss 2dB,W/L=400um=16*1um/40nm,turn on R=16ohm,Vg=.3V=vth,for measurement 75-110Ghz gunn oscillator has been used with a multiplier 2.IF measurement is done by 26.5GHz spectrum analyzer.RF power has been swept upto 16dBm and no compression has been seen.Square shaped balun is used for LO

## Slide 31
Subharmonic mixer topology 1:.25um SGC25 IHP HBT,Ft is 200GHz,LO is 60Ghz,6.6V supply, Gain 23dB,NF=12dB, LO power=3dBm
The quadrature signal that is applied to the stacked LO stages yields the product LO(I-Q) which is twice the LO switching cycle.

## Slide 32
Subharmonic mixer topology 2: in run 2 .13um BiCmos (SG13S) technology is used.ft and fmax is 250 and 300G.in run 3 (SG13G2) SiGe .13 um bicmos tech is used.fourth harmonic signal is function of conduction cycle.
Q1 Q2 are biased at the edge of turn on voltage so that linarity is maximizedm.
Measured result: IF 1GHz,conversion gain <5Db,NF 39dB 1dB compression point -9dBm.

## Slide 34: IQ Mixer
IQ mixer:low power is the goal so transformers are used,telescopic cascode structures are avoided.the input is amplified by three stage LNA.Q5 Q6 acts as power active power splitter from LNA.G5 G6 are biased at peak Ft current.
Conversion gain 5db,1db compression is -10dbm,DSB NF is 18.5dB including the unity gain buffer.
~56mW power consumption

## Slide 35: Double balanced over single balanced
Increased linearilty
Better suppression of spurious products
High intercept point
Good supply rejection
Better IF isolation from LO and RF

## Slide 36
Inductively degenerated cascode topology:
Input matching depends on package parasitic.
Magnetic coupling between and can alter Input matching so careful layout consideration is needed.
A pole(in the order of ) is introduced at node P, thereby adversely impact the gain and noise figure in mm-wave.