## Slide 1: LNA and Mixer Design in Millimeter wave
Presented By
Sadia Afroz

## Slide 2: Outlines
Challenges in mm-wave design and passive components
LNA design
General LNA topology
Design example of W-band LNA
Challenge of mm-wave Mixer design
Homodyne and Heterodyne Mixer
Subharmonic Mixer
Mm-wave Passive Mixer
Layout Methodology

## Slide 3: Challenges in mm-wave Design
Wavelength is few millimeter. λ= so when signal traverse components with appreciable size of wavelength, their true nature is like wave rather than stationary voltage and current.so distributed effect must be considered as a part of design process.
Transmission lines provide better model accuracy than inductors due to well define ground planes. Long transmission lines cause phase shift on impedance.
Ground shielded Coplanar waveguide (G-CPW) is widely used for matching of interconnection. Ground shield is necessary to reduce substrate loss.
Use of T-lines results can occur noticeable increase in chip-area, alternatively SW-CPW are used as a part of matching networks. For same phase delay, it has lower loss than microstrip line.
CPW (IBM process)
SW-CPW

## Slide 4: Passive components
Folded Microstrip lines can also be used for inductor.
Transformer based balun is widely used to make single ended to differential ended.mm-wave transformers usually have one turn and can be square or octagonal shape. Baluns are routed with top two thick metal layers.
Metal-insulator-metal(MIM) capacitor terminations must be considered as T-lines and modeled consequently.
Folded Microstrip line (90nm CMOS Tech.)
Octagonal Transformer(center tapped)
Square Transformer(center tapped)
3pF MIM Capacitor and its equivalent model
(0.13um SiGe BiCMOS process)

## Slide 5: Challenges in LNA Design
Simultaneous conjugate matching and noise matching at LNA input
Multistage LNA: Inter-stage matching and stability
When Transistors operate close to their ,lower gain and higher NF is observed.so devices should have high -current gain, cutoff frequency and breakdown voltage.

## Slide 6: LNA topology
CG LNA faces two serious issue in mm-wave frequency and deep Submicron technology:
  Gate of the input transistor must see a very low input return path to GND so as to avoid degrading input matching and gain. But due to the parasitic inductance of to ground at very high frequency leads to a high impedance. So Matching becomes difficult.
  Gain of CG stage is much lower at mm-wave frequency.
Input matching depends on package parasitic.
Magnetic coupling between and can alter Input matching so careful layout consideration is needed.
A pole(in the order of ) is introduced at node P, thereby adversely impact the gain and noise figure in mm-wave.
Common gate topology
Inductively degenerated cascode topology

## Slide 7: LNA topology(cont.)
.
.
can be used as Series resonance, acts as inter-stage matching.
Transformer feedback LNA
Wide Band impedance and noise matching
Cascading three stage

## Slide 8: W-band LNA
Four stage LNA, Gain=25dB,NF=8.3dB,.18um SiGe BiCMOS technology.
Decoupling MIM capacitor is put as close as possible to the base of in layout to minimize parasitic inductance and ensure stability . further improve stability.
Local decoupling network for power supply is
Capacitance of GSG pad 20fF at 94GHz,should be absorbed by input matching network.
To reduce footprint ,lumped inductors are used instead of T-lines, as well as inter-stage matching.
Next stage

## Slide 9: Common base topology for BJT
245GHz LNA, Gain=12dB, BW=26GHz ,NF=9.4dB, power consumption=28mW,
For design upto 245GHz,Common base can achieve higher gain for each stage in multiple stage LNA, wider bandwidth and higher isolation because CB stage does not contain emitter to collector To cause miller effect.
Parasitic inductance can appear from the connection between base terminal and bypass capacitor(ac ground) which introduces negative resistance at emitter terminal by the equation,
For stability, collector current is reduced ( is reduced) to reduce .
With ensuring stability, parasitic inductance can increase gain and lower NF.
form a low pass filter for dc supply to improve isolation between CB stages.

## Slide 10: Challenges in Mixer Design in mm-wave
Homodyne Mixer : To achieve High performance silicon base oscillator is very challenging in mm-wave frequency. so for direct conversion, LO is generated at a fraction of RF frequency and then use a multiplier prior to the frequency translation.
Heterodyne Mixer: Double conversion mixer is used to relax oscillator and frequency divider requirement in mm-wave application.
IQ Mixer: Generation of I Q phases of LO at mm-wave frequency and its balanced distribution is problematic. Quadrature operation typically degrades phase noise in mm-wave frequency.
LO distribution is difficult because of significant loss and mismatch in interconnects at high frequency.
AT mm-wave frequencies, it is difficult to get large LO signal, so conversion gain is low with weak LO signal.
Parasitic and layout consideration is an important issue for port to port isolation.
Homodyne mixer
N frequency
multiplier
IF amplifier
Mixer

## Slide 11: Conversion Gain or Loss
Conversion gain or loss is the ratio of the desired IF output (voltage or power) to the RF input signal value ( voltage or power).
Improve Gain
LO
CG
Transmission line is used to reduce the parasitic at the common node of switches.
Transconductor bias current is optimized for high gain. Base emitter area and number of finger of transconductance should be high.

## Slide 12: Design of Homodyne Mixer in Millimeter wave
O.C for 2
O.C for
S.C @ 2
Reference: Design considerations for low noise,highly Linear Millimeter-wave Mixer in SiGe Bipolar Technology
@ RF
@ 2RF
@ RF
RF=76GHZ, CG=15dB, SSB NF=11.2dB, IIP3=8.5dBm, Supply=5.5V, SiGe:C technology.
Nonlinearity of B-E junction creates harmonics. High , L3-C1 represents very low impedance path for components generated by T1.
The feedthrough 2can increase IM3,both , 2 is highly attenuated by Low pass filter consisting of Ccs-L1,as RF and LO frequency are quite close.
The effect of parasitic capacitance at node A is lowered by L1 which also improves NF.
L2 and R1 improves stability.

## Slide 13: Folded structure
@ RF
,
Gain ,NF
RC lowpass improves LO-IF isolation
RF=76.5GHz, LO=38.25GHz, CG with IF amplifier=18dB, Supply 3.3V, 200 GHz SiGe BiCMOS technology.
Frequency doubled is used to generate desired LO.
Current in the input RF-pair can be optimized to improve NF and linearity. So Transistors are biased to get highest stable gain.
LO switch quad are biased in low current to reduce noise injected by these transistors.
Voltage headroom available at the IF output help to avoid the clipping of mixer core.

## Slide 14: Heterodyne Mixer
LO @ 52GHz
@ 26 GHz
@ 26 GHz
Two step down conversion scheme with RF =76-81 GHz, IF= 25-27 GHz. CG=5dB,BW=10GHz,NF=11dB
Second quadrature LO is generated by dividing first LO by 2. Single frequency synthesizer can be used as first and second LO generation.
Shielded T-lines are used for matching circuits because required reactance is small, also These lines has high isolation, reduced coupling to adjacent circuits.
Second Mixer achieves 6dB conversion gain and BW=8GHz in base band.

## Slide 15: Subharmonic Mixer
Subharmonic mixer offers an alternative solution to fundamental mixers in mm-wave range since they allow for an LO at lower frequency.so this technique avoids separate multiplier and associated circuitry, resulting in lower power consumption and low active area.
Second harmonic or fourth harmonic of LO frequency are commonly used to downconvert RF signal to IF frequency.
To increase the gain of subharmonic mixer, the desired harmonic mixing product should be maximized. Harmonic component of LO signal is a function of conduction duty cycle.

## Slide 16: Subharmonic Mixer :Topology 1
RF= 50GHz,LO=24 GHz,peak CG=9dB,NF=11.8 dB from 3.3V supply, .12um SiGe BiCMOS process.
Second Harmonic of LO is used. Completely Doubled Balanced Gilbert cell.
This topology uses just two level of transistors hence lower supply voltage.
Differential Two stage ring oscillator is used to generate quadrature phase.
The some of the collector current of all switching pair have the form of full-wave rectified sine wave and composed of even harmonics only. The current has component indicating frequency doubling.
Ring oscillator

## Slide 17: Subharmonic mixer: topology 2
RF =122GHz,LO=60GHz,CG=23dB with +3dBm LO power ,SSB NF=12 dB, SiGe:C HBT technology.
Second Harmonic of LO is used. Doubling the Lo switching cycle is the basis of even harmonic operation.
LO switching transistors yields in a stacked gilbert topology. Quadrature signal is applied to the stacked LO stages yields the product of twice the LO switching cycle.
Reduced size 90 degree Hybrid coupler is used to generate quadrature LO signal.
This topolology Requires High supply voltage, Supply 6.6V,power consumption 150mW.
C=90fF
Reference: A 122 GHz SiGe Active Subharmonic Mixer, A.M¨ uller,M.Thiel,H.Irion,and H.-O.Ruoß,
Dept.CR/ARE,Robert-Bosch-Platz1,70839Gerlingen-Schillerh¨ ohe,Germany,

## Slide 18: Subharmonic Mixer: Topology 3
Topology 2:
RF=245GHz,LO=60GHz,conversion gain .7dB,NF=23dB,=-9.1dBm.SiGe:C BiCMOS Technology, =300GHz.
Fourth Harmonic of LO is used.
Transconductance mixing topology : Switching core may not work as a switch at frequency near .

## Slide 19: Passive Mixer
At very high frequency active mixers becomes complicated. In that case passive mixer can be used. As there is no conversion gain, passive mixer can reduce sensitivity of the receiver.
RC low pass filter
Matching circuit
Balun
Matching circuit
Reference: (1)16.9-mW 33.7-dB Gain mmWave Receiver Front-End in 65 nm CMOS, hun-Hsing Li and Chien-Nan Kuo, 2012 IEEE
(2)Double-Balanced 130-180 GHz Passive and Balanced 145-165 GHz Active Mixers in 45 nm CMOS , Ozgur Inac, Andy Fung2 and Gabriel M. Rebeiz, 2011 IEEE
Single balanced Mixer
65nm CMOS process
67~75GHz RF
Doubled balanced Mixer
45nm CMOS IBM12SOI process
Wide band RF 130GHz-180GHz
Conversion loss 12-13dB with 3dBm LO power

## Slide 20: Layout Methodology : Isolation
LO-RF Isolation
Reference:Low Power and High Gain Double-Balanced Mixer dedicated to 77 GHz Automotive Radar Applications, A. Mariano, T. Taris,
B. Leite, C. Majek, Y. Deval, D. Belot, 2010 IEEE
RF frequency=77GHz,LO Frequency=80GHz,130nm BiCMOS Technology
For X junction, reducing the width of path at crossing point allows minimizing the coupling effect.

## Slide 21: Layout Methodology(cont.)
Bias signals from large signal circuits (like the VCO and PA) must not be shared with sensitive circuit LNA.
When bias lines of different blocks must be crossed, local ground plane should be placed between them to minimize their capacitive coupling.
LNA should be placed as far as possible from frequency divider, PA .
Capacitance of the metal planes contribute on-chip decoupling which prevents the propagation of high frequency noise between adjacent blocks.so power bias and ground planes are interlaced to increase their capacitance.
Circuit blocks should be surrounded by n-well and p-well isolation ring to prevent noise from emerging or leaving.
Local GND plane used
for isolation
Metal planes for bias and
Power distribution (SiGe Tech.)

## Slide 22: Summary

## Slide 23: Thank you

## Slide 24: Back up

## Slide 26
Passive mixer 1:power consumtion 16.9mW from 1 V supply
IF is 8MHz is measured with LO power -2dBm,the highest gain is 33dB with Three stage LNA front end,NF of the front end is 12.2dB,IIP3 is -19dBm(overall)
As Rd isncreases gain is also increasedused rD is 2k,but linearity degraed with high Rd,so it has a good trade off between gain and linearity.

## Slide 27
Passive 2:CMOS SOI has ft 220GHz,balun loss 2dB,W/L=400um=16*1um/40nm,turn on R=16ohm,Vg=.3V=vth,for measurement 75-110Ghz gunn oscillator has been used with a multiplier 2.IF measurement is done by 26.5GHz spectrum analyzer.RF power has been swept upto 16dBm and no compression has been seen.Square shaped balun is used for LO

## Slide 28
Subharmonic mixer topology 1:.25um SGC25 IHP HBT,Ft is 200GHz,LO is 60Ghz,6.6V supply, Gain 23dB,NF=12dB, LO power=3dBm
The quadrature signal that is applied to the stacked LO stages yields the product LO(I-Q) which is twice the LO switching cycle.

## Slide 29
Subharmonic mixer topology 2: in run 2 .13um BiCmos (SG13S) technology is used.ft and fmax is 250 and 300G.in run 3 (SG13G2) SiGe .13 um bicmos tech is used.fourth harmonic signal is function of conduction cycle.
Q1 Q2 are biased at the edge of turn on voltage so that linarity is maximizedm.
Measured result: IF 1GHz,conversion gain <5Db,NF 39dB 1dB compression point -9dBm.

## Slide 31: IQ Mixer
IQ mixer:low power is the goal so transformers are used,telescopic cascode structures are avoided.the input is amplified by three stage LNA.Q5 Q6 acts as power active power splitter from LNA.G5 G6 are biased at peak Ft current.
Conversion gain 5db,1db compression is -10dbm,DSB NF is 18.5dB including the unity gain buffer.
~56mW power consumption

## Slide 32: Double balanced over single balanced
Increased linearilty
Better suppression of spurious products
High intercept point
Good supply rejection
Better IF isolation from LO and RF

## Slide 33
Inductively degenerated cascode topology:
Input matching depends on package parasitic.
Magnetic coupling between and can alter Input matching so careful layout consideration is needed.
A pole(in the order of ) is introduced at node P, thereby adversely impact the gain and noise figure in mm-wave.