## Slide 1: Silicon RF Phased Array at X-, Q-, W-Band and Beyond Kwang-Jin Koh Virginia Tech email: kkoh@vt.edu May 31, 2013

## Slide 2: Outline
Introduction
  Discrete phased array: example
Phase shifter design
  Active phase shifter
  Some comparisons with passive one
Phased array designs
  X-band receiver
  Q-band transmitter & receiver
  W-band & beyond
Conclusion
Phase
shifter
Microwave
phased array
receiver
mm-wave
phased array
transmitter
S
ICTAS 2013: Phased Array Designs

## Slide 3
Discrete design (single element, X-band: 8-12 GHz)
Typical T/R module implementation (B.A. Kopp, T-MTT, 2002)
44.7 %
25.3 %
14.7 %
15.3 %
GaAs
Packaging
Labor
Other
T/R module cost elements ($200-2000) (@ typical performance at X-band)
III-V (GaAs) technology
Discrete implementation: expensive & bulky
50-W interface results in high power consump.
Notes: This is an example of conventional approach of phased-array transmit and receive module. X-band, 8-12 Ghz range is a popular for defense, and satellite RADAR systems. This is just one element and it has LNA, PA, phase shifter and some supporting amplifiers. Because the frequency is decently high compared with commercial cellular systems, most of these components except for this digital control part are based on GaAs technology. As you can see in this figure, everything is discretely attached on a ceramic board.
When we breakdown the cost, GaAs and packaging, and associated laboring costs take up to 70% of the total cost. Which means when successfully integrating these component in silicon technology, we can save roughly up to 50% of the cost.
Again this is just single element, and when 64-element antenna array, we need 64 of this board, which can be quite bulky and very expensive.
Another issue in this discrete system is power consumption. The interface between these RF building blocks is a 50-ohm interface. Which means each building block needs a substantial power consumption to drive the 50-ohm matching impedance.

## Slide 4
Discrete design (single element, X-band: 8-12 GHz)
Typical T/R module implementation (B.A. Kopp, T-MTT, 2002)
44.7 %
25.3 %
14.7 %
15.3 %
GaAs
Packaging
Labor
Other
Integrate these in silicon (low-cost phased array < $ 1-10)
Leverage recent advances in silicon tech.
Integrate many blocks in silicon
Low power consumption
T/R module cost elements ($200-2000) (@ typical performance at X-band)
Notes: This is an example of conventional approach of phased-array transmit and receive module. X-band, 8-12 Ghz range is a popular for defense, and satellite RADAR systems. This is just one element and it has LNA, PA, phase shifter and some supporting amplifiers. Because the frequency is decently high compared with commercial cellular systems, most of these components except for this digital control part are based on GaAs technology. As you can see in this figure, everything is discretely attached on a ceramic board.
When we breakdown the cost, GaAs and packaging, and associated laboring costs take up to 70% of the total cost. Which means when successfully integrating these component in silicon technology, we can save roughly up to 50% of the cost.
Again this is just single element, and when 64-element antenna array, we need 64 of this board, which can be quite bulky and very expensive.
Another issue in this discrete system is power consumption. The interface between these RF building blocks is a 50-ohm interface. Which means each building block needs a substantial power consumption to drive the 50-ohm matching impedance.

## Slide 5: Outline
Introduction
  Discrete phased array: example
Phase shifter design
  Active phase shifter
  Some comparisons with passive one
Phased array designs
  X-band receiver
  Q-band transmitter & receiver
  W-band & beyond
Conclusion
Phase
shifter
Microwave
phased array
receiver
mm-wave
phased array
transmitter
S
ICTAS 2013: Phased Array Designs

## Slide 6
3.8 mm
3.5 mm
LNA
Phase shifter
Ref: Comeau etal (Georgia Tech), “A SiGe Receiver for X-Band T/R Radar Modules”, IEEE JSSC, Sept. 2008
Typical passive phase shifter (example)
Cascading many stages of this cell
 Blue path: low-pass  Phase lagging
Utilize phase difference
Low-pass / High-pass approach
 Red path: high-pass  Phase leading
Issues: area & loss
Freq: 8-10.7 GHz (D=2.7 GHz, < 25% BW)  Phase resolution: 5-bit (11.25o)  RMS phase error < 9o  ~ 36 inductors  Loss ~ 20 dB  Area > 8 mm2
Notes: And this is typical design example of the low-pass, high-pass approaches.
This Blue path is high-pass leading a phase, and the red path is a low-pass, lagging the phase. And by switching one from the other, we can leverage the phase difference to generate different phase state. But to generate multiple phase states, we need to cascade many of this unit cells, demanding a lot of space. For example, in this case they used more than 10 stages, and the size is huge, the size phase shifter alone is bigger than 8 mm2. They used around 36 inductors for the phase shifter itself. Loss is also significant, around 20 dB.
From now on, I will show how we can decrease the size by more than 50 times, while achieving better performance at the same operation frequency.

## Slide 7
Active phase shifter architecture: vector modulator
output phase =tan-1(Q / I)
* The in/out balun stages will not be necessary for fully integrated differential systems
Phase shifter core
Mostly active circuits
Small chip area & Gain
DAC control
Fine accurate phase control & calibration
Balun provides differential signal
I/Q network splits signal into I & Q
vector signals
VGA controls gain for I & Q path
I/Q signals are added in V-domain
(phase interpolation)
DAC provides 4-bit phase control
CAL calibrates DAC to get 5-bit
phase resolution
Operation
Notes: I proposed this active phase shifter architecture, which is basically based on phase interpolation technique.
First stage is a single-to-differential conversion stage, and after that this IQ network generates quadrature phased I and Q signals based on input differential signal. Then, each I and Q signal will be amplified with a predetermined gain for each path, and then, finally be added at the output.
By adding these I and Q signal with different amplitudes, we are actually interpolating phase between I-phase and Q-phase. Different gain setting between I and Q path gives different output phases. This DAC changes gain in each IQ path in a way it can generate 16 different phase states at the output.
The beauty of this active approach is that we can calibrate the output phase by calibrating this DAC. In this design, I utilized the DAC for 4-bit phase control, and eventually calibrated the DAC to get 5-bit phase resolutions.
As you can see, it’s mostly active circuit and we can integrate all the building blocks in a tiny small space. In a fully balanced system, we don’t need the in/out balun circuits. And this is a simplified schematic for the core part of the phase shifter.