## Slide 1: Weekly Report
By
SADIA AFROZ LISA
10/04/2012

## Slide 2: Last Week
Matched LNA with real components with single wire transmission lines, observed performance at 95GHz:
      Observed that Gain is much lower(7.22 DB)
      Noise figure is 7.2DB at 95GHZ
      S11=-19 DB,S22=-23 DB,S12 is below -21DB
      To increase the gain, Re-design LNA with coupled inductors to boost the gain, coupled inductors are used between emitter and collector. The performance was observed at 95 GHz:
            Achieved gain is 10.3 DB
            Noise figure is 7.33 DB
            S11= -21 DB,S22= -23 DB,S12 is below -23 DB
            For all cases K>1 and Bif>0, so stability is maintained.

## Slide 3: Design of LNA ,Using Single wire transmission only,Bias current 6.282mA with 2.2V supply

## Slide 4: S- parameter measurement,S21=7.22 GHz

## Slide 5: Noise figure and minimum noise figure with stability, NF=7.2DB at 95GHz

## Slide 6: Design of LNA with Gain boosting using coupled inductor between collector and emitter,Ic=6.346mA

## Slide 7: S parameter,S21=10.33 DB at 95GHz

## Slide 8: Noise figure and minimum noise figure with stability, NF=7.33DB at 95GHz

## Slide 9: Next Week
Design of second stage of LNA to increase the gain above 15 DB and necessary matching.
Complete LNA structure
Study of Layout