## Slide 1
Report 21st September
Sadia Afroz Lisa

## Slide 2
  Last week
    Studied several papers and journals including books based on LNA
    Designed and simulate several LNA structures with adjusting bias current 6mA including input impedance matching. Beta was high enough (over 500) to get lower NF.
    Measure s-parameter, input impedance and Matched. My target is 100GHz.
    Working on a Common base LNA from a particular journal in 2012 to modify it for supply voltage
    Next Week
    Will try to find out the equations for input output relations and also for impedance matching of that particular three stage cascaded LNA
    Necessary modification of cirucuits for matching and high gain.
    Study the chapters of “Microelectronics circuit design” by Jaeger to understand the cascaded BJT amplifiers and their frequency response

## Slide 3: LNA 1:CE based LNA, with high beta, but problem is very lower gain,

## Slide 4: S11 in DB for LNA 1,Here S11 is minimum at 100GHz

## Slide 5: Input impedance for LNA 1,At 100 GHz Here Zreal is almost 50 ohm ,Zim is nearly zero but some modification is needed to make exactly zero

## Slide 6
Problem
Problem with this structure is S21 is very low,S12 is below -15db.NF is around 7DB at 100Ghz and increases with frequency
No output matching is done yet for this, this will require some modification too.

## Slide 7: LNA 2

## Slide 8: S-parameter shows that with some modification higher gain and lower s11 can be got at 100 GHz

## Slide 9: Real part of Input impedance and output impedance is almost equal to 50 ohm ,imaginary part of Zim is below 0 near 100Ghz

## Slide 10: Simulated noise figure

## Slide 11
Problem
-Supply voltage here is 5V so keeping the same bias current supply voltage has to be decreased so modification is needed.
-Imaginary part of output impedance is still unmatched.