## Slide 1: Weekly Report By Sadia Afroz Lisa 09/29/2012

## Slide 2
Matched impedance of LNA
Simulated collector voltages, Voltage and current gain, changed the component values, to examine whether the gain can be increase .It shows with 5.9mA,L(emitter)=10um,maximum gain at 100GHz can be achieved 14db.
Simulated the IBM8HP library components(R,L,C) individually to measure which components in which values shows better performance at 100GHz.
Simulated the LNA circuit with real L,R,C with using optimized sizes.

## Slide 3: The original circuit of LNA

## Slide 4: S-parameter Simulation,NF=7DB

## Slide 5
Circuit with IBM8HP library Resistance and capacitance

## Slide 6: S parameter Simulation

## Slide 7
Gain is reduced at 100GHz,Bias current is almost same.
The output capacitance is 17fF instead of 13fF with is needed for original circuit, but minimum MIM capacitance is 17fF
NF is 7.2dB

## Slide 8: Components are replaced by IBM8HP library, inductors are replaced by single wire transmission lines

## Slide 9: S-parameter simulation

## Slide 10
Gain is much reduced, NF is 7.7Db at 100Ghz
Inductors are needed upto 200pH so transmission lines are used. Symind inductors shows worse Q at high frequency.
Singlewire transmission lines can not be used to get high L so series combination is used.But Q decreases. resistance is maximum 8 ohm for 200pH.

## Slide 11: Next week
Modify to get high gain
Matching input and outputs because transmission lines added resistive effects
Also need to decrease NF
Install ADS for EM simulation