## Slide 1: SiGe Qualification – Vendor Perspective
Chuck Tabbert
Director, Aerospace & Defense Services
505-823-1293
ctabbert@jazzsemi.com

## Slide 2: Jazz Semiconductor Overview
A Leading Pure-Play Silicon Wafer Foundry With On-Shore Manufacturing
Formed in 2002 from Conexant Systems (formerly part of Rockwell International)
Private but announced plan to merge with Acquicor which will make the combined entity public
17k wpm 8-inch Si wafer Fab in Newport Beach with >15-Year Track Record, >$1B investment
On-Shore foundry
Revenue of ~200M/yr
ITAR Registered, NSA Sponsorship for Trusted Foundry
Focus on Specialty Technology
  0.5-micron to 0.13-micron
  Analog/RF: CMOS, SiGe BiCMOS, High Voltage
  Other: High Q Passives, MEMs, Imager
  A/D Specific: Stitching, foundry for Rad-Hard community
Established as a Trusted Partner Throughout Commercial and DoD Markets

## Slide 3: JAZZ Trusted Foundry Initiative
Jazz is aggressively pursing trusted foundry status to serve CAT 1 program (classified & ITAR) needs
  Jazz is first US semiconductor company to achieve ISO/IEC 27001:2005 certification for Information Security
Three parallel efforts underway
  Desktop accreditation through TAPO and future accreditations through DMEA
    Procedures provided to TAPO/DMEA for review
  DSS Facilities Clearance In Progress
  Employee Clearances In Progress
Accreditation probable within 3 months

## Slide 4: Jazz Process Technology Spectrum
SiGe 150 GHz
Imager
SiGe 200 GHz
Stitching Service
SiGe 80 GHz
SiGe 65 GHz
Si 30 GHz
BiCMOS
8V
12V
20V
40V
Power CMOS BCD
1.2
1.8
2.5V
3.3V
5.0V
Analog / RF CMOS
Now Available
In Development
Other

## Slide 5
Technology
SiGe for High Performance, Low Noise, Low Power Consumption
0
25
50
75
100
125
150
175
200
0.01
0.1
1
10
Ic (mA) for Minimum We and Le = 1μm
Ft
(GHz)
SBC18H2 SBC13H2
0.18µm 0.13µm
SiGe
0.35µm
Si/SiGe
SBC18HX
SBC35
BC35
SBL13
BiCMOS
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: 0.35µm SiGe (SBC35: 62GHz)
0.35µm SiGe BiCMOS
0.35µm CMOS with High Performance SiGe
High volume production (RF Transceivers, TV Tuners, Optical Network, Precision Analog)
MPW service available (scheduled every 2 months)
SBC35 SiGe NPNs
0.35µm Cost Effective, High Performance SiGe BiCMOS Platform
SBC35 CMOS & Passives
BiCMOS

## Slide 7: 0.18µm SiGe (SBC18: 155 and 200GHz)
0.18µm SiGe BiCMOS
0.18µm CMOS with High Performance SiGe (155GHz and 200GHz options)
High volume production (RF Transceivers, TV Tuners, Optical Network, Precision Analog)
MPW service available (scheduled every 2 months)
SBC18 SiGe NPNs
High Performance (155 and 200GHz), Feature Rich, 0.18µm SiGe BiCMOS Platform
SBC18 CMOS & Passives
BiCMOS

## Slide 8
0.13µm SiGe (SBL13: 90GHz)
Cost Effective 0.13µm SiGe BiCMOS for RF and Analog SoC
0.13µm SiGe BiCMOS with same layer count as Cu-based 0.13m RF CMOS
0.13m CMOS front-end with a low-cost Aluminum back-end
100+ GHz Fmax NPN transistors (High Speed and Standard)
High Voltage (6V BVceo) NPN transistor available with 1 mask adder
Design Kit available
SBL13 SiGe NPN Specifications
SBL13 RF CMOS Specifications
CA13HA
Vdd
1.2/3.3
V
Native FET
Coming Soon
Deep Nwell
Available
HV FET
Coming Soon
V
MIM Cap
5.6
fF/µm2
LV Res
310
ohm/sq
HV Res
Coming Soon
ohm/sq
Metal Layers
6
#
Top Metal
3
µm
BiCMOS

## Slide 9
0.13µm SiGe BiCMOS: High Performance Version
0.13µm CMOS front-end with a low-cost Aluminum back-end
200GHz Ft/Fmax NPN transistors
Design Kit Availability Q1 ‘07
SBC13 RF CMOS Specifications
SBC13H2 SiGe NPN Specifications
0.13µm SiGe (SBC13: 200GHz Ft)
BiCMOS
High Performance 0.13µm SiGe BiCMOS

## Slide 10: Complementary BiCMOS – Vertical PNP
Markets
  Push/Pull Amplifiers
  Hard Disk Drive (HDD) Pre-Amp and Driver ICs
  High-Performance Data Converters
VPNP Module Integrated with
  0.35µm SiGe BiCMOS
  0.18µm SiGe BiCMOS
  0.18µm RF CMOS
 | 0.35μm VPNP | 0.18μm VPNP | 
Peak Beta Ft (Vce = -5V) BVceo | 50 15 -7 | 50 17 -7 | GHz V
BiCMOS

## Slide 11: SiGe – High Volume Production & Increasing
Source: Semico Research Corp
$M, Units=M | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | CAGR 02-07
Revenue | $448 | $783 | $1,311 | $1631 | $2,225 | $3,132 | 47.5%
Units Shipped | 407 | 675 | 1,162 | 1,550 | 2,397 | 3,648 | 55.1%
Between 2003 & 2007:
Industry shows a 5X increase in units shipped
Jazz has seen a 15X increase in wafers shipped
Seems like SiGe is a worldwide accepted technology qualified for commercial & industrial use
The question here is – is this technology ready for use in the harsh environments of military and space applications -
Extended Temperature, Long Term Reliability, Radiation Effects?

## Slide 12: SiGe – Where’s It Being Used Now? Radios - Of Course!
Cell Phones - SiGe in the RF Transceiver front-end IC
Fiber optics components (receivers, transmitters, transceivers and amplifiers)
HDD - SiGe technology has a benefit in the read/write channels and the preamplifiers in HDDs
WLAN - More range and higher frequencies for 802.11 modules means that more power will be needed and that the frequency capabilities of RF CMOS will be exceeded
GPS - SiGe can provide a cleaner signal and, most importantly, lower power consumption than other GPS integrated receiver solution
Cordless Phones: frequency requirements and power levels are too low to force non-silicon solutions
Bluetooth - modules are low power modules operating at a frequency low enough that silicon technology is adequate
Digital STB -Amplifier and VCO (Voltage Controlled Oscillator) – Lower noise & better gain
Notice: Two Generation Bump In Performance from RFCMOS to SiGe

## Slide 13: SBC18HX Process Reliability Tests
Standard Industry Process Tests Completed and Passed
  Electromigration
  Hot Carrier Injection
  Gate Oxide Integrity
  Threshold Voltage Stability
  BJT Reverse Stress
  Passivation Integrity
Standard Industry Product Tests Completed and Passed

## Slide 14: Jazz Specific Radiation / Temperature Data
Proton Testing – 62.5MeV @1E12-2E13 fluences – 2006 tests by Univ of Wisconsin
  DC results – slight degradation in base current
  Small-Signal AC results
    slight degradation in power gain
    Slight degradation in Fmax
    Linearity – better linearity – increased IIP3
    Large signal high-power - .0.3dB degradation in Pout, <2%PAE degradation
Cryogenic (77K) & High Temperature (160C) Data showed minor fluxuation in RF Power Performance (Univ of Wisconsin/NASA-GRC)

## Slide 15: RH SiGe Efforts at Jazz
SHAR program developed Rad-Aware models for Jazz SBC18 process.
  Design teams designing circuits and rad testing – 2007
Thick-Film SOI process integration completed.
  Fabrication of 0.13 SiGe circuits (SBC13) on SOI proceeding- 2007
  CMOS library adding deep-trench isolation

## Slide 16: Summary
SiGe is a mainstream commercial technology
Industry push to integrated low power RF transceivers will require SiGe integration into Military & Space technology portfolio
Radiation effects and temperature effects seem very manageable due to robustness of base technology
Jazz is prepared to exploit this technology for Military & Space applications