## Slide 1: Mixer Design
Introduction to mixers
Mixer metrics
Mixer topologies
Mixer performance analysis
Mixer design issues

## Slide 2: What is a mixer
Frequency translation device
  Convert RF frequency to a lower IF or base band for easy signal processing in receivers
  Convert base band signal or IF frequency to a higher IF or RF frequency for efficient transmission in transmitters
Creative use of nonlinearity or time-variance
  These are usually harmful and unwanted
  They generates frequencies not present at input
Used together with appropriate filtering
  Remove unwanted frequencies

## Slide 3: Two operation mechanisms
Nonlinear transfer function
  Use device nonlinearities creatively!
  Intermodulation creates the desired frequency and unwanted frequencies
Switching or sampling
  A time-varying process
  Preferred; fewer spurs
  Active mixers
  Passive mixers

## Slide 4: An ideal nonlinearity mixer
x(t)
y(t)
x(t)y(t)
If
Then the output is
down convert
up convert

## Slide 5: Commutating switch mixer

## Slide 6: A non-ideal mixer

## Slide 7
Conversion gain – lowers noise impact of following stages
Noise Figure – impacts receiver sensitivity
Port isolation – want to minimize interaction between the RF, IF, and LO ports
Linearity (IIP3) – impacts receiver blocking performance
Spurious response
Power match – want max voltage gain rather than power match for integrated designs
Power – want low power dissipation
Sensitivity to process/temp variations – need to make it manufacturable in high volume
Mixer Metrics

## Slide 8: Conversion Gain
Conversion gain or loss is the ratio of the desired IF output (voltage or power) to the RF input signal value ( voltage or power).
If the input impedance and the load impedance of the mixer are both equal to the source impedance, then the voltage conversion gain and the power conversion gain of the mixer will be the same in dB’s.

## Slide 9: Noise Figures: SSB vs DSB
Image
band
Signal
band
Thermal
noise
LO
IF
Signal
band
Thermal
noise
LO
0
Single side band
Double side band

## Slide 10: SSB Noise Figure
Broadband noise from mixer or front end filter will be located in both image and desired bands
Noise from both image and desired bands will combine in desired channel at IF output
  Channel filter cannot remove this

## Slide 11: DSB Noise Figure
For zero IF, there is no image band
  Noise from positive and negative frequencies combine, but the signals combine as well
DSB noise figure is 3 dB lower than SSB noise figure
  DSB noise figure often quoted since it sounds better

## Slide 12: Port-to-Port Isolations
RF
IF
LO
Isolation
  Isolation between RF, LO and IF ports
  LO/RF and LO/IF isolations are the most important features.
  Reducing LO leakage to other ports can be solved by filtering.

## Slide 13: LO Feed through
Feed through from the LO port to IF output port due to parasitic capacitance, power supply coupling, etc.
Often significant due to strong LO output signal
  If large, can potentially desensitize the receiver due to the extra dynamic range consumed at the IF output
  If small, can generally be removed by filter at IF output

## Slide 14: Reverse LO Feed through
Reverse feed through from the LO port to RF input port due to parasitic capacitance, etc.
  If large, and LNA doesn’t provide adequate isolation, then LO energy can leak out of antenna and violate emission standards for radio
  Must insure that isolation to antenna is adequate

## Slide 15: Self-Mixing of Reverse LO Feedthrough
LO component in the RF input can pass back through the mixer and be modulated by the LO signal
  DC and 2fo component created at IF output
  Of no consequence for a heterodyne system, but can cause problems for homodyne systems (i.e., zero IF)

## Slide 16: Nonlinearity in Mixers
Ignoring dynamic effects, three nonlinearities around an ideal mixer
Nonlinearity A: same impact as LNA nonlinearity
Nonlinearity B: change the spectrum of LO signal
  Cause additional mixing that must be analyzed
  Change conversion gain somewhat
Nonlinearity C: cause self mixing of IF output

## Slide 17: Focus on Nonlinearity in RF Input Path
Nonlinearity B not detrimental in most cases
  LO signal often a square wave anyway
Nonlinearity C avoidable with linear loads
Nonlinearity A can hamper rejection of interferers
  Characterize with IIP3 as with LNA designs
  Use two-tone test to measure (similar to LNA)

## Slide 18: Spurious Response
IF Band

## Slide 19: Mixer topologies
Discrete implementations:
  Single-diode and diode-ring mixers
IC implementations:
  MOSFET passive mixer
  Active mixers
  Gilbert-cell based mixer
  Square law mixer
  Sub-sampling mixer
  Harmonic mixer

## Slide 20: Single-diode passive mixer
Simplest and oldest passive mixer
The output RLC tank tuned to match IF
Input = sum of RF, LO and DC bias
No port isolation and no conversion gain.
Extremely useful at very high frequency (millimeter wave band)

## Slide 21
Poor gain
Good LO-IF isolation
Good LO-RF isolation
Poor RF-IF isolation
Attractive for very high frequency applications where transistors are slow.
Single-balanced diode mixer

## Slide 22
Poor gain (typically -6dB)
Good LO-IF LO-RF RF-IF isolation
Good linearity and dynamic range
Attractive for very high frequency applications where transistors are slow.
Double-balanced diode mixer

## Slide 23
CMOS Passive Mixer
M1 through M4 act as switches

## Slide 24: CMOS Passive Mixer
Use switches to perform the mixing operation
No bias current required
Allows low power operation to be achieved

## Slide 25: CMOS Passive Mixer
RF+
RF-
LO+
LO-
IF
[*] T. Lee
Same idea, redrawn
RC filter not shown
IF amplifier can be frequency selective

## Slide 26
CMOS Passive Mixer

## Slide 27
Non-50% duty cycle of LO results in no DC offsets!!
DC-term of LO
CMOS Passive Mixer

## Slide 28
CMOS Passive Mixer with Biasing

## Slide 29: A Highly Linear CMOS Mixer
Transistors are alternated between the off and triode regions by the LO signal
RF signal varies resistance of channel when in triode
Large bias required on RF inputs to achieve triode operation
  High linearity achieved, but very poor noise figure

## Slide 30
Simple Switching Mixer (Single Balanced Mixer)
The transistor M1 converts the RF voltage signal to the current signal.
Transistors M2 and M3 commute the current between the two branches.

## Slide 31: Single balanced active mixer, BJT
Single-ended input
Differential LO
Differential output
QB provides gain for vin
Q1 and Q2 steer the current back and forth at LO
vout = ±gmvinRL

## Slide 32
Double Balanced Mixer
Strong LO-IF feed suppressed by double balanced mixer.
All the even harmonics cancelled.
All the odd harmonics doubled (including the signal).

## Slide 33: Gilbert Mixer
Use a differential pair to achieve the transconductor implementation
This is the preferred mixer implementation for most radio systems!

## Slide 34: Double balanced mixer, BJT
Basically two SB mixers
  One gets +vin/2, the other gets –vin/2

## Slide 35
Mixers based on MOS square law

## Slide 36
Practical Square Law Mixers

## Slide 37
Practical Bipolar Mixer

## Slide 38
MOSFET Mixer (with impedance matching)
IF Filter
Matching Network

## Slide 39: Sub-sampling Mixer
Properly designed track-and-hold circuit works as sub-sampling mixer.
The sampling clock’s jitter must be very small
Noise folding leads to large mixer noise figure.
High linearity

## Slide 40: Harmonic Mixer
Harmonic mixer has low self-mixing DC offset, very attractive for direct conversion application.
The RF signal will mix with the second harmonic of the LO. So the LO can run at half rate, which makes VCO design easier.
Because of the harmonic mixing, conversion gain is usually small
Emitter-coupled BJTs work as two limiters.
Odd symmetry suppress even order distortion eg LO selfmixing.
Small RF signal modulates zero crossing of large LO signal.
Output rectangular wave in PWM
LPF demodulate the PWM

## Slide 41
Features of Square Law Mixers
Noise Figure: The square law MOSFET mixer can be designed to have very low noise figure.
Linearity: true square law MOSFET mixer produces only DC, original tones, difference, and sum tones
The corresponding BJT mixer produces a host of non-linear components due to the exponential function
Power Dissipation: The square law mixer can be designed with very low power dissipation.
Power Gain: Reasonable power gain can be achieved through the use of square law mixers.
Isolation: Square law mixers offer poor isolation from LO to RF port. This is by far the biggest short coming of the square law mixers.

## Slide 42: Mixer performance analysis
Analyze major metrics
  Conversion gain
  Port isolation
  Noise figure/factor
  Linearity, IIP3
Gain insights into design constraints and compromise

## Slide 43: Common Emitter Mixer
Single-ended input
Differential LO
Differential output
QB provides gain for vin
Q1 and Q2 steer the current left and right at LO

## Slide 44: Common Emitter Mixer
Conversion gain
vout1 = ±gmvinRL
Two output component:
vout2 = ±IQBDCRL
So gain = ?
IF signal is the RF – LO component in vout1

## Slide 45: Common Emitter Mixer
Port isolation
At what frequency is Vout2 switching?
vout2 = ±IQBDCRL
vout2 = SW(LO)IQBDCRL
This is feed through from LO to output

## Slide 46: Common Emitter Mixer
Port isolation
How about LO to RF?
This feed through is much smaller than LO to output

## Slide 47: Common Emitter Mixer
Port isolation
How about RF to LO?
If LO is generating a square wave signal, its output impedance is very small, resulting in small feed through from RF to LO to output.

## Slide 48: Common Emitter Mixer
Port isolation
What about RF to output?
Ideally, contribution to output is:
SW(LO)*gmvinRL
What can go wrong and cause an RF component at the output?

## Slide 49: Common Emitter Mixer
Noise Components:
  Noise due to loads
  Noise due to the input transistor (QB)
  Noise due to switches (Q1 and Q2)

## Slide 50: Common Emitter Mixer
Noise due to loads:
  Each RL contributes vRL2 = 4kTRLf
  Since they are uncorrelated with each other, their noise power’s add
  Total contribution of RL’s: voRL2 = 8kTRLf

## Slide 51: Common Emitter Mixer
Noise due input transistor (the transducer):
  From BJT device model, equivalent input noise voltage of a CE amplifier is:

## Slide 52: Common Emitter Mixer
Noise due to input transistor:
  If this is a differential amplifier, QB noise would be common mode
  But Q1 and Q2 just switching, the noise just appears at either terminal of out:

## Slide 53: Common Emitter Mixer
Noise due to input transistor:
  Noise at the two terminals dependent?
  Accounted for by incorporating a factor “n”.

## Slide 54: Common Emitter Mixer
Total Noise due to RL and QB:
  If we assume rb is very small:
  When:
    rb << 1/(2gm) and
    n=1

## Slide 55: Common Emitter Mixer
What about the noise due to switches?
  When Q2 is off and Q1 is on, acting like a cascode or more like a resister if LO is strong
  Can show that Q1’s noise has little effect on vout
  VE1~VC1, VBE1 has similar noise as VC1, which cause jitter in the time for Q1 to turn off if the edges of LO are not infinitely steep

## Slide 56: Common Emitter Mixer
What about the noise due to switches:
  Transition time “jitter” in the switching signal:
Effect is quite complex, quantitative analysis later

## Slide 57: Common Emitter Mixer
How to improve Noise Figure of mixer:
  Reduce RL
  Increase gm and reduce rb of QB
  Faster switches
  Steeper rise or fall edge in LO
  Less jitter in LO

## Slide 58: Common Emitter Mixer
IP3:
  The CE input transistor (QB) converts vin to Iin
    BJTs cause 3rd-order harmonics
  Multiplying by RL is linear operation
  Q1 & Q2 only modulate the frequency
  IP3mixer = IP3CE’s Vbe->I

## Slide 59: Double Balanced Mixer
Basically two CE mixers
  One gets +vin/2, the other gets –vin/2

## Slide 60: Double Balanced Mixer
vout = – gmvinRL
vout = gmvinRL

## Slide 61: Double Balanced Mixer
Benefits:
  Fully Differential
  No output signal at LO
Three stages:
  CE input stages
  Switches
  Output load

## Slide 62: Double Balanced Mixer
Noise:
  Suppose QB1 & QB2 give similar total gm
  Similar to CE Mixer
IP3:
  Similar Taylor series expansion of transducer transistors
  Vin split between two Q’s, it can double before reaching the same level of nonlinearity
  IIP3 improved by 3 dB

## Slide 63: Common Base Mixers
Similar operation to CE mixers
Different input stage
  QB is CB
Slightly different output noise
  Different CB input noise
Better linearity

## Slide 64: Mixer Improvements
Debiasing switches from input transistors:
  To lower NF we want high gm, but low Q1 and Q2 current
    Conflicting!
  We can set low ISwitches and high IQb using a current source

## Slide 65
MOS Single Balanced Mixer
The transistor M1 converts the RF voltage signal to the current signal.
Transistors M2 and M3 commute the current between the two branches.

## Slide 66
MOS Single Balanced Mixer

## Slide 67
IF Filter
MOS Single Balanced Mixer

## Slide 68
IF Filter


LO
RF



LO
RF



LO
RF

MOS Single Balanced Mixer

## Slide 69
RF

S
LO
LO



LO
RF

MOS Single Balanced Mixer

## Slide 70
Single Balanced Mixer (Incl. RF input Impd. Match)
This architecture, without impedance matching for the LO port, is very commonly used in many designs.

## Slide 71
Single Balanced Mixer (Incl. RF & LO Impd. Match)
This architecture, with impedance matching for the LO port, maximizes LO power utilization without wasting it.

## Slide 72
Single Balanced Mixer Analysis: Linearity
Linearity of the Mixer primarily depends on the linearity of the transducer (I_tail=Gm*V_rf). Inductor Ls helps improve linearity of the transducer.
The transducer transistor M1 can be biased in the linear law region to improve the linearity of the Mixer. Unfortunately this results in increasing the noise figure of the mixer (as discussed in LNA design).

## Slide 73
Using the common gate stage as the transducer improves the linearity of the mixer. Unfortunately the approach reduces the gain and increases the noise figure of the mixer.
Single Balanced Mixer Analysis: Linearity

## Slide 74
Single Balanced Mixer Analysis: Isolation
The strong LO easily feeds through and ends up at the RF port in the above architecture especially if the LO does not have a 50% duty cycle. Why?
LO-RF Feed through

## Slide 75
Single Balanced Mixer Analysis: Isolation
The amplified RF signal from the transducer is passed to the commuting switches through use of a common gate stage ensuring that the mixer operation is unaffected. Adding the common gate stage suppresses the LO-RF feed through.
Weak LO-RF Feed through

## Slide 76
Single Balanced Mixer Analysis: Isolation
The strong LO-IF feed-through may cause the mixer or the amplifier following the mixer to saturate. It is therefore important to minimize the LO-IF feed-through.
LO-IF Feed through

## Slide 77
Double Balanced Mixer
Strong LO-IF feed suppressed by double balanced mixer.
All the even harmonics cancelled.
All the odd harmonics doubled (including the signal).

## Slide 78
Double Balanced Mixer
The LO feed through cancels.
The output voltage due to RF signal doubles.

## Slide 79
Double Balanced Mixer: Linearity
Show that:
IIP
in
volts
I
K
DC
SQ
3
8
3



## Slide 80
Mixer Input Match

## Slide 81
Mixer Gain

## Slide 82
Mixer Output Match
Heterodyne Mixer:
  If IF frequency is low (100-200MHz) and signal bandwidth is high (many MHz), output impedance matching is difficult due to:
  The signal bandwidth is comparable to the IF frequency therefore the impedance matching would create gain and phase distortions
  Need large inductors and capacitors to impedance match at 200MHz

## Slide 83
Mixer Output Match (IF)

## Slide 84
Mixer Output Match (direct conversion)

## Slide 85
Mixer Noise Analysis
Instantaneous Switching


LO
RF



LO
RF

Noise in RF signal band and in image band both mixed into IF signal band

## Slide 86
Mixer Noise Analysis
If the switching is not instantaneous, additional noise from the switching pair will be added to the mixer output.
Let us examine this in more detail.
Finite Switching Time

## Slide 87
Mixer Noise Analysis
Noise analysis of a single balanced mixer cont...:
When M2 is on and M3 is off:
  M2 does not contribute any additional noise (M2 acts as cascode)
  M3 does not contribute any additional noise (M3 is off)
Finite Switching Time

## Slide 88
Mixer Noise Analysis
Noise analysis of a single balanced mixer cont...:
When M2 is off and M3 is on:
  M2 does not contribute any additional noise (M2 is off)
  M3 does not contribute any additional noise (M3 acts as cascode)
Finite Switching Time

## Slide 89
Mixer Noise Analysis
Noise analysis of a single balanced mixer cont...:
When VLO+ = VLO- (i.e. the LO is passing through zero), the noise contribution from the transducer (M1) is zero. Why?
However, the noise contributed from M2 and M3 is not zero because both transistors are conducting and the noise in M2 and M3 are uncorrelated.
Finite Switching Time

## Slide 90
Mixer Noise Analysis
Optimizing the mixer (for noise figure):
Design the transducer for minimum noise figure.
Noise from M2, M3 minimized by fast switching :
  making LO amplitude large
  making M2 and M3 short (i.e. increasing fT of M2 and M3)
Noise from M2, M3 can be minimized by using wide M2/M3 switches.

## Slide 91
Mixer Noise Analysis
Noise Figure Calculation:
Let us calculate the noise figure including the contribution of M2/M3 during the switching process.

## Slide 92
Mixer Noise Analysis: RL Noise
Noise Analysis of Heterodyne Mixer (RL noise):

## Slide 93
Mixer Noise Analysis: Transducer Noise
Noise Analysis of Heterodyne Mixer (Transducer noise):

## Slide 94
Noise Analysis of Heterodyne Mixer (Trans-conductor noise):
Mixer Noise Analysis: Transducer Noise

## Slide 95
Mixer Noise Analysis: Switch Noise
Noise Analysis of Heterodyne Mixer (switch noise):

## Slide 96
Noise Analysis of Heterodyne Mixer (switch noise):
Show that:
Mixer Noise Analysis: Switch Noise

## Slide 97
Noise Analysis of Heterodyne Mixer (switch noise) cont...:
Mixer Noise Analysis: Switch Noise

## Slide 98
Noise Analysis of Heterodyne Mixer (switch noise) cont...:
G
t
m
G
f
m
Mixer Noise Analysis: Switch Noise

## Slide 99
Noise Analysis of Heterodyne Mixer (switch noise) cont...:
G
f
m
G
f
m
Mixer Noise Analysis: Switch Noise

## Slide 100
Noise Analysis of Heterodyne Mixer (switch noise) cont...:
Total Noise Contribution due to switches M2 and M3
Mixer Noise Analysis: Switch Noise

## Slide 101
Mixer Noise Analysis: Total Noise
Noise Analysis of Heterodyne Mixer (total noise):

## Slide 102
Noise Analysis of Heterodyne Mixer (total noise):
Mixer Noise Analysis: Total Noise
(VGSQ-VT0) ↑  M1 linearity ↑ and noise↓
ALO ↑  noise contribution from M2/M3 ↓

## Slide 103
Homodyne Mixer Noise Analysis: Transducer Noise
Noise Analysis of Homodyne Mixer (noise from transducer M1):

## Slide 104
Homodyne Mixer Noise Analysis: RL Noise
Noise Analysis of Homodyne Mixer (noise from RL):
Noise from RL

## Slide 105
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)}:

## Slide 106
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M1}:

## Slide 107
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M1}:
DC-term of LO

## Slide 108
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M2/M3}:

## Slide 109
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M2/M3}:

## Slide 110
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M2/M3}:

## Slide 111
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M2/M3}:

## Slide 112
Homodyne Mixer Noise Analysis: non-50% duty LO
Noise Analysis of Homodyne Mixer (M2,M3 mismatched or non-50% duty cycle of LO)--{Noise from M2/M3}:

## Slide 113
Increasing Headroom in DBM (Option 1)

## Slide 114
Increasing Headroom in DBM (Option 2)

## Slide 115
Increasing Headroom in DBM (Option 3)