## Slide 1
Microwave Mixers, Principle of Operation, Performance Characteristics and Applications
Dr. Salam D. Marougi
Notes: <number>

## Slide 2
※ Frequency Mixers are devices that translate the frequency of electromagnetic signals from one frequency band to another.
※ A Frequency Mixer is a three-port device. Two of the ports are designated as input ports while the third is an output port.
※ New set of frequencies are generated at the output of the mixer that do not exist initially at either of the two inputs of the mixer. This implies that Mixers are inherently non-linear devices.
※ Frequency Mixers are made with both active and passive devices. Active mixers are designed using transistors while passive mixers are designed using fast switching diodes.
※ By far, passive mixers are the most widely used in many microwave applications due to its favorable characteristics as compared to active mixers.
Notes: <number>

## Slide 3
RF Port
IF Port
Local Oscillator (LO) Port
The significant components at the mixer’s output are located at the following frequencies,
fout = nfLO  finput in fact  nfLO  finput 
“n” is usually an an odd integer.
 For frequency up-conversion, the IF port is used as input while
the RF port is an output port.
 For frequency down–conversion, the order is reversed.

## Slide 4
A general Voltage-Current relationship of a semiconductor diode is expressed as;
i a1{v1cos t vcos t} a2{v1cos t vcos t}2 ……(2)
When expanded this contains the term 2a2 cos(1t) . cos(2t) which has the trigonometric relationship shown in eqn. (3). It is either the sum or difference term that is the desired output of a mixer.
2 v1v2cos t . cos t = 2v1v2 {cos ( )t + cos ( )t} ……. (3)
If the diode is excited by two sinusoids, v1cos(ω1t) and v2cos(ω2t) the current through the diode is given by equation (2).
Harmonics generation using non-linear mixing
i = a1 v + a2 v2 + a3 v3 + a4 v4 + ………. (1)

## Slide 5
Diodes are “square-law” devices, which means the function describing their non-linear behavior has a strong a2 component. This means that if excited correctly they should be able to produce a strong mixing product.
Thus the basic mixer design entails injecting the signals to be mixed and extracting the desired mixing product whilst maximizing the efficiency of the conversion. One significant problem with mixers is that in addition to the wanted product, there are also numerous unwanted spurious products, often referred to as “spurs”.
The Local Oscillator (LO) is mixed with the desired RF signal to produce a copy of the RF signal at the difference frequency (the IF). In general the mixer will generate outputs at a range of frequencies given by mRF nLO..

## Slide 6
One frequency of particular importance is the image frequency. This is 2IF away from the RF and will be converted directly to the same IF frequency as the RF. Noise and unwanted signals present at this frequency can severely degrade the system performance. Filtering and/or image reject mixers are normally incorporated to address this problem

## Slide 7
Circuit Diagram of a Double-Balanced Mixer

## Slide 8
The operation of a double balanced mixer is best understood by considering the diodes as switches. The LO alternately turns the right hand pair and left hand pair of diodes on and off in anti-phase. Points ‘a’ and ‘c’ are virtual earths to the RF signal and can be considered as connected to ground. Thus points ‘b’ and ‘d’ (the balanced RF signal) are alternately connected to ground (at points ‘a’ and ‘c’). This means an in-phase RF signal and an anti-phase RF signal are alternately routed to the IF port under control of the LO. Thus the signal at the IF port is effectively the RF signal multiplied by an LO square wave of peak magnitude 1.

## Slide 9
IF Port
RF Input
Controlled by the LO
Switch equivalent of the Mixer

## Slide 10
RF input
LO
input
IF
output
Waveforms of the balanced mixer.

## Slide 11
Convolution (*)
fc
fm
fc - fm
fc + fm
3fc
3fc - fm
3fc + fm
5fc
5fc - fm
5fc + fm
Frequency
Baseband signal Vm(f)
fc
Convolved signals
Vc(f)
fc
fc - fm
fc + fm
3fc
3fc - fm
3fc + fm
5fc
5fc - fm
5fc + fm
Output signal Vo(f)
3fc
5fc
. . . . .
-fm
0

## Slide 12
Mixer Performance Specifications
• Image rejection
• Conversion gain: voltage or power
• Port-to-port isolation: dB
• Large signal performance:
• gain compression: P1dB
• intermodulation distortion spec: third-order intercept (TOI)
• Small signal performance: noise figure
• Operating range: Spurious-free dynamic range

## Slide 13
Conversion Loss
The most important mixer metric is conversion loss. Conversion loss is
defined as the difference in power between the input RF power level and
the desired output IF frequency power level. In other words:
CL = PRF - PIF
where PRF and PIF are in dBm and CL is in dB. For example, if the input RF is -10 dBm and the downconverted IF output signal -17 dBm, then the conversion loss is 7 dB.
The theoretically optimum conversion loss for a passive diode mixer is 3.9 dB. Typical values of conversion loss range between about 4.5 to 9 dB, depending on the mixer—the additional losses are caused by factors such as transmission line losses, balun mismatch, diode series resistance and mixer imbalance. In general double balanced mixers have less conversion loss than triple balanced mixers because of circuit losses. Another important trend is that wider bandwidth mixers tend to have higher conversion loss in part due to the difficulty in maintaining circuit balance over the entire bandwidth.

## Slide 15
Conversion loss is the benchmark mixer metric because it correlates closely with other metrics like isolation and 1 dB compression. Experience shows that for a mature mixer design.
B. Isolation
Isolation is a measure of the amount of power that leaks from one mixer port to another. As was described previously, port isolation is obtained through mixer balance and the use of hybrid junctions. Unfortunately, there will always be some small amount of power leakage between the RF, LO and IF ports. Isolation is the difference in power between the input signal and the leaked power to the other ports. In other words, if we place an input signal at the LO port and measure the power available at the RF port at that LO frequency, the isolation in dB is given by:

## Slide 16
PISO (L -R) = Pin(@LO) - Pout(@RF) measured at LO frequency
Note that isolation is approximately reciprocal: the port 1 to port 2 isolation will track closely with the port 2 to port 1 isolation. Hence, a single measurement can be performed to determine the isolation in both directions.
Three types of isolation are commonly quoted in microwave mixers: L-R isolation, L-I isolation and R-I isolation.
L-R isolation is the leakage of the LO into the RF port. Typical L-R isolation values range between about 25-35 dB. L-R isolation is critical in frequency downconversions because LO power can leak into the RF circuitry. If there is poor L-R isolation, LO power can contaminate the RF line by either interfering with the RF amplifier or by leaking to other parallel mixing channels causing cross-channel interference. Poor L-R isolation can also cause problems in frequency upconversions when the LO frequency is very close to the RF output frequency (when the IF frequency is at or near DC).

## Slide 17
In this case, no amount of filtering can separate the arbitrarily close RF signal and LO leakage. This can result in interference between the RF and LO and a degradation in the RF output circuitry.
L-I isolation is the leakage of the LO into the IF port. L-I isolation tends to be the worst of the three types of mixer isolation with typical values ranging from 20-30 dB. When there is poor L-I isolation, the biggest issue occurs when the LO and IF frequencies are close such that the LO contaminates the IF circuitry, as when the LO leakage is strong enough to saturate the IF amplifier
The final mixer isolation metric is R-I isolation. Values of R-I isolation typically range between 25-35 dB. Most systems designers will not find R-I isolation to be a major issue since the RF and IF powers tend to be orders of magnitude smaller than the LO power. Therefore, LO isolation problems are the primary concern of systems engineers. R-I isolation, instead, is a major concern for mixer designers because it serves as a diagnostic metric for the overall conversion efficiency of the mixer circuit. When the R-I isolation is high, the mixer circuit is well balanced and thus the conversion loss tends to be low. In mixers with bad R-I isolation (<20 dB), the conversion loss is higher and the conversion loss flatness is poor.

## Slide 18
RF
IF
LO
RF
IF
LO
RF
IF
LO
Piso(L-R)
Piso(L-I)
Piso(R-I)
Notes: <number>

## Slide 19
* The concept of intercept point can be applied to any intermodulation product; however, it normally refers to two-tone, third-order intermodulation products. If two input RF signals are incident at the mixer RF port, they cause the mixer to generate two-tone intermodulation products.
* They are called third-order products because the coefficients of RF1 and RF2 sum to equal 3. Notice that the order of intermodulation products refers only to coefficients of the RF inputs and does not include that of the LO. The order of the intermodulation product is important because a 1-dB change in the power level of each input RF signal causes the power level of each intermodulation product to change by an amount of dB equal to its order. A 1-dB change in power of each of the two input RF signals causes the power level of each tow-tone third-order product to change by 3 dB.

## Slide 20
fout = ± n fLO ± m1 fRF1 ± m2 fRf2
where n, m1 and m2 are all integers. Two-tone IMD is troublesome because the generated
Interferer (1) = 2 fRF1– fRF2 – fLO
Interferer (2) = 2 fRF2 – fRF1 – fLO
overlap in frequency with the desired downconverted signals. No amount of filtering can separate the two-tone interference and thus the signal to noise ratio of the received signal is degraded.
While fundamental mixing tones (i.e. m=1 and n=1) grow by a slope of 1 to 1 with input RF power, higher order RF mixing terms grow by a slope of m:1. In this case, two-tone IMD grows by a slope of |m1| + |m2| to 1. Hence, interference terms in the above equations are called third-order IMD products and grow by a slope of 3:1

## Slide 23
Carrier Power
Adjacent Channel Power
-80
-70
-60
-50
-40
-30
-20
-10
0
10
20
Adjacent Channel Power Ratio
Impaired Adjacent Channel
Main Channel
Upper Adjacent Channel
Lower Adjacent Channel
What Dominates ACPR Measurements?
Measured ACPR never gets better than the signal source
The receiver contribution is divided into:
  Additive contributions: noise, spurs and phase noise
  Proportional distortion: spectral regrowth within receiver
Notes: <number>

## Slide 24
E. Noise Figure
As long as the quality of the diode is closely monitored, the noise figure of the mixer can be approximated by the conversion loss. Generally, the cumulative noise figure will limit the minimum detectable signal in the receiver. Hence, when choosing mixers for low power applications, conversion loss should be as low as possible.

## Slide 25
MIXERS APPLICATIONS

## Slide 26: Direct Frequency Synthesizers
Frequency divider by 10
Frequency Mixer
Reference Oscillator
fo/10
0.9fo OR 1.1fo
2.9fo OR 3.1fo
Filter
fo
This a class of architectures creates its output frequency by mixing two or more signals to produce sum or difference frequencies by frequency multiplication, by frequency division or by combination thereof. Common components are the reference oscillator, mixers, and frequency dividers. Example of such a synthesizer is shown in the system below.
Notes: <number>

## Slide 27
i  o = e
vd
For e  0.2 rad,
sin(e)  e
sin(0.2rad) = 0.197
Phase detector characteristic of the balanced mixer.
Tangent to the sinusoidal characteristic at e = 0
V2 cos(ct + 2(t))
IF output
V1 sin(ct + 1(t))
LO input
RF input
vd(t)
km
vd(t) = V1 V2 sin[1(t)  2(t)]
km
2

## Slide 28: Indirect Frequency Synthesizers
This technique is the most versatile and accurate for frequency generation down to a small fraction of a Hertz. The fundamental building blocks constitute a Phase locked loop as shown below;
Frequency Divider (/N)
Reference Clock (fo)
Output Frequency (Nfo)
Phase Detector
Lowpass
Filter
Voltage-Controlled Oscillator
Frequency Divider

## Slide 29
Digital Modulation Implementation
I-Q Modulation
/2
Carrier
Good Interface with Digital Signals and Circuits
Can be Implemented with Simple Circuits
Can be Modified for Bandwidth Efficiency
I:
Notes: <number>

## Slide 30
freq.
fm
fc
Vo(t) = sinωct cosωmt ± cosωct sinωmt
Vo(t) = sin(ωc+ωm)t
OR
Vo(t) = cos(ωc–ωm)t
*
fc+fm
fc–fm
OR
Notes: <number>

## Slide 31
Thank You !
Q & A
Notes: <number>