## Slide 1: Phased Array History, Benefits and Architectures
Laya Mohammadi
Prof. Kwang Jin Koh
Virginia Tech
MICS/RF group
/RF Group

## Slide 2: Outline
Phased Array History, Benefits and Architectures
Phased array metric and architectural study
Mm-Wave Phase Shifter and Phased Array IC Design
/RF Group

## Slide 3: Outline
What is a phased array?
Why an array???
Case Study: A 60 GHz WPAN link budget
Phased array versus timed array
/RF Group

## Slide 4: What is a phased array?
A phased array electronically modifies the direction of transmission or reception of the electromagnetic beam.
How?
By introducing a variable time delay
Time delay equal to dsinθin/C .
/RF Group

## Slide 5: What is a phased array?
Additional power gain of N2.
AF is lower for other angles
of incidence,
Spatial Selectivity.
/RF Group

## Slide 6
Why an Array???
A 60 GHz WPAN Link Budget:
Transmitter
Antenna
G : 5 dB
Receiver
Pnoise=-174+10log (325)+ NF= -79 dBm
NF= 10 dB
OFDM (BW:325 MHz)
60 GHz CMOS PAs
P1-dB : 6 dBm (6 dBm back off)
Transmitted power is around 0 dBm.
Antenna
G : 5 dB
Path loss for a 10 m link is 88 dB at 60 GHz
PRX=0-88+5+5-5=-93 dBm.
This CMOS-based WPAN link budget is deep in the negative SNR regime by 14 dB !!!

## Slide 7
Phased array techniques can come to the rescue
8-channel phased array on the transmitter side, gain enhances by 18 dB.
A 4-channel receiver phased array enhances SNR by 6 dB.
The SNR is boosted to a positive 10 dB
/RF Group

## Slide 8: Why an Array???
 | Conventional (>50 years) | Emerging (≈5 years)
Application | Military Radar Radio Astronomy | Wireless Comm. Automotive Radar
Typical Range Array Size | Long Range (> 1km) Large (100-10000) | Short Range (< 100m) Small (4-64)
Why an Array? | Focused, High-Power Beam Multiple, Simultaneous Beams Spatial Interference Cancellation SNR Improvement in RX | SNR Improvement in RX Relaxed PA Requirement Link Reliability (Comm.) Spatial Selectivity (Radar)
Driver | Performance Size Cost | Cost Size Power Consumption
Realization Technology | Module-based III-V | Single Chip Silicon
/RF Group

## Slide 9
Focused, High-Power Beam
SNR
Improvement
Spatial
Selectivity
Link
Reliability
What We Need
Phased Array Provides:
Relaxed
PA
Requirement
Why an Array???
/RF Group

## Slide 10
Phased Arrays versus Timed Arrays
A phased array modiﬁes the direction of transmission/reception of the electromagnetic beam by introducing a variable time delay.
Integrated variable time delay blocks are difﬁcult to implement in practice, particularly
on silicon.
In narrowband systems, the required variable time delay is often approximated with a variable phase shift, and the variable delay elements are replaced with phase shifters.
/RF Group

## Slide 11
Phased Arrays versus Timed Arrays
The validity of the delay-phase approximation in phased arrays naturally depends on the instantaneous bandwidth !!!
Array-induced Inter-Symbol Interference is a direct result of this approximation.
5GHz of ISI-free bandwidth can easily be achieved in a 60GHz phased array,
but would require a true-time-delay implementation if deployed in the 3-10GHz frequency range.
/RF Group
Another reason to go to mm-wave frequencies

## Slide 12
Summary
Phased array provides:
SNR improvement.
Spatial selectivity.
Focused high power beam.
For narrowband signals, the required variable time delay is often approximated with a variable phase shift.
The phase-shifters can be incorporated in different parts of the transmitter/receiver chain. This results in three distinct phased array architectures.
RF Phase-shifting, LO Phase-shifting, Digital Arrays

## Slide 14: Conventional phase array architectures
The phase-shifters required to achieve phased-array functionality can be incorporated in different parts of the transmitter/receiver chain. This results in three distinct phased array architectures
RF Phase-shifting
LO Phase-shifting
Digital Arrays
/RF Group

## Slide 15: 1) RF Phase-shifting
Signals in the various channel are phase-shifted and combined in the RF domain.
After combiner the receiver path can be configured as conventional receivers (heterodyne, homodyne or other image rejection architectures).
/RF Group

## Slide 16: 1) RF Phase-shifting
The most widespread phased-array architecture because of
The dynamic range requirements on the mixer and the blocks that follow it are alleviated.
The main advantage:
Is the implementation of RF phase-shifters in silicon. (Passive- active)
The main challenge:
insulating a larger portion of the receiver chain from strong, in-band from undesired direction interferers.
/RF Group

## Slide 17: 2) LO Phase-shifting
/RF Group

## Slide 18: 2) LO Phase-shifting
Mixers must have sufficient dynamic range to withstand the interferers.
Routing of strong LO in different paths.
The advantage
The nonlinearity, loss and the noise performance of the phase-shifters no longer have a direct impact on the system performance.
Performance requirements on LO-path phase shifters are more relaxed
consume less area/power.
Disadvantage:
/RF Group

## Slide 19: 3) Digital Arrays
/RF Group

## Slide 20: 3) Digital Arrays
In this architecture each channel is digitized using an (ADC) and the bits of all channels are then processed using a Digital Signal Processing unit (DSP), where the spatial filtering is performed.
RF mixer and ADC of each channel and the DSP unit must have sufficient dynamic range to handle the interferers.
The entire RF chain is replicated for each channel which results in a rather power-hungry design.
Disadvantage :
Is its versatility and flexibility.
Such phased arrays are extensively used in the cellular-phone industry.
The main advantage:
/RF Group

## Slide 21: Comparative View of the Conventional Architectures
Arch. | Phase Shifter | B.W (Data rate) | Area | Power
RF Path | TTD Phase-shifter | High(T. D) Moderate(P-S) | High | Low
LO Path | Phase shifter | Moderate | Moderate | Moderate
BB Path | Digital Array | High | High | High
/RF Group

## Slide 22: Conclusion
Using phase array architectures provides SNR improvement, spatial selectivity, and relaxes PA requirements.
In RF phase shifting the dynamic range requirements on the mixer and the blocks that follow it are alleviated.
In LO phase shifting the nonlinearity, loss and the noise performance of the phase-shifters no longer have a direct impact on the system performance.
Different DSP algorithem can be used to perform spatial filtering.
/RF Group

## Slide 23
Thanks
/RF Group

## Slide 24
Phased Arrays versus Timed Arrays
/RF Group